## Slide 1
Lessons learned in the North Sea:
Closing the gaps in permanent well plugging
Malin Torsæter, PhD
Research Manager
SINTEF Industry, Dept. Petroleum
INTERPORE, New Orleans 14.05.2015

## Slide 2
Motivation: Eternal leakage protection
Gas leakage
Bacterial mats
Vielstädte et al. (2017), Dealing with legacy wells: Implications from subsea leakage along abandoned North Sea gas wells. http://ieaghg.org/docs/11mon/Session11_Talk1_IEAGHG_lvielstaedte.pdf
"Permanently abandoned wells shall be plugged with an eternal perspective"
- NORSOK D-010
"The objective of P&A is to restore the integrity of the cap rock"
- Oil & Gas UK

## Slide 3
Country | Min. plug length (m)
Denmark | 100 (or 50 + mech plug)
Norway | 100 (or 50 + mech plug)
Netherlands | 100 (or 50 + mech plug)
United Kingdom | 30
Australia | 60
Canada | 15
China | 30
Japan | 30
USA - API | 30
From:
Kuip et al, Energy Procedia 4 (2011) 5320–5326
100 m
100 ft
What do we mean by "safe plug length"?

## Slide 4
P&A
25-60 days!
Norway: P&A almost as expensive as drilling

## Slide 5
Main challenges
Log annular cement quality
Set plugs
Verify/monitor
Cut and pull pipes
(Remove steel/cement)
(Regain well access)
Use of expensive rigs:
Heavy lifting
Rotation based methods (cutting, milling)
Need for well control
Time consuming:
Plug all fluid bearing zones
Relatively long plug lengths
Extensive "tripping"
~ 80% of time

## Slide 6
Learnings from P&A research in Norway

## Slide 7
Low-hanging fruits: Save rig time
Save time on pipe cut & pull
Explosives
Erosion
Corrosion
Pipes corrode at +
Even stainless steel can be readily removed
Temperature
Cooling by gas expansion can be used to fracture cement/rock.
Vibration
A. Lavrov et al. (2016), AIMS Materials Science 3(3): 1199-1207.
J. Todorovic et al. (2016), Soc. of Petr. Eng., SPE 180052-MS
Log through multiple steel tubulars
Physics: material/fluid impact on signals
Eliminate human log interpretation
 machine learning
casing
Fast signal along casing
Slow signal in mud
ANNULUS
Trans-mitter
Receivers
Lab study of signals

## Slide 8
Well integrity: Material choice & placement
CO2-injection in the period 2009-2013
Reference
521 m
522 m
523 m
Pores
Contamination
Cement
Cement from well plug placed in 2013, cored in 2015
K.Gawel et al., Study of materials retrieved from a Ketzin CO2 monitoring well, Energy Procedia (2017)
Microscopy study of pipes
Inside casing
Outside casing
Inside tubing
Outside tubing
tubing
casing

## Slide 9
Nature's solution: shale as a barrier
pressure
permeability
Cylindrical shale sample creeping towards pipe
How can we plan to use shale as a barrier?
Can we facilitate shale creep/swelling?
"Field proven" to last for a long time!
Selected field shale
Outcrop shale
Pores/cracks
Steel pipe
Intact shale
Good barrier!
Poor barrier!
E. Fjær et al. (2016), How creeping shale may form a sealing barrier around a well, Am. Rock Mech. Assoc., ARMA 16-482.

## Slide 10: Way ahead
Norway is aiming high when it comes to well plugging & abandonment, both on the regulatory side and on R&D
A new plugging industry is foreseen
  Global and long-lasting
We see a large potential for export of technology and services
  Plugging the ~3000 wells in Norway will take 40 years
  +/- 5000 wells to plug in UK North Sea
  More than 1.8 million wells to plug globally
Thank you for your attention!