## Slide 1: Abstract ID 285 Optimization of injection strategies for field-scale leakage remediation using microbially induced calcite precipitation
Svenn Tveit and David Landa-Marbán
NORCE Norwegian Research Centre

## Slide 2: CO2 storage
Saline aquifers or depleted hydrocarbon reservoirs have large volumetric storage potential
High injection rate can lead to hazardous pressure build-up
Fractures and/or fault reactivation can occur  CO2 leakage
Sealing technology must be efficient and reliable

## Slide 3: Field-scale application of MICP
Goal: Seal leakage paths potentially tens-of-meters away from the injection well
Injection components:
  Microbial solution
  Growth solution
  Cementation solution
MICP model implemented in Open Porous Media (OPM) Flow simulator (www.opm-project.org)
 suspended microbes
 oxygen
 urea

## Slide 4: Injection strategy
= microbial solution
= growth solution
= cementation solution
= water injection

## Slide 5: Optimization
Goal:
  Maximizing sealing of leakage paths and minimize total injection and no-flow periods
Objective function
  = volume fraction of calcite at leakage path
  = end of phase
  = regularization parameter
are injection and no-flow periods, which are the control variables
Optimization problem solved with EnOPT steepest ascent method:
  Gradient approximated by sample covariance matrix  no derivatives needed!
= number of phases
= number of injection and no-flow periods

## Slide 6: Numerical setup
Two aquifers separated by a caprock (not shown explicitly)
Simulate quarter of the domain (shown with dotted lines)
5 phases of injection and no-flow periods
Leakage path permeability twice the aquifer permeability
Assessed leakage by simulating CO2 injection before and after optimized MICP treatment
= 30m
= = 100m
= = 5m

## Slide 7: Test case 1
= 1m
= 13m
= 14m
When , permeability 0D

## Slide 8: Test case 1
Before MICP:
4.3 % CO2 leakage
After MICP:
6.67∙10-12 % CO2 leakage

## Slide 9: Test case 2
= 1m
= 11m
= 19m
When , permeability 0D

## Slide 10: Test case 2
Before MICP:
7.04 % CO2 leakage
After MICP:
1.28∙10-9 % CO2 leakage

## Slide 11: Summary
Field-scale optimization procedure for sealing leakage paths with MICP
  OPM Flow simulator
  EnOPT optimization method
Injection strategy for efficient sealing at the leakage location
Test cases showed that optimized MICP treatment effectively closed leakage paths for CO2 through the caprock

## Slide 12: Acknowledgements
The authors are grateful for the financial support from Research Council of Norway through the MICAP project, grant 268390.
Thank you for your attention!