## Slide 1
Numerical simulation of reactive flow in fractured vuggy carbonate reservoirs considering hydro-mechanical-chemical coupling effects
InterPore2026: MS20—Special Session in Honor of Jun Yao
a Research Center of Multiphase Flow in Porous Media, China University of Petroleum (East China), China
b Earth Systems Science and Engineering, King Abdullah University of Science and Technology, Saudi Arabia
c Department of Petroleum Engineering, Colorado School of Mines, United States
Zhao-Qin Huanga, Cun-Qi Jiab, Jun Yaoa, Yu-Shu Wuc
19-22 May 2026, Nantes, France
Notes: Good morning/afternoon, everyone. It is a great honor to be here at InterPore 2026, especially in this special session organized in honor of Professor Jun Yao. My name is [Your Name], from the Research Center of Multiphase Flow in Porous Media at the China University of Petroleum (East China). Today, I will be presenting our research on the "Numerical Simulation of Reactive Flow in Fractured Vuggy Carbonate Reservoirs."

## Slide 2
1. Background and motivation
2. The hydro-mechanical-chemical model
3. Numerical scheme and examples
4. Remarks and future works
Outline
Notes: My presentation is divided into four main parts. First, I’ll discuss the background and motivation behind this work. Then, I will introduce our theoretical model, the Discrete Fracture-Vug Network (DFVN). Next, I'll briefly cover the numerical scheme, followed by several numerical examples to validate the model and explore the coupling effects. Finally, I will conclude with some remarks and our plans for future work.

## Slide 3
1.1 Background
Fractured vuggy carbonate reservoirs: more than 60% of the world's oil and 40% of the world's gas reserves are held in carbonate reservoirs, and fractured vuggy systems often host giant fields, especially important in Middle East, Mexico, West China, Brazil, ...
Karst aquifers: supply 10~25% of global drinking water in the world, especially important in Europe, China, Middle East, ...
The world karst aquifer map (WOKAM)
Nico Goldscheide, et al., Hydrogeol J (2020) 28:1661–1677
The world distribution of carbonate reserves
http://www.slb.com/~/media/Files/industry_challenges/carbonates
Notes: Deep carbonate reservoirs are essential for increasing oil and gas reserves. However, they are characterized by extreme heterogeneity where matrix pores, tectonic fractures, and dissolution vugs coexist. This complex spatial connectivity leads to highly unpredictable flow paths and, unfortunately, low recovery efficiency.

## Slide 4
Void spaces: pore, fractures, vugs, caves
Multi scales： from μm to m
Multi flow modes： porous + free flow
Multi physics：geomechanical + reactive flow
microscale fractures
millimeter vugs
centimeter small cavity
macroscale large cavity
fractures
vugs
well
Huang et al., Physics of Fluids, 2023, 35: 027116
The key characteristics: unlike typical porous media, karst systems have large conduits (cave-like channels), small fractures and fissures, and rock matrix with low permeability. The fluid flow and transport are the complex coupling process of porous media flow and free fluid flow.
1.1 Background

## Slide 5
1.2 Acid fracturing stimulation
Why acid fracturing stimulation is needed?
Jianyi Liu, et al. Geomech. Geophys. Geo-energ. Geo-resour., 2024,10: 69
(a) Seismic features of a karst cave
(b) Schematic of the geological model
Schematic of the geological model with acid fracturing well
Poor matrix permeability
Uneven connectivity between vugs and fractures
Strong channeling and bypassing
Low productivity
Rapid decline
Poor sweep efficiency
The strong heterogeneity and anisotropy
Acid fracking process:
Hydraulic fracking→ creates fractures
Acid reaction → etches fracture surfaces

## Slide 6
fractured vuggy carbonate rock
fractured carbonate rock
carbonate matrix rock
vug
fractures
matrix
fractures
matrix
matrix
1.3 Previous works
Acid stimulation simulation in carbonate rocks: based on the classical two-scale continuum model developed by Panga et al. (2005), we have developed a new two-scale continuum model which considers mass conversion between liquid and solid phases.
The fluid flow models: the Darcy-scale model describes the reactive-transport process of acid and the evolution of the rock matrix and fractures. The Stokes model have been applied in vugs.
porosity
Cunqi Jia, Jun Yao, Kamy Sepehrnoori. Springer, 2025
Cunqi Jia, Kamy Sepehrnoori, Zhaoqin Huang, Jun Yao - SPE Journal, 2021

## Slide 7
Chart: Time/s
| 0 | 20 | 40 | 60 | 80 | 100 | 120 | 140 | 160 | 180 | 200 | 220 | 240 | 260 | 280 | 300 | 320 | 340 | 360 | 380 | 400 | 420 | 440 | 460 | 480 | 500 | 520 | 540 | 560 | 580 | 600 | 620 | 640 | 660 | 680 | 700 | 720 | 740 | 760 | 780 | 800
不考虑应力 | 0.1 | 0.11122 | 0.13763 | 0.15981 | 0.17809 | 0.1936 | 0.20745 | 0.22 | 0.23154 | 0.24226 | 0.25232 | 0.26182 | 0.27082 | 0.27941 | 0.28762 | 0.29549 | 0.30305 | 0.31034 | 0.31738 | 0.32419 | 0.33079 | 0.33718 | 0.3434 | 0.34945 | 0.35534 | 0.36108 | 0.36668 | 0.37215 | 0.37751 | 0.38274 | 0.38787 | 0.3929 | 0.39783 | 0.40267 | 0.40743 | 0.4121 | 0.4167 | 0.42122 | 0.42567 | 0.43006 | 0.43439
考虑应力 | 0.1 | 0.10053 | 0.10371 | 0.10768 | 0.11163 | 0.11542 | 0.11908 | 0.12263 | 0.12606 | 0.1294 | 0.13266 | 0.13583 | 0.13893 | 0.14197 | 0.14494 | 0.14784 | 0.15069 | 0.15347 | 0.15621 | 0.15889 | 0.16151 | 0.16409 | 0.16662 | 0.1691 | 0.17154 | 0.17394 | 0.17629 | 0.17861 | 0.18088 | 0.18312 | 0.18532 | 0.18749 | 0.18962 | 0.19172 | 0.19379 | 0.19583 | 0.19784 | 0.19982 | 0.20177 | 0.2037 | 0.2056
10MPa
10MPa
fracture apertures / mm
water saturation Sw
0.1 0.3 0.5 0.7 0.9
0.01 0.05 0.1
no hydro-mechanical
hydro-mechanical
The water saturation Sw at point-A
the difference of Sw is 130%
without hydro-mechanical
hydro-mechanical
0MPa
0MPa
Mises stress
fractured vuggy rock
water saturation Sw
Fluid flow: the coupling of porous media flow and free fluid flow, not only the Darcy equation
Hydro-mechanical: fractures will be open or closed, and the cavities will deform during production
collapse
Lijun Liu, Zhaoqin Huang, Jun Yao, et al., International Journal of Rock Mechanics & Mining Sciences 137 (2021) 104543
What is the effect of hydro-mechanical behavior on the production of fractured vuggy carbonate reservoirs?
1.3 Previous works
A
A

## Slide 8
Acid injection
1. Rock dissolution
2. Deformation under geostress
3. Flow paths change
Is the HMC coupling effects important? acid dissolution enlarges flow channels, while in-situ stress causes compaction and fracture closure, which is a typical hydro-mechanical-chemical (HMC) coupling process. These feedbacks continuously alter permeability, aperture, and flow paths. How to simulate?
Acid reacts with rock and dissolves minerals
Matrix compaction and fracture/vug deformation
Geometry changes lead to redistribution of flow paths
Hydro-Mechanical-Chemical coupling
Mechanical
Hydro
Heat
Chemical
T
M
C
H
porosity
permeability
dissolution and precipitation
heat conduction
pH concentration
reaction rate
thermal stress
convective mass transfer
Hydro-Mechanical-Chemical coupling
1.4 Hydro-Mechanical-Chemical coupling process
Notes: To improve connectivity, acidizing is commonly used to dissolve rock and connect isolated vugs. However, in deep reservoirs, we face a competition: while acid dissolution increases fracture aperture and vug geometry, high in-situ stress causes matrix compaction and fracture closure. Understanding this interaction between chemical dissolution and mechanical deformation is critical.

## Slide 9
1. Background and motivation
2. The hydro-mechanical-chemical model
3. Numerical scheme and examples
4. Remarks and future works
Outline
Notes: My presentation is divided into five main parts. First, I’ll discuss the background and motivation behind this work. Then, I will introduce our theoretical model, the Discrete Fracture-Vug Network (DFVN). Next, I'll briefly cover the numerical scheme, followed by several numerical examples to validate the model and explore the coupling effects. Finally, I will conclude with some remarks and our plans for future work.

## Slide 10
2.1 The fluid flow models in fractured vuggy rocks
Porous-flow region
Darcy equation
Free-flow region
Navier-Stokes equation
Coupling interface conditions
coupling Darcy-Stokes model
multi-scale characteristic
coupling porous-flow & free-flow characteristic
DFVN
DFN（porous-flow region）
Vug System（free-flow region）
+
=
Yao and Huang, SPE & CiCP, 2010, 2011
The Discrete Fracture-Vug Network (DFVN) model

## Slide 11
Porous media | Matrix | Fractures
Solute transport |  | 
Solute exchange |  | 
Chemical dissolution |  | 
2.2 The chemical reaction and solute transport models
Darcy scale
pore scale
Dimension-reduction fracture model
Modified two-scale continuum model
hydrochloric acid (HCl) and calcite carbonate rock (CaCO3)
Notes: Moving on to the theoretical model. We developed the Discrete Fracture-Vug Network (DFVN) model to simulate this complex system. In this framework, the matrix, fractures, and vugs are fully coupled, with fractures and vugs treated as lower-dimensional internal boundaries to significantly save computational cost.

## Slide 12
2.3 H-M-C coupling model of fractured vuggy rocks
outcrops
1. Porous media：Biot equations
2. Vug：Stokes equations
4. Interface：extended BJS conditions
DFVN model
Hydro-mechanical model
3. Vug：Reactive acid transport
Matrix: porosity
fracture: normal stress
fracture: stress compaction

## Slide 13
1. Background and motivation
2. The hydro-mechanical-chemical model
3. Numerical scheme and examples
4. Remarks and future works
Outline
Notes: My presentation is divided into five main parts. First, I’ll discuss the background and motivation behind this work. Then, I will introduce our theoretical model, the Discrete Fracture-Vug Network (DFVN). Next, I'll briefly cover the numerical scheme, followed by several numerical examples to validate the model and explore the coupling effects. Finally, I will conclude with some remarks and our plans for future work.

## Slide 14
3.1 Numerical scheme
(1) Fluid flow discretization
(2) Acid transport and reaction discretization
matrix
fracture
vug
matrix
fracture
vug
Fluid flow region: The FEM has been used to discretely solve the flow, solute transport and stress equations. Quadratic Taylor-Hood element is used for the velocity and linear elements for the pressure in the porous flow equations.
Reactive acid transport: Linear elements are used for the solute transport equations
Stress field: classical quadratic nodal elements are used in the displacement field.
(3) Stress field discretization

## Slide 15
3.1 Numerical scheme
thin elastic
layer model
The real fractures: are some narrow high permeable regions with small width.
Simplified fracture model: we use the discrete fracture model, which is a dimension-reduction model, to reduce the number of local refined fracture mesh.

## Slide 16
3.2 Model Validations
Comparison of dissolution patterns between physical experiment and numerical simulation results
The accuracy of the acid–rock reactive flow module was verified by comparing the simulation results with the core acidizing experiments of Hoefner and Fogler (1988).
Experimental literature results
Numerical simulation results
10.2 cm
3.8 cm
Face
dissolution
Conical wormhole dissolution
Wormhole dissolution
Uniform dissolution
low
high
Injection rate
10.2 cm
3.8 cm
low
high
Injection rate
Face
dissolution
Conical wormhole dissolution
Wormhole dissolution
Uniform dissolution
 | Parameters | Values
ϕ0 | Initial porosity | 0.2
Δϕ | Porosity variation | 0.15
Nac | Acid capacity number | 0.1
Sh∞ | Asymptotic Sherwood number | 3
Sc | Schmidt number | 252.53
λX | Longitudinal pore structure coefficient | 0.5
λT | Transverse pore structure coefficient | 1
αos | Pore structure efficient | 0.5
parameter values used in the simulation
Notes: First, we validated our reactive flow module against the classic experiments by Hoefner and Fogler. As shown here, our model successfully captures the transition from face dissolution at low injection rates to wormholing, and finally to uniform dissolution at high rates, matching experimental observations perfectly.

## Slide 17
In the continuum model, fractures are treated as mesh elements similar to the porou matrix. The highly refined mesh around the fractures guarantees accurately capturing the influence of fractures on fluid flow and mechanical behavior.
Parameters | Value | Parameters | Value
Young’s modulus of matrix E/GPa | 40 | Fracture aperture b/mm | 1
Matrix Poisson’s ratio ν | 0.25 | Normal stiffness Kn/GPa·m-1 | 40.9
Matrix Poisson’s ratio Ef/GPa | 40 | Rock density ρs/kg·m-3 | 2600
Fracture Poisson’s ratio νf | 0.1 | Fracture storage coefficient Sf/Pa-1 | 1.0×10-15
Porosity of matrix ϕ | 0.1 | Permeability of matrix k/m2 | 1.0×10-18
Storage factor for matrix S/Pa-1 | 1.0×10-14 | Permeability of fracture kf/m2 | 1.0×10-10
Benchmark model
Continuum model
Discrete fracture model
Displacement
pressure
Displacement on the
observation line
displacement at Point A
pore pressure at Point B
Comparison of parameter values calculated by continuum model
and discrete fracture (DFN) model at 100 days
Continuum
model
Discrete fracture
model
Continuum
model
Discrete fracture
model
Comparison of parameter distributions calculated by continuum model
and discrete fracture model at 100 days
3.2 Model Validations
Comparison of the classical narrow fracture with real width and the d-1 discrete fracture model
Notes: We also compared our Discrete Fracture Model (DFN) with conventional continuum models. The pressure and displacement distributions across the fracture at 100 days show that the DFM approach provides a more precise representation of the discontinuities while maintaining overall accuracy.

## Slide 18
Concentration profile
Porosity profile
Velocity profile
Under higher stress conditions, the porosity of the target core sample after acid dissolution is lower compared to conditions without stress. In the absence of stress, a competitive balance between acid transport and reaction is achieved, leading to an optimal state.
When the mechanical process is coupled to the matrix acid stimulation process, the acid fluid has a greater effective stress load and receives a localized acceleration. The enhanced migration strength leads to a higher volume of acid fluids being ineffectively transported and increasing the acid breakthrough volume.
3.3 Numerical examples: carbonate rock matrix
Flow boundary condition
Mechanical boundary condition
Damkohler number
=500
Notes: Visualizing the profiles, we see that higher stress promotes acid transport along dominant channels but limits overall matrix dissolution, which explains the lower utilization efficiency.

## Slide 19
3.3 numerical examples: single fracture and vug cases
Single fracture
Single fracture + vug
Flow B.C.
Mechanical B.C.
Single vug
Stress plays a crucial role in influencing fracture aperture, particularly during the initial stages of stress application. In the early stages of stress application, substantial fracture closure occurs, which decreases the efficiency of acid transport along the fracture.
The reduction in fracture conductivity compels a greater volume of acid to flow into the surrounding matrix, thereby enhancing matrix dissolution and contributing to the increase in PVBT. In the single-vug model, stress-induced deformation is minimal. Although vug existence induces acid fluid flow, the impact of stress on flow paths is limited.
Damkohler number
=500
porosity
Notes: Visualizing the profiles, we see that higher stress promotes acid transport along dominant channels but limits overall matrix dissolution, which explains the lower utilization efficiency.

## Slide 20
At high injection rates: stress induction results in increased acid dissolution across broader areas.
At lower injection rates: the acid solution preferentially migrates into the vugs and the fracture networks. The interconnectivity between vugs and fractures progressively emerges as increasingly crucial in the acid stimulation.
Compared to the matrix region: fractures and vugs establish preferential pathways for acid migration. Less acid solution is needed to achieve a breakthrough. Stress diminishes the fluid flow capacity within these fractures, prompting enhanced dissolution in the adjacent matrix and increasing the PVBT.
with stress 20 MPa
without stress
3.3 numerical examples: complex fractures and vugs case
Flow B.C.
Mechanical B.C.
with stress 20 MPa
without stress
concentration
porosity
Notes: We also investigated the Damköhler number (Da), which represents the ratio of reaction rate to transport rate. In complex fracture-vug systems, the breakthrough volume increases as the reaction becomes more transport-limited (lower Da), and high stress further exacerbates this inefficiency.

## Slide 21
1. Background and motivation
2. The hydro-mechanical-chemical model
3. Numerical scheme and examples
4. Remarks and future works
Outline
Notes: My presentation is divided into five main parts. First, I’ll discuss the background and motivation behind this work. Then, I will introduce our theoretical model, the Discrete Fracture-Vug Network (DFVN). Next, I'll briefly cover the numerical scheme, followed by several numerical examples to validate the model and explore the coupling effects. Finally, I will conclude with some remarks and our plans for future work.

## Slide 22
4.1 Conclusions
The presence of isolated fractures and vugs increases storage capacity but has a minimal effect on hydraulic conductivity. As the number of fractures and vugs increases, both core porosity and permeability also rise. However, the enhancement in core permeability remains relatively limited.
When the mechanical process is coupled to the matrix acid stimulation process, the acid fluid has a greater effective stress load and receives a localized acceleration. The enhanced migration strength leads to a higher volume of acid fluids being ineffectively transported and increasing the acid breakthrough volume.
Compared to the matrix region, fractures and vugs establish preferential pathways for acid migration. Less acid solution is needed to achieve a breakthrough. Stress diminishes the fluid flow capacity within these fractures, prompting enhanced dissolution in the adjacent matrix and increasing the PVBT. Within models incorporating vugs, stress has limited deformation effects.
Higher injection rates promote a more uniform dissolution pattern. Lower injection rates concentrate on dissolution in fractures and vugs. The acid does not fully saturate the vug spaces. Instead, the acid solution tends to dissolve the solid matrix and potentially connect with adjacent vugs or fractures.

## Slide 23
4.2 Future works
Experimental research: hydro-mechanical-chemical coupled acid-fracturing test
Build a visualized HMC experimental platform for single-fracture acidizing. Quantify the competition between acid etching and stress closure.
Identify dissolution patterns under different Pe-Da conditions. Quantify the real-time contribution of acid etching and stress closure. How the fracture’s permeability evolve under the HMC coupling process.
Notes: Looking ahead, our future work will heavily focus on experimental validation. We are planning a new series of visualized Hydro-Mechanical-Chemical (HMC) experimental tests to better understand the coupling mechanisms in physical core samples.

## Slide 24
The end
Thank You！
Notes: That concludes my presentation. I would like to thank our team at the China University of Petroleum and our collaborators. Thank you all for your attention, and I am happy to take any questions.