## Slide 1
Dali Zhao
Research Center of Multiphase Flow in Porous Media
China University of Petroleum (East China)
19-22 May 2026, Nantes, France
InterPore2026: MS20—Special Session in Honor of Jun Yao
A Variable-Dimension Evolutionary Transfer Optimization Framework for Well-Fracture Pattern Co-optimization of Fractured Horizontal Wells in Shale-Gas Reservoirs

## Slide 2
1. Background
Natural gas is an important low-carbon and clean energy source, and shale gas serves as an important supplementary and replacement resource.
Global energy consumption shares, 2024
Global demand growth, 2024
U.S. shale gas vs. total natural gas
The data is sourced from EIA and is up to date as of 2024. The data for 2025 will be released in June 2026.
shale gas
Conventional natural gas
82%
Notes: First, let me briefly introduce the research background.
Natural gas is an important low-carbon and clean energy source. As of 2024, it accounts for about 25% of the global energy mix.
Shale gas is an important supplementary resource for natural gas supply. Taking the United States as an example, by 2025, shale gas accounts for about 82% of its total natural gas production.
Therefore, further research on shale gas development remains highly important.

## Slide 3
1. Background
Horizontal well hydraulic fracturing and three-dimensional development are key technologies for efficient shale gas development.
Rational well placement and hydraulic fracturing design can significantly improve shale gas production performance.
Hydraulic fracturing. Credit: Oregon State University
3D development mode of shale gas
Notes: Horizontal wells, hydraulic fracturing, and three-dimensional development have been widely used to improve shale gas production.
In this process, where to place the wells and how to design the fractures are two key factors that directly affect production performance.

## Slide 4
1. Background
3D development model
Well–fracture optimization parameters
In iterative optimization, the numbers of horizontal wells and hydraulic fractures may vary. The dimensionality of the optimization variables is variable.
Variable-Dimensional Evolutionary Transfer Optimization(VDETO) framework
Transformed dimensional sample matrix
The dimension of variable is n * m, where both m and n are variables.
  [1] Zhao, D., Yao, J., Huang, Z. et al. 2026. A Variable-Dimension Evolutionary Transfer Optimization Framework for Well-Fracture Pattern Cooptimization of Fractured Horizontal Wells in Shale-Gas Reservoirs. SPE J. SPE-233396-PA (in press; posted 17 April 2026). https://doi.org/10.2118/233396-PA
An example of a 3×2 matrix and a 3×4 matrix
Notes: For example, in a shale gas reservoir, we not only cannot determine the optimal well placement and fracture parameters, but we also cannot determine the optimal number of wells and the number of fractures. In field studies, we usually assume a range for the number of wells and the number of fractures, and then perform sensitivity analysis to optimize parameters such as well placement and fracture half-length. This works in some scenarios, but it restricts the search space to a very small range and may miss potential optimal schemes. The solution is to also treat the number of wells and the number of fractures as variables. For example, a well–fracture scheme can be viewed as an m×n matrix, where m represents the number of wells and n represents the fracture-related parameters; both m and n are variable. This raises a new problem: during the optimization process, the uncertainty in the dimensionality of the well-fracture scheme leads to solutions with varying dimensions. For instance, in the same optimization iteration, we may have both a 3×2 matrix and a 3×4 matrix. How to achieve information exchange between a 3×2 matrix and a 3×4 matrix becomes a new challenge. Traditional optimization algorithms have two processing methods. One is to add zero values, for example, expanding a 3×2 matrix to a 3×4 matrix by padding with zeros, but this introduces a large amount of redundant information. The second method is to truncate the matrix, for example, reducing a 3×4 matrix to a 3×2 matrix, which causes loss of the information carried by the matrix. Neither method is conducive to improving the optimization performance. Therefore, we propose an optimization method based on knowledge transfer to solve this problem."

## Slide 5
Task repository containing the optimal well–fracture scheme
Adaptive adjustment of solution-vector dimensionality
Efficient information exchange among populations with different dimensions
Coordination between individual historical best solutions and global multidimensional decisions
①
②
③
2. Optimization algorithm
Notes: This is the framework of our method.
First, we transform the variable-dimensional optimization problem into a multitask optimization problem. Each task represents one specific dimensionality, and the task dimension can be adjusted during the optimization process.
After building this task library, we perform the optimization following the framework shown on the right. It mainly includes three parts

## Slide 6
2. Optimization algorithm
1. Probability-Controlled Dimensional Adaptation
Probability-controlled dimensional adaptation
Transformed dimensional sample matrix
increase if pr > pc
decrease if pr > pc
The variable dimensionality is 5 × m, where m is also a variable.
Under stochastic probability control, specific rules for dimension increase and decrease are defined for high and low dimensional problems, respectively, enabling the automatic optimization of the number of horizontal wells without the need to prescribe it in advance through sensitivity analysis.
Pseudo-code of dynamic dimension adjustment mechanism
Low dimensional tasks
High dimensional tasks
Notes: First, we propose a probability-controlled adaptive dimension mechanism.
Different dimension-changing rules are designed for different dimension tasks. For low dimension, It only allows for an increase or decrease of one dimension. For high dimension , it allows the dimension to vary within a certain range. To avoid premature convergence, dimension adjustment is triggered only when a random probability exceeds a predefined threshold during each iteration.

## Slide 7
2. Optimization algorithm
2. Cross-Task Mapping Based on Population Feature Differences
Target task feature vector:：
Cross-dimensional mapping optimization model:
Internal fitness function:
Source task feature vector
A cross-dimensional mapping optimization model is established based on the characteristic differences among population individuals, and the internal fitness function is solved using the differential evolution algorithm
Notes: Then, we propose a cross-task mapping mechanism based on population feature differences. As shown in the figure, the source task and target task have different dimensions. To transfer schemes from the source task to the target task, we first calculate their feature differences in the source task and then compare them with the assumed mapped schemes in the target task. After that, an internal fitness value is defined to measure the mapping quality. Finally, differential evolution is used to optimize the mapped schemes, and the schemes with the smallest internal fitness are selected as the final mapped scheme.

## Slide 8
2. Optimization algorithm
PSO Velocity Update Equation(Ranking high) ：
GLPSO Velocity Update Equation(Ranking low):
Particle Position Update Equation ：
Ranking of Particle Fitness Values
3. Global-Local Particle Swarm Optimization Algorithm Based on Fitness Ranking
Particle
Current-task global best direction
Personal best direction
Inertia direction
GLPSO particle direction
Global best direction across all tasks
PSO particle direction
Particle Sorting Calculation Equation ：
Resultant vector
Heterogeneous knowledge was globally shared among populations of different dimensionalities.
Notes: We develop a global-local particle swarm optimization strategy.
All particles are ranked by their fitness values. Particles with better performance update their velocities using the standard PSO rule, while poorly performing particles are updated using the GLPSO rule.
The key idea of GLPSO is to replace the current-task best solution with the global-task best solution. In this way, good particles continue searching in their current promising direction, while poor particles receive a global guidance to explore potentially better regions.

## Slide 9
3. Practical Problems
Multi-Well Well Pattern and Fracture Network Optimization
Physical model settings
Shale gas reservoir mechanism model
3D shale gas model :1000×1500×100 m, 50×150×10. Adopt three-layer development, with 2–3 wells in each layer. A gas–water two-phase flow model incorporating gas adsorption and Knudsen diffusion effects was implemented using CMG IMEX.
Basic data of shale-gas reservoir
Notes: Next, we apply VDETO to a practical case.
We build a 3D shale gas reservoir model .Adopt three-layer development, with 2–3 wells in each layer. the numerical simulation is performed using CMG IMEX.

## Slide 10
Net present value model
Optimization variables: number of horizontal wells, well placement, half-length of horizontal wells, number of fractures, and fracture half-length.
Qg​ and Qw denote the gas production and water production, respectively, over the time step Δt. Rg​ and Rw​ denote the prices of natural gas and water, respectively. O denotes the operating cost. b denotes the discount rate. m denotes the number of horizontal wells. Nf​ denotes the number of fractures in each well. Cwell​ denotes the cost of a horizontal well. Cxf​ denotes the relationship between the fracturing-stage cost and the fracture half-length.
Fracture Network Non-Intersection Model
3. Practical Problems
Notes: We build an optimization model with net present value (NPV) as the objective.
To avoid fracture interference, we build a Fracture Network Non-Intersection Model, where the spacing between two wells must be larger than the sum of their maximum fracture half-lengths.

## Slide 11
Surrogate model to accelerate optimization process
1.CNN
CNN encoder extracts spatial features
2. Mask Attention Aggreation
Challenge: sparse well-fracture data make conventional CNNs insensitive to key spatial features.
Innovation: Learnable mask attention adaptively weights wellbore, perforation, and fracture masks to highlight production-critical sparse features.
3.LSTM
LSTM decoder predicts gas production and flowback volume over time
3. Practical Problems
Notes: To accelerate the optimization process, we build a CNN–LSTM surrogate model to replace part of the numerical simulations.
We encode the well–fracture network as digital inputs, but the well and fracture features are sparse compared with the reservoir matrix, making them difficult for CNN to capture. Therefore, we introduce Mask Attention to assign higher weights to these key features and these weights can be automatically learned and adjusted during model training.

## Slide 12
4. Optimization Results
Result
The VDETO achieves the highest NPV of 1.57 × 10⁹ CNY, improving it by 7.5% and 8.1% over MVPSO and VPSO, and by 11%–17% over the baseline scheme.
VDETO shows the narrowest confidence interval, indicating better stability and robustness
Iteration curve
Baseline scheme
Variable-dimensional optimization scheme
Notes: These are the optimization results.
We compare VDETO with other variable-dimensional methods and baseline schemes, where the baseline uses equally spaced fractures with the same half-length for each well.
VDETO achieves the highest NPV, improving it by 7.5% and 8.1% over MVPSO and VPSO, and by 11%–17% over the baseline schemes. It also shows the narrowest confidence interval, indicating better robustness.

## Slide 13
Result
Well placement: VDETO result shows clear inter-layer adaptation: more wells are placed in Layers 1 and 3 with better flow conditions and fewer wells are placed in Layer 2.
Fracture layout: The optimized fractures adapt to reservoir heterogeneity and form an alternating spindle–dumbbell fracture pattern.
Optimal well placement and fracture layout
4. Optimization Results
Cumulative Gas Production and Flowback Volume
Notes: The VDETO result shows clear inter-layer adaptation: more wells are placed in Layers 1 and 3 with better flow conditions, while fewer wells are placed in Layer 2.
For the fractures, longer fractures are mainly arranged in high-permeability areas, while shorter fractures are used in low-permeability areas, forming an alternating spindle–dumbbell fracture pattern.

## Slide 14
Acknowledgements & Q&A
  The author would like to sincerely acknowledge the guidance of Professor Jun Yao and the financial support from the Research Center of Oil and Gas Flow and the National Natural Science Foundation of China (Grant No. U24B6001).
Acknowledgements
Contact Information
  Name: Zhaodali
  Research Center of Oil and Gas Flow
  State Key Laboratory of Deep Oil and Gas/China University of Petroleum (East China)
  Email: zhaodaliupc@163.com
Thank You for Your Attention!
Notes: Finally, I would like to thank Professor Jun Yao for his guidance on this work, and the National Natural Science Foundation of China for the financial support. Thank you for your attention.