## Slide 1
HTHP microfluidic platforms for In-situ
pore-scale studies of mineral reactions
Presenter: Ziyou Zhu (PhD candidate, Nanjing University)
Supervisor: Zhaoyang Ma Date：22/05/2026
1
Notes: Investigation of Pore-Scale Dynamics of Dissolution-Precipitation of Mineral Using Micromodel

## Slide 2: What is microfluidics
2
Microfluidics = precise control of fluids in micron-scale channels
Typical length scale: nm - μm
Flow regime: laminar (Re << 1)
Ultra-low reagent consumption: nL - μL
Enables direct visualization of process
Microfluidics let us see physics, chemistry and biology at the pore-cale
Microfluidics is widely used across many fields
Minimal sample and reagent consumption
Precise fluidic control
Rapid analysis and high-throughput capability

## Slide 3: Micromodel for subsurface systems
3
Overview of the Reservoir-On-a-Chip (ROC) Workflow
(Naga Siva Kumar Gunda, et al., 2011)
Micromodel = microfluidic representation of porous media
Mimics pore-scale structure of real rocks
Geometry derived from
Real rock imaging (FIB-SEM, micro-CT)
Or idealized pore networks
Fabricated in glass/silicon/PDMS…
Enables direct visualization of flow, reactions, and microbes in porous media
Micromodels translate real reservoir structures into observable microfluidic systems

## Slide 4: Microfluidics in geo-energy research
4
Developing HTHP microfluidics is essential & critical for deep-earth resources development
Conventional microfluidics cannot replicate the in-situ reservoir conditions

## Slide 5: HTHP microfluidic experimental platform
5
Photographs of the developed equipment platform in Nanjing University.
Microfluidic platforms can simulate the conditions of subsurface resource exploitation
Four parts
HTHP cabin
Displacement system
Data acquisition system
Microfluidic chips

## Slide 6: HTHP cabin
6
Replicates deep subsurface reservoir conditions up to 70 MPa and 300 ℃
Micromodel holder 1（150℃ 70MPa）
Ultra-deep Oil and Gas Development
Micromodel holder 2（300℃ 30MPa）
Hot Dry Rock and Supercritical Geothermal
Micromodel holder 3（100℃ 10MPa）
CCUS and EOR
Adopt the “sealed cabin” design
Hastelloy and sapphire windows
Fluid-delivered (water) confining pressure
Independent, high - precision control of confining / pore pressure and temperature

## Slide 7: Displacement & Data acquisition system
7
Displacement system
Data acquisition system
High-precision, highly stable flow rates (0.00001ml/min- 30ml/min)
Multiphase and multi-component injection (3 containers)
Integrated system controlling the flow rates, temperature and pressure.
Microscope + high-resolution camera to observe and capture the dynamic displacement process
Features an anti-vibration platform, enabling stable high-resolution imaging
Containers and
back pressure value
Integrated operating interface
Long-focal-length optical microscope
Fluorescence microscope

## Slide 8: Microfluidic chips
8
Two important elements in the design and fabrication process
Geometry of the small volid space in the chip
Materials used to fabricate the chip (eg. silicon, glass)
Examples of geometries of microfluidic void spaces
Schematics for dry etch and wet etch (Anbari et al., 2018)
Microfluidic Chips are made for different research goals (multiphase flow, wettability, mineral reactions…) and rock structures.
(Gu et al., 2011)
(Gu et al., 2011)
(Willingham et al., 2008)
(Xu et al., 2017a)
(Gunda et al., 2011; Anbari et al., 2018)
(Park et al., 2012)

## Slide 9: Geochemical processes in fractured system
9
Chemical reactions in GCS sites (Dai et al., 2020)
Carbonate rocks dissolution
Formation of carbonic acid
Formation of secondary precipitation
Pore space is decomposed into two regions:
Dead-end fractures (immobile zone)
Diffusion-dominant reaction zone
No impact on primary flow channels
Flowing fractures (mobile zone)
Depends on ratio of flow to dissolution
Precipitation can cause clogging
Investigating how fracture characteristics impact reactions using micromodel.
1
2

## Slide 10: Micromodel design
10
Conventional microfluidic chips
Lack of real mineral composition and geochemical reactivity
Smooth surfaces, absence of natural pore surface roughness
Uniform and unstable wettability
Rock-on-a-chip
（Rajveer Singh et al., 2017）
（Bowen Ling et al., 2021）
Flow channel design
55*55*0.2mm
Micromodel with a main channel and lateral cavities
Main channel : 200μm
7 dead-end channels
DEP aspect ratio:1, 2, 4, 5, 10
Calcite grains were placed inside the cavity
-calcite
Exploring how dead-end geometry affects mineral reactions.

## Slide 11: Micromodel Fabrications
11
Samples preparation
Calcite
Thin slices
Grind and polish
1*1*0.2mm
Fabrication workflow
Deep silicon etching
Drilling for inlet/outlet holes
Loading the calcite samples into the cavity.
Anodic bonding to a cover glass plate.
Cutting for favorable chip size.
Photomask preparation
Photoresist deposition
Photolithography
Development
Preprocessing
Notes: In our laboratory, microfluidic chips are fabricated from glass. The fabrication follows standard photolithography and hydrofluoric acid etching procedures. The workflow includes seven main steps: 1) photomask preparation, 2) photoresist deposition, 3) photolithography (with photomasks that have the desired geometry patterns), 4) development, 5) HF etching, 6) glass cutting and drilling for favorable chip size and inlet/outlet holes, 7) thermal bonding to a plain cover glass plate. In the following sections we detail the steps of the workflow.

## Slide 12: Experiments in dead-end fractures
12
Post-Experimental analyses
Confocal Laser Scanning Microscope
Scanning Electron Microscopy
(mineralogy)
Experimental conditions
T(℃) | Pconf | Pback | Flow Rates(μL/min)
50 | 9 | 8 | 0.1 or 1 or 10
Future work
Simulating authentic reservoir conditions
Different flow rates corresponding to varying Péclet numbers
Constant-flow injection
Conduct microfluidic experiments to visualize calcite dissolution (and subsequent reprecipitation inside dead-end pores at 50 ℃ and 8 MPa.
Study the correlation between micro-scale dissolution regimes and Péclet numbers in dead-end pores under confinement.
Quantitatively interpret the experimental phenomena using the lattice Boltzmann method (LBM).

## Slide 13: Thank you for listening！
13
Email：
652025840006
@smail.nju.edu.cn