## Slide 1: Hydrogen and Brine Displacement Processes in Clashach Sandstone: Relevance of Haine´s Jumps and Intermittent Flow
Eike M. Thaysen, Ian B. Butler, Damien Freitas, Aliakbar Hassanpouryouzband, Catherine Spurin, Roberto Rizzo, Fernando Alvarez Borges, Robert Atwood, Katriona Edlmann
Grant number EP/S027815/1

## Slide 2
H2 fluid flow
injectivity
recoverability
INTERSEASONAL POROUS MEDIA H2 STORAGE- A TECHNOLOGY IN ITS INFANCY SHOES
Notes: H2 storage in porous media could be a corner stone in our transition to a zero carbon society, providing H2 energy with the necessary large storage capacities. But several uncertainties are still connecting to H2 storage in porous media –one of them being the H2 fluid flow affecting the H2 injectivity and recoverability

## Slide 3
Rock sample inside X-ray transparent
pressure vessel
4 high pressure pumps for injecting H2 and brine, for the confining pressure and for backpressure
HIGH PRESSURE APPARATUS FOR VISUALIZING H2 FLOW IN ROCKS

## Slide 4
(d)
H2
H2
brine
rock
H2
0.5 mm
H2 (black) fills the centre of the pores
Residual brine (dark grey) remains in corners, pore throats and in thin films around grains
Clashach sandstone after injection of 10 PV of brine (0.5 M CsCl) followed by 10 PV H2
H2 BEHAVES AS A NON-WETTING PHASE
Thaysen et al., 2023, Int J Hydrogen Energy, 48 (8), 3091-3106
Notes: Moving on to the results what you see here is a an image that was taken after saturation of the rock sample with 10 pore volumes of brine (where we used 0.5 molar Cesium chloride) and subsequent injection of 10 pore volumes of hydrogen. The rock is shown in different tones of light grey, the brine appears as dark grey and the hydrogen is black.
Looking more closely at the distribution of brine and hydrogen in the pore space we see that the hydrogen fills the centre of the pores with residual brine shown in the pore throats and corners, and as thin films around grains.
So clearly, hydrogen behaved as a nonwetting phase and brine as a wetting phase in our experiments.

## Slide 5: STEADY STATE INJECTIONS @ 1:1 INJECTION RATIO 20-22% H2 SATURATION & WEAK CONNECTIVITY

## Slide 6: STEADY STATE INJECTIONS @ 4:1 INJECTION RATIO H2 SATURATION INCREASES UP TO 28%. WEAK H2 CONNECTIVITY
Miniminal influence of connectivity on pore space saturation
Thaysen et al., 2025, J Colloid Interface Sci, 694 (137704)

## Slide 7: H2 FILLING OF PORE SPACE: INTERMITTENT FLOW IN PARTS OF THE VOLUME
Darcy´s law, widely applied for reservoir
simulations, assumes continuous flow
Thaysen et al., 2025, J Colloid Interface Sci, 694 (137704)
Ca=4.7 ×10-9

## Slide 8: STEADY STATE INJECTIONS @ 1:1 INJECTION RATIO INTERMITTENT FLOW
volume of H2 moving intermittendly is minor
Thaysen et al., 2025, J Colloid Interface Sci, 694 (137704)

## Slide 9: PRESSURE FLUCTUATIONS AT CORE OUTLET CONFIRM INTERMITTENT FLOW
Thaysen et al., 2025, J Colloid Interface Sci, 694 (137704)
injection ratio 4:1
red noise
injection ratio 1:1
Notes: Power spectra: Transformation of the pressure data into the frequency domain using a continuous wavelet transformation
At both the 1:1 and 4:1 H2/brine injection ratios, the pressure oscillations had intervals of 2-3 minutes (Fig. 9b and d; ´bumps at ̴ 10-2´). Both injection schemes were characteristic of red or Brownian noise, i.e. pressure signals produced by Brownian motion (shown by the red dashed lines in Fig. 9b and d). The pressure signal prior to gas arrival was characterized by white noise (random noise for frequencies > 10-3 Hz; SI Fig. S4).
Red noise indicates a stochastic process where pressure fluctuations are seen throughout the pore space, resulting in intermittent filling of pores over a wide range of time-scales, from seconds to minutes

## Slide 10: H2 RELATIVE PERMEABILITY ESTIMATION
LET MODEL
Lomeland, 2018
Lw = 8.0
Lg = 8.5
Ew = 0.06
Eg = 0.01
Tw = 2.0
Tg = 4.0
LET PARAMETERS
predictions of gas injectivity and recovery should be made with caution due to the neglection of the irreducible water saturation in fractional flow data
Flowrate: 20 µl min-1 (Nc: ~2*10-8 for drainage; ~2*10-6 for imbibition), Pc = 80 Bar, temp = ambient
Notes: Krevor et al. [59] observed similarly low CO2 saturation ratios and relative permeabilities in Berea sandstone at 50 °C and 9 MPa injection pressure (Fig. 11). Compared to CO2, H2 is more wetting (Fig. 11), as shown previously [60].

## Slide 11
2D radiography to provide insights on dynamic fluid processes that occur over timescales of 10s to 100s of milliseconds
Haines jumps are important energy-dissipating pore-scale events that are key to understand multiphase fluid flow
2D RADIOGRAPHS DURING
UNSTEADY STATE INJECTIONS:
HAINES JUMPS?
Thaysen et al., 2025, J Colloid Interface Sci, 694 (137704)

## Slide 12
2D RADIOGRAPHS DURING
UNSTEADY STATE INJECTIONS :
HAINES JUMPS IN ACTION
mean pore diameter: 0.035 µm
Thaysen et al., 2025, J Colloid Interface Sci, 694 (137704)

## Slide 13
Higher H2 fractional flow increased H2 saturation from 20-22% to 28%
lower H2 storage capacity in aquifers with higher hydrodynamic flow
H2 connectivity: weak and unchanged at different fractional flows
minimal influence of connectivity on H2 saturation
low H₂ recovery in aquifers with hydrodynamic flow
Intermittent flow detected but limited volume of fluctuating H2
applicability of Darcy´s law to describe the bulk H2 and brine fluid flow not challenged
Geological models should include Haines jumps and intermittent flow to improve accuracy
CONCLUSIONS
Notes: A higher H2 fractional flow of 0.75 relative to 0.5 increased the H2 saturation in the pore space from 20-22% to 28%, implying a lower H2 storage capacity in aquifers with higher hydrodynamic flow.
Hydrogen connectivity was weak and remained similar across different H2 fractional flows, indicating minimal influence of connectivity on pore space H2 saturation, and suggesting low H₂ recovery in aquifers with hydrodynamic flow, which may adversely affect the economic feasibility of the storage operation.
Confirm at higher resolution
Intermittent flow was detected in parts of the rock during steady-state injections, but the volume of fluctuating H2 was limited, indicating that the applicability of Darcy´s law to describe the bulk H2 and brine fluid flow based on relative permeability and capillary pressure was not challenged

## Slide 14
Confirm connectivity at higher resolution
Determine the capillary number at which intermittent flow will affect macroscale flow behaviour
lower viscosity ratio → relatively more intermittent flow can be expected for a given flow rate and shifts in the relative permeability can be expected at lower capillary number than for N2.
FUTURE EXPERIMENTS
N2 steady state experiments
Spurin et al. (2019): Adv Water Res 150 (103868),1-7
Notes: The fraction of intermittent flow is likely to increase at flow rates corresponding to higher capillary numbers. To model intermittent flow alongside laminar flow, new reservoir models incorporating Navier-Stokes equations may have to be developed. Future experiments should quantify the volume of H2 fluctuating intermittently as a function of capillary number and fractional flow to quantify the increase of intermittent flow with increasing capillary number and to determine the capillary number at which intermittent flow will affect macroscale flow behaviour such as the relative permeability.
Considering the lower viscosity ratio of the H2-brine system compared to the N2-brine system, relatively more intermittent flow can be expected for a given flow rate and shifts in the krH2 can be expected at lower Nc than for N2.

## Slide 15
Thank you!
eike.thaysen@idaea.csic.es

## Slide 16: H2 RELATIVE PERMEABILITY ESTIMATION
LET MODEL
Flowrate: 20 µl min-1 (Nc: ~2*10-8 for drainage; ~2*10-6 for imbibition), Pc = 80 Bar, temp = ambient
Lw = 8.0
Lg = 8.5
Ew = 0.06
Eg = 0.01
Tw = 2.0
Tg = 4.0
LET PARAMETERS
high permeability relative to previous studies in similar systems
predictions of gas injectivity and recovery should be made with caution due to the neglection of the irreducible water saturation in fractional flow data
Notes: Krevor et al. [59] observed similarly low CO2 saturation ratios and relative permeabilities in Berea sandstone at 50 °C and 9 MPa injection pressure (Fig. 11). Compared to CO2, H2 is more wetting (Fig. 11), as shown previously [60].

## Slide 17
Key parameters:
Pore network connectivity, relative permeability/capillary pressure relationships with varying fluid saturation, porosity
Other parameters:
Wettability (contact angle between H2, brine and rock), tortuosity, absolute permeability
Cushion gas
Biofilm
PARAMETERS THAT AFFECT H2 INJECTIVITY & RECOVERY
Clogging of pores and pipes

## Slide 18
5 mm diameter Clashash sandstone
20-70 Bar
HIGH PRESSURE APPARATUS FOR VISUALIZING H2 FLOW IN ROCKS