## Slide 1: Underground Hydrogen Storage
Waleed Dokhon
Martin J. Blunt
Branko Bijeljic
The combined effects of pressure decline and gas withdrawal in UHS

## Slide 2: Why pressure decline in UHS is different
Rapid hydrogen withdrawal required to meet intermittent renewable power demand.
UHS operates fast pressure cycles (months), unlike decades-long oil and gas production.
UHS may experience significant pressure decline rates.
Rates of pressure decline can differ depending on aquifer strength (Alobaidan etl a., 2025).
Oil & Gas
CO2 Sequestration
Continuous production/injection
Pressure is mostly maintained
Mostly injection only
Pressure increases
UHS
Injection during excess energy => Pressure increases
Withdrawal during high demand (typically for 90 days) => Pressure declines, likely at a high rate
Chart: Date
| 2021-09 | 2021-10 | 2021-11 | 2021-12 | 2022-01 | 2022-02 | 2022-03 | 2022-04 | 2022-05 | 2022-06
 | 38932.681 | 0 | 42245.126 | 0 | 45119.104 | 0 | 48871.638 | 0 | 52922.332 | 0 | 46306.003 | 0 | 43244.911 | 0 | 36894.067 | 0 | 34181.928 | 0 | 31921.412
Source: EuroStat
Monthly energy demand in France
High demand
(withdrawal)
Low demand
(storage)
Figure: Depressurisation in an UGS reservoir
(Egermann et al., 2010)

## Slide 3: Has pressure decline been studied elsewhere?
Extensively studied in oil reservoirs via solution-gas drive and depressurisation.
Focus on gas exsolution and measuring the critical gas saturation.
Pressure decline rate has weak influence on the critical gas saturation (Bagudu et al., 2018).
Measuring Sgc at Sgi or Sgr shows different results (Egermann & Vizika, 2000).
Chart: Critical gas saturation (Sgc)
| Kamath & Boyer (1995) | Kamath & Boyer (1995) | Egermann & Vizika (2000) | Egermann & Vizika (2000) | Petersen et al. (2004) | Petersen et al. (2004) | Petersen et al. (2004) | Zuo et al. (2012) | Zuo et al. (2012) | Sun et al. (2018) | Sun et al. (2018) | Sun et al. (2018) | Berg et al. (2020) | Al-Masri & Shapiro (2021) | Al-Masri & Shapiro (2021) | Moghadasi et al. (2025)
Sgc | 0.1 | 0.1 | 0.2 | 0.48 | 0.05 | 0.09 | 0.13 | 0.11 | 0.155 | 0.036 | 0.047 | 0.0588 | 0.2 | 0.08 | 0.26 | 0.61
Pressure decline rate | 0.096 | 0.479 | 16.7 | 16.7 | 0.55 | 1.43 | 3.5 | 20 | 1000 | 6.7 | 13.3 | 26.7
Swir
Swi
Figure: Experimentally measured Sgc from previous studies and their PD rates
8 MPa
6 MPa
Sg = 0.58
Sg = 0.62
Trapped gas
Spanning gas
Figure: Stepwise pressure decline in CO2-brine system (Moghadasi et al., 2025)

## Slide 4: Pressure decline in UHS: Objectives
Most studies examine solution-gas drive, not the expansion of trapped gas.
Pressure decline is usually studied without simultaneous water injection.
Most studies ignore testing the impact of different initial conditions (Sgr vs Sgi).
Figure: Schematic of UHS in an aquifer showing the sequence of displacement events (Dokhon et al., 2025)
Connected gas phase
(Above GWC)
Trapped gas (below GWC)
Water
Connected gas
Trapped gas
Produced by expansion
Gas expansion
Sg > Sgr
Pressure
decline
Sg
Examine gas expansion due to pressure decline.
Study pressure decline with a continuous brine flow.
Study the impact of initial conditions.
Objectives
Literature gaps

## Slide 5: Theory
Continuous-phase pressure declines faster than trapped-gas pressure.
Local drainage displacement from each ganglion as Pc increases.
Pore pressure drop is proportional to gas volume increase (expansion)
Expansion number compares expansion-driven flow to brine-driven displacement.
Equate t to be the necessary time for displacement
To evaluate E at the time when Sgr reaches Sgc using eq. 2
1
2
3
Ideal gas law
Figure: Schematic of phase pressure
Figure: Pc(Sw) diagram
E = 70
at 0.05 ml/min Qw
E(Sgc) = 2×104
at Sgr =0.4 and
Sgc = 0.65
x
P
Pc
Time
Gas pressure (at Sgr)
Brine pressure

## Slide 6: Method: Experimental setup
Hydrogen-brine displacement in water-wet Bentheimer sandstone.
Impose controlled outlet pressure decline during brine injection.
Two initial conditions: High gas saturation (Sgi) and residual gas (Sgr)
Vary capillary number using two brine flow rates (10-8 – 10-7).
Track gas expansion, connectivity, and saturation using micro-CT.
(a) Dry: Full length scan (9.6 µm/voxel)
(b) Circular ROI scan (3.1 µm/voxel)
Figure: Flow loop schematic
Figure: Experimental sequence
Black: gas
Gray: solid
White: brine

## Slide 7: Method: Measurements
Bentheimer sandstone: 12.6 mm diameter, 36.1 mm length
Water-wet ceramic porous plate at outlet (Pe = 100 kPa)
Hydrogen-brine system at 4 MPa and 23°C.
Brine injection rates: 0.01 ml/min and 0.05 ml/min (capillary-dominated).
Programmed outlet pressure decline: 1 kPa/min.
Hydrogen exsolution estimated using Henry’s law
Gas dissolution assessed via saturation profiles and injected pore volumes.
L
L
Sg
Sg
Gas dissolution (transient)
No gas dissolution (uniform)
Figure: grayscale images of gas-saturated brine flooding the gas
Gao et al. (2023)

## Slide 8: Results: Tracking saturation and volume changes
Pressure decline increases gas saturation despite continuous brine injection.
Gas saturation increase scales approximately with fractional pressure drop.
Similar expansion behaviour observed at both brine flow rates.
Pressure decline starting at Sgi yields higher remaining gas saturation.
Most of the gas was produced by expansion rather than normal displacement.
Figure: Gas saturation profiles for every case
Figure: Ganglia counts (left) and volume (right) distributions
Reference: Dokhon, W., Bijeljic, B. and Blunt, M.J., 2026. The combined effects of pressure decline and gas withdrawal in underground hydrogen storage: A pore-scale experimental study. Advances in Geo-Energy Research, 20(1), pp.71-84.

## Slide 9: Results: Exsolved gas and gas dissolution quantification
Exsolved gas contribution in orders of magnitude smaller than expansion-driven saturation change
Exsolution increases slightly at lower gas saturation due to the higher brine volume.
Minimal gas dissolution observed at low injected pore volume (< 3 PV).
Inlet-side dissolution more pronounced due to pressure equilibration offset.
Figure: Exsolved gas contribution to the saturation
Figure: Comparing gas dissolution assuming no pre-equilibration (orange) vs observed gas saturation (blue)

## Slide 10: Results: 3D images of ganglia volumes

## Slide 11: Conclusions
Pressure decline shows drainage-dominated displacement at the pore-scale, even during continuous brine injection.
Gas saturation increases approximately proportional to the fractional pressure decline.
Better gas connectivity is observed when the initial condition is Sgi.
Hydrogen exsolution is negligible; gas expansion is the dominant mechanism.
Sgc measurement is strongly process-dependant.
The critical gas saturation was estimated to be larger than 0.55 at these conditions.
Future work
Measure gas relative permeability during pressure decline under steady-state conditions.
Evaluate the solution-gas drive by injecting H2-saturated brine and drop the pressure (gas nucleation).
Investigate the effects of wettability and heterogeneity.

## Slide 12
Published work
(This study) The combined effects of pressure decline and gas withdrawal in underground hydrogen storage: A pore-scale experimental study.
Pressure decline and gas expansion in underground hydrogen storage: A pore-scale percolation study.
Micro-CT imaging of drainage and spontaneous imbibition for underground hydrogen storage in saline aquifers.
connection
Roof snap-off
P = 570 kPa
P = 350 kPa
Pressure decline

## Slide 13: Thank you Happy to discuss and answer questions!
Email - waleed.dokhon21@imperial.ac.uk
LinkedIn profile

## Slide 14: What we learned previously
Compare the pore filling of hydrogen in gas injection vs gas expansion.
Drainage and Sgi by:
gas expansion vs gas injection
connection
Roof snap-off
P = 570 kPa
P = 350 kPa
Pressure decline
Figure: Sample schematic
Injection
Expansion
Figure: Pore occupancy
Figure: 3D gas images in injection vs expansion
Figure: Example of Roof snap-off

## Slide 15: What we learned previously
Porous plate as an aquifer source
Reduce Pc gradually
Perform water injection at Pc = 0
Spontaneous imbibition and Sgr
Figure: Gas saturation profiles and their corresponding pressure drop
Figure: Gas rearrangement at Pc = 0
Figure: Gas connectivity with dropping Pc
Figure: Pc(Sw) diagram of drainage, SI, and brine injection