## Slide 1: 4D X-ray particle tracking velocimetry of multiphase flow through rough fractures: quantifying influence of roughness on flow dynamics
department of Geology
  research group PProGRess
Sojwal Manoorkar, Robert Van der Merwe, Sharon Ellman, Parsa Damanshokouh, Hossein Younesian Farid, Andreas Busch, Tom Bultreys

## Slide 2
Why is flow in fractures important?
https://www.fluxys.com/en/hydrogen/activities/loenhout-hydrogen-underground-storage
First of their kind field tests
State-of-the-art Laboratory Experiments
Van der Voet et al 2020
Manoorkar et al (2026)
Notes: Can lab-based 4D micro-CT and PTV connect rough-fracture pore-scale displacement events to measurable macroscopic flow signals?

## Slide 3
Outline
Interface dynamics: multiphase co-injection
Methodology: lab-based micro-CT
4D Velocimetry: Smooth vs rough fractures

## Slide 4
Outline
Interface dynamics: multiphase co-injection
Methodology: lab-based micro-CT
4D Velocimetry: Smooth vs rough fractures

## Slide 5
Drainage core-flooding with dynamic scanning with 30s at 12µm
Exp 1: co – injection
Goal : Dynamic interface
Exp 2: single injection
Goal : Particle - tracking velocimetry
Flow Regimes:
Samples:
Fluids:
Oil
Brine
∆P
1. wetting phase: 96 wt% glycerol +KI
2. non-wetting phase: silicon oil
1. wetting phase: 96 wt% glycerol +KI
2. non-wetting phase: silicon oil + Ag coated hollow glass spheres as tracers
Capillary dominated
1. Viscosity ratio (M) ~ 1
2. Capillary number (Ca) = 10-6 - 10-5
Capillary dominated
1. Viscosity ratio (M) ~ 1
2. Capillary number (Ca) = 10-6 - 10-5
Carmel Sandstone
Carmel Sandstone
Belgian blue limestone
Notes: Reduction in global emissions
Green economy
Current ongoing projects
Potential sites
Goals and how much it can reduce the emissions
Blue hydrogen, green hydrogen, gray hydrogen

## Slide 6
Bultreys et al (2022)
Oil
Brine
Exp 1: co – injection
Goal : Dynamic interface
Exp 2: single injection
Goal : Particle - tracking velocimetry
Dynamic events
Rucker et al (2015)
From 4D interface dynamics to Lagrangian flow pathways
Notes: Reduction in global emissions
Green economy
Current ongoing projects
Potential sites
Goals and how much it can reduce the emissions
Blue hydrogen, green hydrogen, gray hydrogen

## Slide 7
Outline
Interface dynamics: multiphase co-injection
Methodology: lab-based micro-CT
4D Velocimetry: Smooth vs rough fractures

## Slide 8
Dynamic connectivity with evolving topology
Dynamic connectivity over time
Dynamic connectivity over increasing fractional flow
Foil = 0.2
Foil = 0.4
Foil = 0.6
Foil = 0.8
Brine
Oil

## Slide 9
Snap-off events are captured in macroscopic pressure signals for low fractional flow
Foil = 0.4
Brine
Oil
Event A
Event B
Event B
Event A

## Slide 10
Snap-off events are sensitive to local geometry: adjacent aperture distribution

## Slide 11
Interface and pressure fluctuations dampen on a matched ~20-min timescale at moderate fractional flow
Brine
Foil = 0.6
Oil

## Slide 12
Outline
Interface dynamics: multiphase co-injection
Methodology: lab-based micro-CT
4D Velocimetry: Smooth vs rough fractures

## Slide 13
Stable displacement
Unsteady-state drainage experiments with dynamic scanning with lab based micro-CT
Oil segmented
Lagrangian Particle tracks

## Slide 14
Cubic-law validation with velocity field

## Slide 15
Carmel rough fracture shows complex dynamics
Oil segmented
Lagrangian particle tracks

## Slide 16
Scientific:
Pore-scale topology events leave macroscopic pressure signatures
Moderate fractional-flow transitions are non-stationary: saturation and pressure fluctuations decay together over ~20 min
Lab-based PTV recovers cubic-law in smooth fractures and resolves complex Lagrangian dynamics in rough ones
Methodological:
Established methodology for range of M and Ca using lab-based micro-CT for multiphase flow in rough fractures
Tracking could be improved with larger and higher atomic number metal coating
Summary and Prospectives
Notes: arXiv papers

## Slide 17
Acknowledgements