## Slide 1
Christopher Zahasky
Associate Professor, Department of Geoscience
University of Wisconsin-Madison
Email: czahasky@wisc.edu
Website: Zahasky.geoscience.wisc.edu
InterPore 2026– May 22, 2026
Collin Sutton
NSF-EAR Postdoctoral Fellow
Colorado School of Mines
Email: Collin.Sutton@Mines.edu
Optimization and experimental validation of graph-based model of complex transport processes in fractured porous media

## Slide 2: Modeling transport on graphs lead to 4-5 orders of magnitude speed up
[Karra et al, 2017]
DFN model
Graph model
Notes: Graph based models are a way to represent fractures with a small number of nodes and edges rather than a fully meshed discrete fracture network. This reduced-physics representation has been shown to enable 4-5 orders of magnitude speed up in computational time.

## Slide 3: Despite the promise of graph models, validations against observational data is lacking
Current Objectives
Validate first-order reactions and fracture/matrix processes on graph-based flow and transport models in fractured rock cores
Determine if models can capture more complex, meso-scale fracture flow and transport behavior
Design flexible optimization framework for robustly fitting graph-based models to observational data across scales

## Slide 4: Core-scale Experiments
Confining fluid
Core/fracture
End caps
Flow direction
Shrink wrap and neoprene
Inlet port
10 cm
5.08 cm
Niagaran Dolomite
Berea Sandstone
Sierra Granite
Outer coreholder

## Slide 5: Core-scale Experiments Imaged with Positron Emission Tomography (PET)
Confining fluid
Core/fracture
End caps
Flow direction
Shrink wrap and neoprene
Inlet port
Outer coreholder
Scanner parameters:
30-60 second timesteps
Voxel dimension = 0.77 x 0.77 x 0.8 mm
[Zahasky et al, 2019]
PET scanner
Radiotracer sensors measure inlet and outlet radioconcentration

## Slide 6: Core-scale Tracer Experiments Imaged with PET
Scanner parameters:
60 second timesteps
Voxel dimension = 0.77 x 0.77 x 0.8 mm
Experiment parameters:
0.5 mL/min flow rate
1mL injection of 18F-FDG tracer
Direction of flow
Distance from inlet [cm]
PET scanner
Radiotracer sensors measure inlet and outlet radioconcentration

## Slide 7: Core-scale Colloid Experiments Imaged with PET
Scanner parameters:
60 second timesteps
Voxel dimension = 0.77 x 0.77 x 0.8 mm
Experiment parameters:
0.5 mL/min flow rate
1mL injection of 64Cu-labeled kaolinite
Direction of flow
PET scanner
Radiotracer sensors measure inlet and outlet radioconcentration

## Slide 8: Graph network from PET images
Peak PET voxel concentrations used to make graphs from transport data
Heirarchical-based clustering approach for nodes [Ester et al., 1996]
K-nearest neighbors for edge connection

## Slide 9: Solve flow equations
Finite volume resistance network formulation
[Moreno et al, 1988]
Constant flow nodes
Constant pressure nodes

## Slide 10: Solve for transport with Time Domain Random Walk Model
Empirically corrected lognormal PDF used when edge Pe > 10
Lookup table at Pe <10, draw a random uniform number from (0,1) and lookup to determine travel time.
Matrix diffusion
First order reactions if deposition/reaction time is less than travel time
[Bodin et al, 2023]
[Yosri et al, 2020; Liu et al, 2022]
[Liu et al, 2022]
Notes: To match laboratory experiments where breakthrough is measured at a detector connected to the
fracture outlet by tubing of length Lt and inner radius rt, particle arrival times are convolved with
a Taylor–Aris response

## Slide 11: Fractured Sierra granite with subtle matrix diffusion and colloid transport
First-order attachment term and dispersivity are the only colloid transport tuning parameters relative to tracer fit

## Slide 12: In addition to breakthrough curves, we can also compare deposition profiles
Flow solution

## Slide 13: In addition to breakthrough curves, we can also compare deposition profiles
Flow solution

## Slide 14: … but what about more complex fracture networks and boundary conditions?
Notes: these graph-based models can describe flow, transport, matrix diffusion, and first-order reactions at the core scale

## Slide 15: Use multiwell fracture caging to generate hydraulic fractures in laboratory
[Frash et al, 2021]
31MPa
5.9MPa
Same well arrangement but in granite block
(45 x 30 x 30 cm) under triaxial stress conditions

## Slide 16: Multiwell tracer tests
31MPa
5.9MPa
BTC at open wells measured with custom flow-through cuvette in UV-Vis spectrophotometer
Fluorescene tracer injected into center well

## Slide 17: Initial graph parameterization uses known wells at nodes and random interior nodes
Side view
Top view
5 cm

## Slide 18: Initial graph parameterization uses known wells at nodes and random interior nodes
Constant pressure nodes
Constant flow node

## Slide 19: Given a fixed network geometry, we can apply classic inversion methods to fit node apertures and global transport parameters to pressure, flow, and BTC observations.
Ensemble Smoother Multiple Data Assimilation (ES-MDA) with 2000 models runs each flow iteration in 20 seconds on 8 processors.
Misfit reduction across 12 ES-MDA iterations

## Slide 20: Given a fixed network geometry, we can apply classic inversion methods to fit node apertures and global transport parameters to pressure, flow, and BTC observations.
Ensemble Smoother Multiple Data Assimilation (ES-MDA) with 2000 models runs each flow iteration in 20 seconds on 8 processors.
Misfit reduction across 12 ES-MDA iterations
Posterior models
Well 2 Experiment
Notes: 15 min per TDRW iteration on downsampled ensemble of 400 models

## Slide 21: The next step is to assimilate acoustic emission and strain data to constrain graph parameters
[Opperman MS, 2026]
Time-resolved granite block deformation measured with DSS
Fiber optic strain measurements
Notes: Distributed Strain Sensing - Fiber sensing is interferometry
Rayleigh Optical Frequency Domain Reflectometry
Frequency Sweep
Differences in beat frequency encode strain and temperature changes
Hydromechanical coupling was documented with DSS data
Flow controls fracture extent and velocity
Caged geothermal systems were successfully created and described in lab-scale granite samples.

## Slide 22: Summary
At the core scale, graph-based models can effectively describe flow, transport, matrix diffusion, first-order reactions, and colloid transport.
Models fit to one set of conditions can be used to forecast to other system physics or boundary conditions.

## Slide 23: Summary
At the core scale, graph-based models can effectively describe flow, transport, matrix diffusion, first-order reactions, and colloid transport.
Models fit to one set of conditions can be used to forecast to other system physics or boundary conditions.
The computational efficiency of graph-based models enables ensemble-based inversion methods
Ongoing work is focused on assimilating multiple datastreams, geometry optimization, and increasing TDRW model speed.
KNN - 4

## Slide 24: Questions? Interested in this work? I’m looking for PhD students and postdocs!
C/C0
  References:
  Zahasky et al, (2019) Positron emission tomography in water resources and subsurface energy resources engineering research. AWR
  Sutton and Zahasky (2024) In Situ Quantification of Colloidal Kaolinite Transport and Attachment in Porous Media Using Positron Emission Tomography. TiPM
  Sutton and Zahasky (2025) A laboratory‐validated, graph‐based flow and transport model for naturally fractured media. GRL
Frash, L., et al (2021) Fracture Caging to Limit Induced Seismicity. GRL
  Liu, L., et al. (2022) A new analytical solution of contaminant transport along a single fracture connected with porous matrix. J. Hydrology
InterPore 2026– May 22, 2026
Grant No. 66040-DNI9
Grant No. 2002412,
2437912
  Email: czahasky@wisc.edu

## Slide 26
Extra slides

## Slide 27: Creating Axial-Parallel Fractured Cores

## Slide 28: Solve for transport with Time Domain Random Walk Model
Empirically corrected lognormal PDF used when edge Pe > 10
Lookup table at Pe <10, draw a random uniform number from (0,1) and lookup to determine travel time.
[Bodin et al, 2023]
KS distance between CDF of TDRW methods and analytical solution
Notes: To match laboratory experiments where breakthrough is measured at a detector connected to the
fracture outlet by tubing of length Lt and inner radius rt, particle arrival times are convolved with
a Taylor–Aris response

## Slide 29: Solve for transport with Time Domain Random Walk Model
Empirically corrected lognormal PDF used when edge Pe > 10
Lookup table at Pe <10, draw a random uniform number from (0,1) and lookup to determine travel time.
Matrix diffusion
First order reactions if deposition/reaction time is less than travel time
[Bodin et al, 2023]
[Yosri et al, 2020; Liu et al, 2022]
[Liu et al, 2022]
Notes: To match laboratory experiments where breakthrough is measured at a detector connected to the
fracture outlet by tubing of length Lt and inner radius rt, particle arrival times are convolved with
a Taylor–Aris response

## Slide 30: Graph model with no matrix diffusion or reactions was compared with core-scale experimental data in our paper last year
Model fit to one experiment showed generalizability across experiments with different boundary conditions without tuning

## Slide 31: Fractured dolomite with subtle matrix diffusion and first-order decay
First-order reaction uses exact 18F half-life and model uses measured porosity.

## Slide 32: Exploring different connectivity algorithms (K-nearest neighbors vs Gabriel graph)
Gabriel graph
KNN - 4
Constant flow node
Notes: Knn and Gabriel graph with 50 total nodes
Two nodes are Gabriel neighbors if the smallest circle/sphere through both of them is "empty" of other points.
Gabriel graph is a subgraph of the Delaunay triangulation. Every Gabriel edge is a Delaunay edge. This makes sense because both are "empty region" graphs — Delaunay requires some empty circle through the two points, while Gabriel requires the specific diametral circle to be empty, a stricter condition.

## Slide 33: System is also instrumented with distributed strain sensing and acoustic emission sensors
31MPa
5.9MPa
Same well arrangement but in granite block under triaxial stress conditions
Fiber optic strain measurements