## Slide 1
Microfluidic platforms for anaerobic hydrogen–mineral–microbial reactions
Na Liu | University of Bergen
Edgard Frank Viveros Acosta, Chaojie Cheng, Christian Ostertag-Henning
InterPore Conference, Nantes, France 2026

## Slide 2
The micromodel for biogeochemical study duirng UHS
Naga Siva Kumar Gunda, et al. Lab on a Chip 2011. 22: p. 7.
Micromodel = microfluidic representation of porous media
Micromodels provide direct visualization of these coupled pore-scale processes that are difficult to observe in conventional core-scale experiments.
Microbial processes Biofilm growth, hydrogen consumption, sulfate reduction, and bioclogging
Flow & transport:
Hydrogen distribution, phase trapping, accessibility, and mass transfer at the pore scale
Mineral reactions: Dissolution, precipitation, and microbe–mineral interactions under reactive flow conditions

## Slide 3
A three-platform strategy: pressure control → chemistry → geological realism
Platform comparison: which research questions can each chip answer reliably?
Platform I — Silicon–glass chip
High P–T, gas-tight, quantitative flow and biofilm analysis.
Synthetic minerals (calcite, gypsum)
Platform II — Polymer ibidi chip
Real mineral grains, excellent Raman/confocal compatibility.
Ambient pressure condition
Platform III — Real-rock chip
Real pore texture, roughness and mineral heterogeneity.
Limited control, ambient pressure condition

## Slide 4
Representative case
Hydrogen-driven sulfate reduction in porous media
Research question: Which microfluidic platform can directly observe H₂ transport, microbial activity, and mineral reactions under relevant experimental conditions?
Biofilm

## Slide 5
Platform I — silicon–glass high-pressure micromodel
Experimental capability
What we can measure
H₂ consumption,
biofilm-induced bioclogging,
wettability changes,
flow redistribution.
Main limitation
Idealized geometry/surfaces
Limited Raman access through thick glass.
Reservoir-relevant pressure and temperature
stable anaerobic condtions
quantitative pore-scale flow visualization

## Slide 6
Multimineral reactive micromodel
Gypsum
Vaterite
Calcite
Silicon pillar
Base geometry: silicon micromodel
Mineral phases introduced:
  Calcite&Gypsum (sulfate source)
Controlled pore structure
Enables direct observation of H₂ transport, microbial activity and mineral reactions under reservoir conditions.

## Slide 7
Example from platform I: biofilm growth changes flow
This platform is strongest for dynamic flow–biofilm coupling.
Liu et al. 2025, https://doi.org/10.1021/acs.est.4c13893

## Slide 8
Example from platform I: gypsum dissolution
The reaction rate is controlled by local mass transfer, not mineral chemistry alone.
Dissolution is delayed and reduced when gas surrounds the mineral.
0h
6h
15h
25h
0h
33h
59h
149h

## Slide 9
Platform II — ibidi chip coupled with Raman/confocal microscopy
N2 gas
In situ Raman measurement
Work done in BGR
Raman objective
Laser
Scattered Raman light
In situ Raman spectroscopy for chemical mapping in a reactive microfluidic system.
Ibidi microfluidic channel
Optical images
Biofilms
Representative Raman spectra
This setup enables non-destructive, in situ chemical mapping of biofilms and minerals at the pore-scale.
Work from Dr. Christian Ostertag-Henning, BGR

## Slide 10
Platform III — Real rock chip
Real-rock micromodel containing sulfates and carbonates for bio-geochemical reactions.
  Natural rock texture and heterogeneity
  Contains sulfates & carbonates
  (e.g., limestone, calcite, dolomite, anhydrite)
A realistic platform for studying coupled transport, biofilm activity, and mineral reactions in porous rocks.
Real rock chip thin section
Work from Dr. Chaojie Cheng, KIT
Real rock chip
Micromodel assemply

## Slide 11
Platform comparison: complementary, not competing
Physical chip (UiB)
Silicon-glass chip
Chemical chip (BGR)
Polymer(ibidi) chip
Real-rock chip (KIT)
Thin section chip
Strengths:
High P–T (up to 150 bar)
Gas-tight → stable anaerobic conditions
Quantitative flow & biofilm analysis
Limitations:
Idealized geometry
Limited Raman access
Strengths:
Raman + confocal compatible
Good for chemical mapping
Controlled anaerobic conditions
Limitations:
Atmospheric pressure
Simpler flow conditions
Strengths:
Natural mineralogy & roughness
Real pore structure
High geological realism
Limitations:
H₂ leakage risk
Experimental constraints
No single platform is sufficient, mechanistic understanding requires integration.
Chemistry
Dynamics
Mineral heterogeneity

## Slide 12
Conclusion
Outlook
Integrating complementary micromodels provides a stronger framework for studying biogeochemical processes relevant to underground hydrogen storage.
Platform | Research questions
Silicon–glass HP chip | Dynamic H₂ transport, pressure effects, quantitative biofilm–flow feedback
Ibidi polymer chip | Interfacial chemistry, spatial sulfate depletion, biofilm localization, In situ Raman/confocal imaging and interfacial chemistry
Real-rock micromodel | Mineral heterogeneity, natural pore structure, and realistic rock surfaces influence microbial colonization, H₂ accessibility, and mineral reactions
Micromodels resolve coupled H₂–microbe–mineral processes at the pore scale
…but no single platform captures all relevant subsurface conditions.

## Slide 14
https://hydrahydrogen.eu