## Slide 1: Model Calibration and Prediction of Biogeochemical Processes in Porous Hydrogen Storage Birger Hagemann Clausthal University of Technology Nantes, May 20, 2026
Presented at:

## Slide 2: Content
Introduction
Reactive transport model
Model calibration by experimental studies
Model validation
Conclusions & learnings

## Slide 3: Introduction – Underground Hydrogen Storage
(Laminar) flow through the porous rock
Horizontal dimension much larger than vertical dimension
  Flow predominantly in horizonal direction
Mobile water might be present
  Two-phase flow
Schematic structure of a pore storage
(Source: Adapted from Katz & Lee (1990))
Underground hydrogen storage enables large-scale balancing of renewable energy

## Slide 4: Introduction – Relevant transport and reactive processes
Advective flow and mechanical dispersion in high permeable layers
Molecular diffusion in lower permeable (water-saturated) layers
Microbial reactions:
e.g. methanogenesis:
and sulfate reduction:
caprock
storage rock
underlying rock
H2
H2
H2
H2
H2
H2
CH4
CH4
CH4
CH4
H2
caprock
storage rock
underlying rock
H2
H2
H2
H2
H2
H2
CH4
CH4
CH4
CH4
H2
During and after injection
During and after withdrawal
Molecular diffusion
Mechanical dispersion
Microbial reaction
Adapted and extended from Arekhov et al. (2023)

## Slide 5: Reactive transport model – Assumptions and scales
Various physical, chemical and biological processes on different time and length scales
Upscaling to Darcy scale by using a representative elementary volume:
Further assumptions:
  Kinetic consideration of bio-reactions
  Thermodynamic equilibrium for dissolution/vaporization
Continuum scale for lab and field scale simulation

## Slide 6: Reactive transport model – Equations
Multicomponent two-phase (gas – water) reactive transport model based on Darcy’s law:
Population dynamics for microbial species:
Numerically implemented in DuMux
Diffusive and dispersive transport
Bio-reactions
Advective flow/transport
Microbial growth

## Slide 7: Model calibration by experimental studies
Effective molecular diffusion coefficients
  Measurements on over 50 real rock samples under reservoir conditions
  Development of a correlation for simulation models:
Mechanical dispersivity
  ~20 measurements using a 25 m slim tube coil filled with porous material under reservoir conditions
  Development of a correlation for simulation models:
Microbial growth and reaction kinetics
  Observations of microbial behavior using a microfluidic setup with methanogenic archaea and an H₂/CO₂ gas mixture
  Development of a new model for growth and reaction kinetics
Microscopic image of the gas-water saturated pore space partially populated with microbes
Range of effective diffusion coefficients

## Slide 8: Model validation by field test data
Near-wellbore region around the operational well
Investigation of layered model realizations
Main calibration parameters
  Mechanical dispersivity ()
  Reaction kinetic parameters
Reservoir
K=0.4 ∙ K, φ=φ, Sw=0.5
K=K, φ=φ, Sw=0.15
Single-layered
K=1.6 ∙ K, φ=φ, Sw=0.15
Reservoir
Multi-layered
H2
CO2
H2S
No flow BC (Neumann)
No flow BC (Neumann)
Open BC (Dirichlet)
Open BC (Dirichlet)

## Slide 9: Conclusions & Learnings
A mathematical model for the bio-reactive two-phase flow in UHS was developed and numerically implemented
Different laboratory measurements are applied for calibrating and improving the model
  Gas mixing effects: Effective diffusion coefficients and mechanical dispersivities
  Microbial growth and reaction kinetic function and empirical coefficients
Multi-layer reservoir characteristics are important during initial filling and early H₂ cycling
  In high-permeability rocks, mechanical dispersion can dominate over molecular diffusion even at low flow velocities
  In low-permeability, water-saturated rocks, molecular diffusion is the dominant transport mechanism
Model validation through history matching with field data is ongoing
  Numerical diffusion/dispersion should be minimized but is challenging to be reduced below physical levels
Measurement uncertainties (lab and field) must be considered
  Model calibration should not exceed data accuracy limits

## Slide 10: Thank you for your attention!

## Slide 11: Experimental setup and procedure
Dynamic experiments using methanogenic archaea and a H2-CO2 gas mixture
  Preparation of a 5 ml nutrient-microbial mixture
  Attain a liquid-phase saturation inside the micromodel
  Inject 5 bar pressurized H2-CO2 into the micromodel
  Divert gas flow to the gas chromatograph
  Maintain constant injection rate of 2.8 µl/min
  Repeated gas composition measurement and image acquisition of microbial count
50 mm
9 mm

## Slide 12: Microbial growth and metabolic reactions
Double Monod model extended by population limit function to describe microbial growth
Population limit function
Metabolic reaction rate