## Slide 1: Design of a microfluidic setup to assess scale-dependent metabolic kinetics in Azotobacter vinelandii biofilms producing polysaccharides
Loisa Borde1,2, Maike Werdin1, Stefanie Duvigneau3, Nicole Vorhauer-Huget1
1 Chair of Thermal Process Engineering, Otto von Guericke University, Magdeburg, Germany
2 Process Synthesis and Process Dynamics, Max Planck Institute for Dynamics of Complex Technical Systems, Magdeburg, Germany
3 Technical University of Munich, Germany
InterPore 2026
18th annual meeting & conference courses
19th – 22nd May 2026, Nantes, France
loisa.borde@ovgu.de

## Slide 2: Productive Biofilms For biopolymer Production
Biofilms: microbial communities embedded in extracellular polysaccharides (EPS) that adhere to surfaces
A. vinelandii produces biofilms consisting of alginate (biopolymer used in food industry and medicine)
Media with high surface-to-volume ratio  increased biofilm formation  increased alginate production
Schematic overview of biofilm formation
loisa.borde@ovgu.de

## Slide 3: Pore Network Model (PNM)
Pore Network Model: biofilm formation in porous structures
Experimental data for model parametrization and validation
  Boundary and initial conditions
  Transport parameters (permeability, diffusion)
  Maximum biofilm thickness
  Attachment and detachment of biofilm
loisa.borde@ovgu.de

## Slide 4: Motivation and Goals
Polymer production for food industry and medical applications
Production of biopolymers using bacteria
Biofilm formation in porous substrates
Experimental data for modeling
Objective: investigate biofilm formation and measure kinetic parameters
loisa.borde@ovgu.de

## Slide 5: Development of Experimental SetUP For Biofilm formation
Devices fabricated from polydimethylsiloxane (PDMS)
Channel geometry designed to imitate a single pore enabeling geometry-dependent biofilm formation (V = 400 µl)
Medium
Peristaltic pump
PDMS Device
Inoculation with cultures pre-grown in shaking flasks
Continuous medium flow: 40 µl/min for 9 days
8 mm
10 g/l Sucrose
10 g/l Succinate
Salt solution
Phosphate buffer
loisa.borde@ovgu.de
30 mm
Experimental setup for biofilm cultivation

## Slide 6: Development of Experimental SetUP For Biofilm formation
HPLC:
Succinate and Sucrose Concentration (Carbon Sources)
Rinse after Cultivation
Carbazole Assay: Alginate Quantification
Dried Biomass: Biomass Concentration
Image Analysis:
Growth Curve
Medium
Peristaltic pump
Collection Tube
PDMS Device
Camera
loisa.borde@ovgu.de
10 g/l Sucrose
10 g/l Succinate
Salt solution
Phosphate buffer

## Slide 7: Image Analysis To Observe Biofilm Growth
loisa.borde@ovgu.de
Light intensity change in relation to the zero value
Substraction of zero value
Capture image every hour under constant lighting conditions
Calculate mean grey values of seven sectors for each image

## Slide 8: Biofilm Growth Observed in Microfluidic Devices
1 h
48 h
96 h
144 h
192 h
Continuous growth for 160 h, followed by slower growth
Stationary phase reached after 200 h
Chart: Biofilm Growth
loisa.borde@ovgu.de

## Slide 9: BioFilm Growth Depending on PDMS Thickness
PDMS: oxygen permeable
thinner PDMS-layer  higher oxygen availability  faster biofilm formation
 Biofilm growth depends on oxygen availability
Chart: Biofilm Growth
loisa.borde@ovgu.de

## Slide 10: Experimental procedure to measure the biomass concentration
Biomass concentration (up to 17 g/l)
loisa.borde@ovgu.de
Rinse after cultivation
Biofilm Growth
250 h
10.000 x g
10 min
wash pellet
80 °C
24 h
Weigh dried biomass
Workflow for biomass measurement
Rinse out biofilm at different time points  Calibration curve for biomass concentration depending on light intensity change

## Slide 11: Outlook
Improvement of currently used methods (measurement of substrates and alginate, calibration curve for calculation of biomass concentration)
Model parametrization and validation based on experimentally derived kinetic parameters
Expansion of kinetic parameter measurement (oxygen content, pH-values, attachment and detachment of biofilms)
Deeper understanding of biofilm formation depending on pore geometry and enhanced biopolymer production in biofilms growing in porous substrates
loisa.borde@ovgu.de

## Slide 12: Thank you for your attention!
M. Sc. Loisa Borde
Institute of Process Engineering
Otto-von-Guericke University Magdeburg
Universitätsplatz 2
39106 Magdeburg
loisa.borde@ovgu.de
+49 (0) 391 67 50246
Many thanks to:
Dr. Nicole Vorhauer-Huget
Prof. Dr. Stefanie Duvigneau
Maike Werdin
Transport in porous media research group
Acknowledgement: The authors gratefully acknowledge the funding by the European Regional Development Fund (ERDF) within the programme Research and Innovation - Grant Number ZS/2023/12/182075.

## Slide 13: References
Iain D. Hay, Zahid Ur Rehman, M. Fata Moradali, Yajie Wang, and Bernd H. A. Rehm. Microbial alginate production, modification and its applications. Microbial Biotechnology, 6(6):637–650, 2013. DOI: 10.1111/1751-7915.12076;
George E. Kapellos, Terpsichori S. Alexiou, and Stavros Pavlou. Chapter 8 - fluid-biofilm interactions in porous media. In Sid M. Becker and Andrey V. Kuznetsov, editors, Heat Transfer and Fluid Flow in Biological Processes, pages 207–238. Academic Press, Boston, 2015. ISBN 978-0-12-408077-5. DOI: 10.1016/B978-0-12-408077-5.00008-0;
Aamer, E., Faber, F., Bhaskaran, S. et al. Pore Network Model for Study of Biofilm Growth Limitations in Porous Substrata. Transp Porous Med 153, 12 (2026). DOI: 10.1007/s11242-025-02261-6