## Slide 1: Model based assessment of pore-size dependent biofilm growth kinetics with application to productive biofilm-reactors
Maike Werdin1, Loisa Borde1,2, Nicole Vorhauer-Huget1
1 Chair of Thermal Process Engineering, Otto von Guericke University, Magdeburg, Germany
2 Process Synthesis and Process Dynamics, Max Planck Institute for Dynamics of Complex Technical Systems, Magdeburg, Germany
InterPore 2026
18th annual meeting & conference courses
19th – 22nd May 2026, Nantes, France
tvt.ovgu.de/tpm

## Slide 2: Motivation and GOALS Biofilms in porous structures
Sustainable production based on microorganisms
Natural growth formation: biofilms
Enhancement: porous structures in bioreactor
Investigation of influence of pore geometry on biofilm growth
Extra polymeric substances (EPS)
Microorganisms
Surface

## Slide 3: Reconstruction of porous structures
Pore Network Model for Study of Biofilm Growth Limitations in Porous Substrata, Aamer et al, 2025, Transport in porous Media
Deepen understanding on single pore scale
Visualization of scanned X-ray tomography
Reconstructed Pore Network
Total Biomass Concentration
Biomass

## Slide 4: Model – Calculation Sequence in each time step
Substrate Concentration
Biomass Concentration
Single pore in detail:
Current concentration of metabolites and microorganisms
Microorganisms consume substrates to produce biomass

## Slide 5: Model – Calculation Sequence in each time step
Substrate Concentration
Biomass Concentration
Biomass Growth
Established mathematical approach of biomass growth ():
  Experimental parametrization of and
Biomass Concentration
Concentration Substrate
Specific Growth Rate
Half Saturation Constant

## Slide 6: Model – Calculation Sequence in each time step
Substrate Concentration
Biomass Concentration
Biomass Growth
Substrate Consumption
Consumption of substrates for growth
  Experimental parametrization of substrate to biomass yield ()

## Slide 7: Model – Calculation Sequence in each time step
Substrate Concentration
Biomass Concentration
Biomass Growth
Substrate Consumption
Limited Volume
Limited volume in pore
  Bioreactor:
  Pore:
  Biomass growth: reduction of  increase
Change of fraction biomass:
Biomass ()
Fluid (Medium, )

## Slide 8: Model – Calculation Sequence in each time step
Substrate Concentration
Biomass Concentration
Biomass Growth
Substrate Consumption
Volume Effect
Mass Transport
Mass transport in pore through cylindrical throats
  Diffusion:
  Or
  Flow:
Diffusion
Flow
Diffusion Coefficient Substrate
Volume Pore
Cross Section Throat
Length Throat
Flow Rate

## Slide 9: Model – Calculation Sequence in each time step
Substrate Concentration
Biomass Concentration
Biomass Growth
Substrate Consumption
Volume Effect
Mass Transfer
Substrate Concentration Change
Total substrate concentration change in pore
Substrate = Consumption + Volume Change + Mass Transfer

## Slide 10: Model – Calculation Sequence in each time step
Substrate Concentration
Biomass Concentration
Biomass Growth
Substrate Consumption
Volume Effect
Mass Transfer
Substrate Concentration Change
Update substrate and biomass concentration

## Slide 11: Results - Influence of process conditions
Batch:
Pore:
Diffusion:
Flow:
Higher substrate concentrations under mass transport conditions
Increased biomass growth
Batch; Pore
Diffusion
Flow
Batch;
Pore
Diffusion
Flow
Batch-Model: Weiler et al.. „Strain and Model Development for Auto- and Heterotrophic 2,3-Butanediol Production Using Cupriavidus Necator H16“. Biotechnology for Biofuels and Bioproducts 17, Nr. 1 (2024): 108. https://doi.org/10.1186/s13068-024-02549-7.
Initial conditions:

## Slide 12: Conclusion & Outlook
Growth highly dependent on substrate supply:
  Influenced by pore and throat geometry
  Increased substrate supply  increased biomass growth
Outlook:
Biofilm:
  Determination of kinetic parameters by experimental biofilm data
  Characterization
    Recommendation: MS04, part 3: 88. Design of a microfluidic setup to assess scale-dependent metabolic kinetics in Azotobacter vinelandii biofilms producing polysaccharides - Loisa Borde
Identify process conditions in reconstructed porous structures
Interactions of biofilm and porous structures: clogging of pores
 Application of characterized biofilm growth on reconstructed Pore Network Models

## Slide 13
Thank you for your attention!
Acknowledgement: The authors gratefully acknowledge the funding from the Deutsche Forschungsgemeinschaft (DFG priority program SPP2494, project no. 559381551 (Assessing terpene productivity of Methanosarcina acetivorans biofilms in porous substrata using a mathematical physiological approach)
Thanks to
Dr. Nicole Vorhauer-Huget
Loisa Borde
Research Group Transport in Porous Media
Transport in porous media research group

## Slide 14: Initial and boundary conditions
Variable | Symbol | Value
Initial biomass (dry weight) |  | 2e-5 g (0.02 mg)
Initial substrate Concentration |  | 20 g/L
Maximum biomass concentration |  | 20 g/L
Volume Pore |  | 2e-4 L (200 )
Cross Section Throat |  | 1.5e-4 (1.5 )
Length Throat |  | 13.5e-3 m (1,35 cm)
Diffusion Coefficient substrate (fructose) |  | 0.744e-9
Variable | Symbol | Value
Initial biomass (dry weight) |  | 2e-5 g (0.02 mg)
Initial substrate Concentration |  | 20 g/L
Maximum biomass concentration |  | 20 g/L
Volume Pore |  | 
Cross Section Throat |  | 
Length Throat |  | 13.5e-3 m (1,35 cm)
Diffusion Coefficient substrate (fructose) |  | 

## Slide 15: Kinetic parameters
Batch-Model: Weiler et al.. „Strain and Model Development for Auto- and Heterotrophic 2,3-Butanediol Production Using Cupriavidus Necator H16“. Biotechnology for Biofuels and Bioproducts 17, Nr. 1 (2024): 108. https://doi.org/10.1186/s13068-024-02549-7.

## Slide 16: Influence initial biomass concentration
Same mass in different volumes  different concentrations
 Initial biomass concentration determines kinetics

## Slide 17: Influence initial biomass concentration
= 2e-5 g
Small: = 2e-5 L  c = 1 g/L
medium: = 2e-4 L  c = 0.1 g/L
big: = 2e-3 L  c = 0.01 g/L

## Slide 18: Diffusion
 | Diffusion | Rp [mm] | Vp [m3] | Rt [mm] | At [m2] | Lt [mm]
A | Low | 4 | 2e-7 | 1.7 | 9.1e-6 | 54
B | Medium | 4 | 2e-7 | 3.4 | 3.6e-5 | 27
C | high | 4 | 2e-7 | 6.8 | 1.5e-4 | 13.5

## Slide 19: Flow rates
Low flow = 4ul/min
Medium Flow = 40 ul/min
High = 400 ul/min