## Slide 1
研究学术 造就人才 佑启乡邦 振导社会
Pore-Network-Continuum Model for Two-Phase Flow in Porous Media
Chao-Zhong Qin, Bowen Shi, Jianqi Rong, Bo Guo, Majid Hassanizadeh
School of Resources and Safety Engineering, Chongqing University, China
http://czqin.github.io
InterPore 2026, 19-22 May, Nantes, France
MS05: Physics of multiphase flow in diverse porous media

## Slide 2
Outline
Multiscale pore structures (shales, tight sandstones, carbonate rocks, etc.)
The pore-network-continuum modeling (motivation, mesh coarsening)
Single-phase flows (permeability prediction, solute transport)
Quasi-static two-phase flows (capillary pressure, relative permeability, resistance index)
Summary and outlook
Notes: Energy transition

## Slide 3
Examples of multiscale/across-scale pore structures
Gas diffusion layers + Micro porous layer
MPL
GDL
Organic matters and clays in shale MAPS
PU8
Sandstones
Zoom in
To sum up:
Multiscale pore structures are ubiquitous
Associated with different minerals or materials, which may have complex wettability
Necessitate the hybrid models for flow and transport
Notes: Balance FoV and resolution

## Slide 4
Digital Rock Physics: the image-based modeling
Nubian sandstone
Microporosity
Estaillades
100×100×200 image, DNS of spontaneous imbibition
900×900×2000 image
DPNM of spontaneous imbibition
(Qin et al., AWR, 2021, 2025)
100 µm
(Zhang, Guo, Qin, and Xiong, AWR, 2024)
subresolution
Macropore
Multiscale PNM
Pore-Network-Continuum model
Micro-Continuum model
(Zhao et al., TiPM, 2025)
Notes: 引入3类模型：各有优缺点。

## Slide 5
Outline
Multiscale pore structures (shales, tight sandstones, carbonate rocks, etc.)
The pore-network-continuum modeling (motivation, mesh coarsening)
Single-phase flows (permeability prediction, solute transport)
Quasi-static two-phase flows (capillary pressure, relative permeability, resistance index)
Summary and outlook
Notes: Energy transition

## Slide 6
The pore-network-continuum model: framework
Transition-layer module
macropores
microporosity
solid
40×40 pixels
Interfacial voxels
outward-coarsening module
interface-coarsening module
8×8 voxels
Computational mesh
Volume or volumeless pore throats?
Pressure depletion
Shi et al., Modeling of flow and transport in multiscale digital rocks aided by grid coarsening of microporous domains, Journal of Hydrology 633 (2024) 131003.
CG1
CG2
CG3
Notes: Regarding the interface treatment, one can refer to our paper.

## Slide 7
The pore-network-continuum model: coarsening effect
Shi et al., Modeling of flow and transport in multiscale digital rocks aided by grid coarsening of microporous domains, Journal of Hydrology 633 (2024) 131003.
2003 Berea sandstone
Microporosity filling
macropores: 539，microporosity: 273176
macropores: 539，microporosity: 1922662
Gas production curves
Breakthrough curves

## Slide 8
Outline
Multiscale pore structures (shales, tight sandstones, carbonate rocks, etc.)
The pore-network-continuum modeling (motivation, mesh coarsening)
Single-phase flows (permeability prediction, solute transport)
Quasi-static two-phase flows (capillary pressure, relative permeability, resistance index)
Summary and outlook
Notes: Energy transition

## Slide 9
3D reconstruction
~3 mm
~3 mm
PNCM modeling
Case 1: Absolute permeability of GDL
Fibers
MPL
PTFE
CT image of the composite material
SEM of MPL
Void space
Notes: The challenges lie in the segmentation, and characterization of MPL

## Slide 10
1.53×10-16 m2
3.88×10-13 m2
1.5×10-11 m2
Case 1: Absolute permeability of GDL
Test of three samples:
Fibers penetrate into the MPL
Cracks in the MPL form preferential flows
Experimental validation is ongoing: design of proper apparatuses
Notes: Breakthrough pressure, in-plan and through-plan permeability, and relative permeability

## Slide 11
Case 2：Estaillades carbonate rock
Porosity map
Entry pressure map
CT grey-scale map
Solid
Microporosity
6.5 µm, 1316×1316×1087 voxels
(Wang et al., WRR, 2022)
4003 test core：
Computational mesh
Porosity map
Pore-size map
Absolute permeability: 160 mD (Exp. 95~283 mD)
The Digital Rock Portal
Notes: Challenge: how to characterize material properties of subresolution microporosity? I will introduce some in the section of two-phase modeling.

## Slide 12
Outline
Multiscale pore structures (shales, tight sandstones, carbonate rocks, etc.)
The pore-network-continuum modeling (motivation, mesh coarsening)
Single-phase flows (permeability prediction, solute transport)
Quasi-static two-phase flows (capillary pressure, relative permeability, resistance index)
Summary and outlook
Notes: Energy transition

## Slide 13
Quasi-static modeling: verification against the full PNM
RT1
RT2
X
Z
Microporosity
Mesh
CT image
Binary
Rock typing
Shi et al., The pore-network-continuum modeling of two-phase flow properties for multiscale digital rocks, AWR, 206, 105138, 2025
Match well
Capillary pressure and relative permeability
Notes: Invasion-percolation algorithm.
RT1: the pc and kr are obtained by PNM, and given back to the PNCM.

## Slide 14
Quasi-static modeling: tight sandstones
solid
illite
chlorite
void
Sparsely distributed resolved void spaces
Lowly permeable chlorite
Highly permeable illite, and some kaolinite
① Sub-rock typing: resolved pores, lowly permeable minerals, and highly permeable ones
2800×2800 voxels of 0.67 µm
Notes: Invasion-percolation algorithm.
RT1: the pc and kr are obtained by PNM, and given back to the PNCM.

## Slide 15
Quasi-static modeling: tight sandstones
solid
illite
chlorite
void
Sparsely distributed resolved void spaces
Lowly permeable chlorite
Highly permeable illite, and some kaolinite
① Sub-rock typing: resolved pores, lowly permeable minerals, and highly permeable ones
2800×2800 voxels of 0.67 µm
Multiple imaging
Notes: Invasion-percolation algorithm.
RT1: the pc and kr are obtained by PNM, and given back to the PNCM.

## Slide 16
Quasi-static modeling: tight sandstones
The digital rock
Highly permeable minerals
Macropores
Lowly permeable minerals
Complete characterization
Flow parameters of each type of microporosity
Heterogeneity of each type of microporosity
0
0.5
Porosity
1
② Flow parameters of microporosities or each type of minerals
Notes: Invasion-percolation algorithm.
RT1: the pc and kr are obtained by PNM, and given back to the PNCM.

## Slide 17
Quasi-static modeling: tight sandstones
T1：600×600×520
T2：550×550×510
T3：600×600×500
Three samples and their sizes
Samples | T1 | T2 | T3
Macropores | 181548 | 48703 | 17422
Grids of highly permeable minerals | 11863451 | 7436487 | 5106151
Grids of highly permeable minerals | 3410228 | 4886052 | 5007589
Total porosity % | 10.73 | 8.43 | 5.54
Mesh information
The prediction of Pc-s curves
Notes: Invasion-percolation algorithm.
RT1: the pc and kr are obtained by PNM, and given back to the PNCM.

## Slide 18
Summary and outlook
Multiscale/across-scale pore structures are ubiquitous in unconventional formations and industrial porous materials
We present the pore-network-continuum hybrid modeling, which can balance efficiency and accuracy
Sub-rock typing is crucial to the characterization of multiscale pore structures and the associated digital rock modeling
Develop dynamic PNCM
Extend empirical equations for two-phase flow parameters
Develop AI-based construction of multiscale digital rocks
Applications in industrial porous materials
Notes: 核心是建立数字岩心，在此基础上，可以分析连通性与多物理场模拟！

## Slide 19
《Earth Energy Science》: Open Access and Free
Earth Energy Science
Emerging journal that serves the national "dual-carbon" strategy and
pays special attention to the frontier research of earth energy
Editor-in-Chief
Associate Editors
Ranjith P. G.
Derek Elsworth
Baisheng Nie
Zhaolong Ge
Michael Hood
Ting Ren
Majid Hassanizadeh
Jeffrey Gu
Yujing Jiang
Yiyu Lu
Journal Focus: Green mining technology and mineral processing, energy and resource engineering geomechanics, underground energy storage, oil and gas exploration and development, geothermal energy development and utilization, CCUS and other related fields.
Journal features:
Global OA publishing, free of APC
Key journal promoted by KeAi press
ScienceDirect (Elsevier) spread platform
Editorial Manager submission system
Journal progress (2023.12-2026.3)
It has been included in Scopus, DOAJ, CAS, INSPEC and OARL databases, and EI collections are under review.
The editorial board and young editorial team composed of renowned scholars from both domestic and international backgrounds have been established.
5 issues (33 articles) have been published, 5 manuscripts have been accepted, and the journal is published quarterly.
The first International Conference on earth energy science was successfully held in 2023, and the second conference was successfully held in November 2025.
It was selected as the high starting point new journal of the excellent action plan of Chinese Sci tech journals in 2024.
Notes: 核心是建立数字岩心，在此基础上，可以分析连通性与多物理场模拟！

## Slide 20
Thank you for your attention!
Notes: 我的汇报完毕，衷心感谢各位评审专家！