## Slide 1: Effects of permeability and flow orientation on CO₂ capillary trapping in saline aquifers
Rayana Peres, Yan S. de Medeiros, Felicle Lopez, Ranena Ponce, Daniela Hartmann, and Marcio Carvalho
Laboratory of Microhydrodynamics and Flow in Porous Media (LMMP)
Department of Mechanical Engineering, PUC-Rio, Rio de Janeiro, Brazil

## Slide 2: Mitigating carbon emissions through geological storage
https://watchwire.ai/carbon-capture-utilization-storage-pipe-dream-potential-solution/
CCS/ CCUS Promising strategy to mitigate anthropogenic greenhouse gas emissions through CO2 injection into deep geological formations.
Flow dynamics and CO₂ trapping in saline aquifers
Storage capacity in saline aquifers is controlled by CO₂–brine distribution and displacement dynamics
Long-term storage performance depends on trapping mechanisms such as capillary and solubility trapping
Improved understanding of subsurface flow is crucial for reliable injection design and minimizing leakage risks
Saline aquifers are attractive due to their large storage potential and availability

## Slide 3: Key controls on CO2 trapping efficiency
Reservoir heterogeneity and permeability contrasts influence CO2 plume migration, sweep efficiency, and trapping behavior
Flow direction may alter migration pathways, buoyancy effects, and residual trapping mechanisms
Capillary trapping efficiency depends on how CO2 distributes within porous media during drainage and imbibition
Core-scale experiments help evaluate these mechanisms under controlled subsurface conditions.
Hefny et al., International Journal of Greenhouse Gas Control 103 (2020) 103164

## Slide 4: Goals
Evaluate CO₂ storage capacity through capillary trapping in carbonate rocks representative of saline aquifers
Investigate how permeability and flow orientation influence CO₂ trapping efficiency

## Slide 5: Fluids, operational conditions, and rock properties
Saturation with brine (NaCl 186 g/L)
Determination of absolute permeability (Kbrine)
CO2 flooding
(v = 1 ft/ day)
Brine flooding
(v = 1 ft/ day)
Experimental
steps:
Test | Plug | Length (cm) | Plug properties (brine) |  |  | Plug orientation | Temperature (°C) | Pore pressure (PSIG)
 |  |  | K (mD) | φ (%) | PV (cm3) |  |  | 
1 | IL5C-4-16 | 10.02 | 3.93 | 16.40 | 18.92 | Horizontal | 40 | 4,000
2 | IL7C-32-18 | 9.94 | 28.21 | 17.22 | 19.71 | Horizontal |  | 
3 | IL7A-32-18 | 9.80 | 25.36 | 17.48 | 19.72 | Vertical |  | 
Indiana limestone

## Slide 6: Experimental set-up
Inlet
Outlet
Inlet
Outlet

## Slide 7: Results

## Slide 8: Impact of permeability on CO2 displacement and trapping
IL5C-4-16
IL7C-32-18
Gas breakthrough at 0.51 PV
Gas breakthrough at 0.35 PV
Earlier gas breakthrough
Low-permeability
Medium-permeability
Low-permeability
Medium-permeability

## Slide 9: Impact of permeability on CO2 displacement and trapping
The low-permeability plug exhibited a more gradual decline in gas saturation
Storage efficiency was higher in the medium-permeability plug

## Slide 10: Impact of flow orientation on CO2 trapping
Horizontal injection
IL7C-32-18
IL7A-32-18
H = vertical height over which gravity acts
L = characteristic flow length (distance fluid travels)
Vertical injection
Orientation effects were limited under the tested conditions

## Slide 11: Conclusions
This study highlights the complex interplay of rock properties and flow dynamics in determining the capillary storage efficiency of CO2 in saline aquifers.
Despite lower gas saturation during drainage, the medium-permeability plug achieved higher residual trapping efficiency after imbibition, likely due to improved water reconnection and gas disconnection.
Flow orientation had limited influence under similar gravity conditions, with comparable sweep efficiency and residual trapping.

## Slide 12
rmartins@lmmp.mec.puc-rio.br
msc@puc-rio.br
R. Peres