## Slide 1: Pore-scale modeling of multiphase flow and phase change in porous media by lattice Boltzmann method
, , , , ,
1 Institute of Extreme Mechanics, Northwestern Polytechnical University, Xi’an, 710072, Shannxi, China.
2 Chair of Building Physics, Department of Mechanical and Process Engineering, ETH Zurich (Swiss Federal Institute of Technology in Zurich), Zurich 8092, Switzerland
3 Key Laboratory of Thermo-fluid Science and Engineering, Ministry of Education, School of Energy and Power Engineering, Xi’an Jiaotong University, Xi’an, Shaanxi 710049, China
4 College of Petroleum Engineering, China University of Petroleum in Beijing, PR China
5 Earth and Environment Sciences Division (EES-16), Los Alamos National Laboratory (LANL), Los Alamos, NM 87545, USA
6 Center for Life Nano Science at La Sapienza, Fondazione Istituto Italiano di Tecnologia, Viale Regina Margherita 295, 00161, Roma, Italy
7 Physics Department and Institute for Applied Computational Science, John A. Paulson School of Applied Science and Engineering, Harvard University, Oxford Street 29, Cambridge, MA 02138, USA.
8 Dep. of Civil and Building Engineering, Universite de Sherbrooke, Sherbrooke Qc J1K 2R1, Canada

## Slide 2: Contents
01
Background
02
Numerical model
03
Results and discussions
04
Conclusion and outlook

## Slide 3: Multiphase flows and phase change in porous media
Enhanced cooling of 3D chip stacks (evaporation)
Thermal protection of high-speed aircrafts
(boiling + evaporation)
Combustion in aircraft engines (boiling + evaporation)
Water flooding in Proton Exchange Membrane Fuel Cell (condensation)

## Slide 4: Contents
01
Background
02
Numerical model
03
Results and discussions
04
Conclusion and outlook

## Slide 5: Numerical model and validation
1. Single-component multi-phase model
Kinematic part
Shear part
Higher order part
Minimum entropy.
Kinematic viscosity
D2Q9
collision
propagation
Karlin et al, (2014). Physical review E, 90 (3).
Iso-entropy lines
To realize a large range of kinematic viscosity!

## Slide 6: Numerical model and validation
1. Single-component multi-phase model
External force for two-phase modeling
Our approach to consider the external force:
3. Considering the influence of the error term brought by the EDM force scheme.
2. Introducing Wang’s method of two-phase force to EDM scheme to adjust the surface tension;
EDM force scheme to make it compatible with the KBC collision operator;
Qin et al. Journal of Fluid Mechanics, (2026) 1028:A20.

## Slide 7: Numerical model and validation
1. Single-component multi-phase model
Theoretical equation:
Tunable range of over 200 times.
Different density ratios agree well with Maxwell equal area rule
Different liquid-vapor density ratios with tunable surface tension
Qin et al. Journal of Fluid Mechanics, (2026) 1028:A20.

## Slide 8: Numerical model and validation
1. Single-component multi-phase model
Droplet impact, penetration and splashing on hydrophobic mesh structures
Qin et al. Journal of Fluid Mechanics, (2026) 1028:A20.

## Slide 9: Numerical model and validation
0.896
0.896ms
1.12
2r/d=0.12
2r/d=0.25
2r/d=0.38
(a)
(b)
(c)
Qin et al. Journal of Fluid Mechanics, (2026) 1028:A20.
1. Single-component multi-phase model
The influence of pore size on liquid penetration, spreading and splashing at Re=15200,We=1020

## Slide 10: Numerical model and validation
1.12
2r/d=0.52
1.34
2r/d=0.63
1.34
2r/d=0.75
(d)
(e)
(f)
Qin et al. Journal of Fluid Mechanics, (2026) 1028:A20.
1. Single-component multi-phase model
The influence of pore size on liquid penetration, spreading and splashing at Re=15200,We=1020

## Slide 11: Numerical model and validation
2. Temperature model for non-isothermal phase change
Two-way coupling by equation of state (EoS)
convection
EMRT LBM
EoS
Temperature equation
Finite difference method
(2nd/4th order Runge-Kutta scheme)
diffusion
latent heat
Li et al. (2015), INT J HEAT MASS TRANSF, 85, 787-796

## Slide 12: Numerical model and validation
2. Temperature model for non-isothermal phase change
1) Single droplet evaporation
Fei, Qin, et al. Physical Review E 105.2 (2022): 025101.
Heating at four sides
Constant pressure

## Slide 13: Numerical model and validation
2. Temperature model for non-isothermal phase change
2) Single bubble nucleation and departure
θ=30,
θ=90,
θ=135,
1. Friz, (1935). Physic. Zeitschz, 36, 379-354.
Bubble :
Bubble departure diameter agrees with the theoretical relation.

## Slide 14: Numerical model and validation
2. Temperature model for non-isothermal phase change
3) Vapor condensation on a cold vertical flat plate
Pr=12
Ja=2.3
Cold
Wall
,
x
y
Nusselt, Zetrschr. Ver. Deutch. Ing. 60 (1916) 541–546.
Both the film thickness and temperature profile agree well with Nusselt’s theory.

## Slide 15: Numerical model and validation
3. Particle transport and deposition model for evaporation of colloid suspension
Qin et al., 2019. Physical Review E, 99(5), p.053306.
T-EMRT LBM
Particle transport
Fluid-particle interaction
Flow velocity
Wall boundary--
1. Local concentration/drying completion
Particle deposition
2. Adjacent node is wall or particle deposition
3. No particle penetration at wall
One-way or two-way coupling
Qin et al., 2023. Journal of Fluid Mechanics, 963, A26.

## Slide 16: Numerical model and validation
3. Particle transport and deposition model for evaporation of colloid suspension
Deposition pattern under different particle volume fraction
240 lattices
240
48
Top cover
Bottom substrate
Simulation
d=40
Experiment
Su et al., 2018
Liquid contact angle: 30
Polystyrene nanoparticle (PSNP) suspension
Qin et al., 2020. INT J HEAT MASS TRANSF, 158, 120000.

## Slide 17: Contents
01
Background
02
Numerical model
03
Results and discussions
04
Conclusion and outlook

## Slide 18: Results and discussions: evaporation
1. Non-isothermal liquid drying in micropore structures
50
Side view
Liquid contact angle: 30(plasma treatment of geometry)
Rectangular-spiral shape
D
180μm
80
20x20
L
Gradient shape
20x20
230μm
180
123
105
91
80
71
200
165
135
115
100
85
75
147
L0
D
L0
L=7L0
Pillar height of 60

## Slide 19: Results and discussions: evaporation
1. Non-isothermal liquid drying in micropore structures
Evaporation Exp.
LBM modeling of
liquid configuration
LBM modeling of temperature
Liquid internal flow
Liquid pressure
实验 模拟
Laplace pressure:
Surface tension
Qin et al., 2019. Journal of Fluid Mechanics, 866, pp.33-60.

## Slide 20: Results and discussions: evaporation
2. Evaporation-induced particle transport and deposition
Contact angle of , initial nanoparticle concentration 5.0%, particle contact angle 4, diffusion coefficient 0.03
Qin et al., 2023. Journal of Fluid Mechanics, 963, A26.

## Slide 21: Results and discussions: evaporation
2. Evaporation-induced particle transport and deposition
Evolution of liquid mass and normalized particle deposition volume / under different conditions
An empirical relation between the evaporation rate and the influential factors is established.
Qin et al., 2023. Journal of Fluid Mechanics, 963, A26.

## Slide 22: Results and discussions: boiling
Ja=0.1660（Tw=0.90Tc）
a
1. Boiling in simple porous media (PM) compared with pool boiling (at θ=90°)
Qin et al., 2026, under review
Ja= 0.1992（Tw=0.92Tc）
Nucleate boiling
d
Contact line is pinned
Contact line keeps moving

## Slide 23: Results and discussions: boiling
Ja=0.2656（Tw=0.96Tc）
e
Ja= 0.2324（Tw=0.94Tc）
b
1. Boiling in simple porous media (PM) compared with pool boiling (at θ=90°)
Qin et al., 2026, under review
Transition boiling
Notes: The behaviors are similar, but the bubble nucleation and coalescence are very intensive.

## Slide 24: Results and discussions: boiling
Ja=0.3321（Tw=1.0Tc）
f
Ja= 0.8301 （Tw=1.3Tc）
c
1. Boiling in simple porous media (PM) compared with pool boiling (at θ=90°)
Qin et al., 2026, under review
Film boiling
Film is higher than bottom solid
Film is relatively lower

## Slide 25: Results and discussions: boiling
2. Comparison of heat transfer performance——boiling curves
Qin et al., 2026, under review
Ja=0.2324 (point b)
Ja=0.4981 (point g)
Ja=0.6641 (point h)
The starting Ja of nucleate boiling is smaller in PM (point a compared with d)
The effective heat transfer range is 5 times higher in PM (0.6641 compared with 0.1329)
The maximum heat flux is increased by 32% in PM (8.88e-6 than 6.74e-6)
h

## Slide 26: Results and discussions: boiling
2. Comparison of heat transfer performance——boiling curves
Qin et al., 2026, under review
The qualitative trend is the same for different contact angles of and
The highest difference of effective boiling range is at (6.4 times by 0.5313/0.083)
The highest difference of maximum heat flux is at (8.88e-6 than 6.74e-6)

## Slide 27: Results and discussions: condensation
1. Vapor condensation in a 2D cross-section of 3D fiber structures (analogous to PEMFC)
Zhang, Qin*, et al., 2026, under review
Contact angle: ; porosity:
Kinematic viscosity：
Thermal diffusion coefficient：
periodic
periodic

## Slide 28: Results and discussions: condensation
1. Vapor condensation in a 2D cross-section of 3D fiber structures (analogous to PEMFC)
Zhang, Qin*, et al., 2026, under review
Density
Temperature
Liquid mass increase rate:
Initial period
Stable period
The condensation is divided to an initial fluctuation period, followed by a stable period

## Slide 29: Results and discussions: condensation
1. Vapor condensation in a 2D cross-section of 3D fiber structures (analogous to PEMFC)
Zhang, Qin*, et al., 2026, under review
Vapor income rate
Condensation rate
Vapor accumulation at interface-> lower vapor pressure gradient-> less vapor income
Vapor income rate
Condensation rate
Vapor reduction at interface-> higher vapor pressure gradient-> more vapor income
The initial fluctuation period is induced by the competition between vapor income and condensation

## Slide 30: Results and discussions: condensation
1. Vapor condensation in a 2D cross-section of 3D fiber structures (analogous to PEMFC)
Zhang, Qin*, et al., 2026, under review
In the time period of - -, both the temperature and velocity profiles show condensation is approaching a stable state
The stable period is due to the balance of condensation and liquid transport at left liquid-vapor interface (yellow)

## Slide 31: Results and discussions: condensation
2. The influence of different parameters on the condensation mechanisms—contact angle
Zhang, Qin*, et al., 2026, under review
Small contact angle is favorable for vapor condensation due to high capillary pressure
High contact angle may lead to isolated vapor which prevents the condensation
Liquid mass evolution with time
A
Isolated vapor

## Slide 32: Results and discussions: condensation
2. The influence of different parameters on the condensation mechanisms—porosity
High porosity promotes condensation due to less viscous dissipation, while heterogeneous pore structures may lead to variation of condensation rate in a certain period of time
From to , the condensation is faster
at than at
Liquid mass evolution with time

## Slide 33: Results and discussions: condensation
2. The influence of different parameters on the condensation mechanisms—Ja number
At high Ja (low T of porous medium), the temperature/pressure gradient is high, leading to high vapor income rate, and thus more intensive condensation
High Ja leads to strong vapor accumulation at left liquid-vapor interface, even inducing evaporation
Liquid mass evolution with time

## Slide 34: Contents
01
Background
02
Numerical model
03
Results and discussions
04
Conclusion and outlook

## Slide 35: Conclusions and outlook
Conclusions
Isothermal two-phase flow
Evaporation
Boiling
Condensation
Outlook
The influence of interfacial flow on evaporation-induced particle transport and deposition
The consideration of air in evaporation and boiling
Microfluid experiment for engineering applications

## Slide 36
Thank you for your attention