## Slide 1
Flow-induced surface charge heterogeneity
and its impact on cation exchange
A coupled PNP Stokes - surface-exchange COMSOL study
Shahar Shahror, Yael Mishael, Nimrod Schwartz
Hebrew University of Jerusalem · Soil & Water Sciences
May 2026

## Slide 2
Motivation
Same chemistry, same surface -different reported rates.
Flow-induced surface charge heterogeneity & cation exchange kinetics · S. Shahror, Y. Mishael, N. Schwartz · HUJI
2 / 13
Ion-exchange kinetics are central to many natural and technological systems
• Soils · K⁺ / NH₄⁺ release, heavy-metal mobilization under leaching
• Membranes · selectivity, breakthrough, kinetically limited
• Electrochemical interfaces under flow · batteries, fuel cells, biosensors
The puzzle
“….Desorption varied with flow rate and since by definition the desorption rate coefficient is constant a new term, apparent desorption rate coefficient was defined for each flow rate in the system…”
Sparks et al., Soil Sci. Soc. Am. J. 44: 1205-1208 (1980)
These systems are commonly described using fitted rate coefficients

## Slide 3
Ion Exchange at the Solid Liquid Interface
A conceptual view of cation exchange between the flowing solution and reactive surface sites.
Flow-induced surface charge heterogeneity & cation exchange kinetics · S. Shahror, Y. Mishael, N. Schwartz · HUJI
3 / 13
Existing approaches typically emphasize different parts:
solution transport
surface chemistry
electrokinetic transport
Negatively charged patch
Advection
Diffusion
Electromigration
Surface reaction

## Slide 4
Ion Exchange at the Solid Liquid Interface
A conceptual view of cation exchange between the flowing solution and reactive surface sites.
Flow-induced surface charge heterogeneity & cation exchange kinetics · S. Shahror, Y. Mishael, N. Schwartz · HUJI
3 / 13
Existing approaches typically emphasize different parts:
solution transport
surface chemistry
electrokinetic transport
these processes are rarely coupled in one framework
Advection
Diffusion
Electromigration
Surface reaction
Negatively charged patch

## Slide 5
Our model · general Overview
2-D microchannel · Poisson-Nernst-Planck.
Flow-induced surface charge heterogeneity & cation exchange kinetics · S. Shahror, Y. Mishael, N. Schwartz · HUJI
4 / 13
Negatively charged patch
Negatively charged patch

## Slide 6
Our model · the bulk
2-D microchannel · Poisson-Nernst-Planck.
Flow-induced surface charge heterogeneity & cation exchange kinetics · S. Shahror, Y. Mishael, N. Schwartz · HUJI
5 / 13
Nernst-Planck
flux: diffusion + electromigration + advection
→ ions move by diffusion, drift in the field, and with the flow.
Poisson - charges set the potential
→ Pressure-driven flow, solving Hagen-Poiseuille.
Negatively charged patch
Notes: Relation between potential and the space charged density

## Slide 7
Our model · the surface
Maxwell-Stefan style cross-flux · Dₛ in the tangential transport.
Flow-induced surface charge heterogeneity & cation exchange kinetics · S. Shahror, Y. Mishael, N. Schwartz · HUJI
6 / 13
evolution of surface species (K⁺, Ca²⁺ )
→ the number of K⁺ (or Ca²⁺) sites changes due to reaction.
K⁺ exchange
Ca²⁺ exchange
→ Ca²⁺ binds two sites, giving the squared site dependence.
vertical flux: reaction kinetics
⁺
²⁺
-
-
-

## Slide 8
Our model · the surface
Maxwell-Stefan style cross-flux · Dₛ in the tangential transport.
Flow-induced surface charge heterogeneity & cation exchange kinetics · S. Shahror, Y. Mishael, N. Schwartz · HUJI
6 / 13
evolution of surface species (K⁺, Ca²⁺ )
→ the number of K⁺ (or Ca²⁺) sites changes due to reaction and tangential flux and.
K⁺ exchange
Ca²⁺ exchange
→ Ca²⁺ binds two sites, giving the squared site dependence.
vertical flux: reaction kinetics
Werkhoven et al., Phys. Rev. Lett. 120, 264502 (2018)
⁺
²⁺
tangential flux: diffusion + electromigration
-
-
-

## Slide 9
Results · K+ concentration gradients and ion-flux maps
K+ concentration gradients with diffusion, electromigration, and advection flux vectors near the reactive patch.
Flow-induced surface charge heterogeneity & cation exchange kinetics · S. Shahror, Y. Mishael, N. Schwartz · HUJI
7 / 13
K⁺ ()
t = 50 min
t = 300 min
red · diffusion black · electromigration white · advection

## Slide 10
Results · Surface Kinetics
K⁺ and Ca²⁺ desorption and re-adsorption rates. The 1000-min mark is the kinetic window.
Flow-induced surface charge heterogeneity & cation exchange kinetics · S. Shahror, Y. Mishael, N. Schwartz · HUJI
8 / 13
• (a): K⁺ adsorption/desorption rate over time at the surface.
• (b): Ca²⁺ adsorption/desorption rate over time at the surface.

## Slide 11
Results · Surface heterogeneity along the reactive patch
Coefficient of variation (CV) computed along the reactive patch for ​, ​ and .
Flow-induced surface charge heterogeneity & cation exchange kinetics · S. Shahror, Y. Mishael, N. Schwartz · HUJI
9 / 13
Heterogeneity increases with flow velocity for all surface species.
and develop the strongest spatial variability along the reactive patch.

## Slide 12
Results · Surface exchange dynamics under flow
Cumulative K+ desorption and re-adsorption for different surface mobilities ()
Flow-induced surface charge heterogeneity & cation exchange kinetics · S. Shahror, Y. Mishael, N. Schwartz · HUJI
10 / 13

## Slide 13
Flow-dependent apparent desorption kinetics
Desorption rate coefficient for different flow velocities.
Flow-induced surface charge heterogeneity & cation exchange kinetics · S. Shahror, Y. Mishael, N. Schwartz · HUJI
11 / 13
Without lateral surface transport (), the apparent desorption rate is nearly flow-independent.
Enabling surface transport introduces strong flow dependence in the fitted apparent kinetics.
(a) No lateral surface transport,
(b) With lateral surface transport,

## Slide 14
Conclusions · interpreting fitted kinetic rates
Three key observations from the coupled model
Flow-induced surface charge heterogeneity & cation exchange kinetics · S. Shahror, Y. Mishael, N. Schwartz · HUJI
12 / 13
Flow-induced interfacial heterogeneity affects the measured exchange kinetics.
Flow changes the local chemical environment along the reactive patch, altering both ion distributions and surface composition.
Surface heterogeneity is generated by the coupled system, rather than imposed as a fixed surface property.
Apparent kinetic coefficients are not purely intrinsic and may include contributions from transport-coupled interfacial dynamics.

## Slide 15
Thank you
Questions, comments, ideas are welcome.
shahar.shahror@mail.huji.ac.il