## Slide 1: Coupled Flow and Mechanics Simulations using the Fracture Displacement-Pressure Basis Function Method for Highly Fractured Rock
Giulia Conti, Daniel Stalder, Patrick Jenny
Institute of Fluid Dynamics, ETH Zurich
Institute of Fluid Dynamics
InterPore 2026

## Slide 2: Goal: Hydro-Geomechanical Simulations of Highly Fractured Rock
Western Norway
Odling, N.E., 1997, Journal of Structural Geology
Geomechanical Simulations
  Deformation of rock
  Shear displacement
  Tensile opening
Flow Simulations
  Porous fractured rock
  Transport
Efficient solvers needed for highly fractured rock
  Few degrees of freedom per fracture
Fracture Displacement Basis Function Method
(FDBF)
Pressure Basis Function Method
InterPore 2026
Conti G., Matthai S., Jenny P., 2025, Int. J. Rock Mech. Min. Sci.
Conti G., Matthai S., Jenny P., 2026, submitted
Stalder D., Cao S., Meyer-Masetti D., Jenny P., 2026, in preparation
Notes: preexisting fractures
We developed a method which needs only very few degrees of freedom pre fracture, which makes it very efficient. For the mechanics we called it the ... And a colleague of mine is working on a very similar method for the pressure. In this talk I will present the method for the mechanics and then briefly talk about the pressure and the coupling.

## Slide 3: FDBF 1. Step: Find Unit Basis Function for Shear Slip
Calculate normalized basis function
  Assume elliptical displacement profile
  Solve assuming linear elasticity
basis function
Displacement and stress fields:
shear slip
Compute fracture specific BF
InterPore 2026
Notes: To find basis functions we will make the assumption that we know shape of slip profile
Transformation
Since we assume that the problem is linear, we can describe the displacement field u as a superposition of some fracture specific basisfunctions and their weigths which are the shear displacements. First step is to compute our basis functions. For that we look at the simple case of an horizontal fracture in the field and we will asssume/impose an elliptical slip profile and the displacement at infinity to be 0. We can solve for the displacecement in the field assuming linear elasticity and using the finite volume method. The resulting displacement field will be the basis function u hat

## Slide 4: FDBF 2. Step: Find Shear Displacement
Interaction
coefficients
„Boundary conditions“
shear slip
N: # fractures
Condition for shear slip
Solve N x N matrix equation:
InterPore 2026
Same procedure for tensile opening: 2N x 2N matrix
Notes: Shear stress and normal are rewritten using our ansatz, so as a superposition of all the fracture specific basisfunctions. So essentially the shear stress is the summation over all the fractures of the induced force of fractures f on fracture g and the corrisponding weight/shear slip.
INDUCED FORCE BY FRACTURE F ON FRACTURE G. SO WE INTEGRATE OER THE SHEAR AND NORMAL STRESS INDUCED BY F ALONG G.

## Slide 5: Example: 33 Fractures
InterPore 2026

## Slide 6: 33-Fracture Test Case – Displacement and Stress Fields
66 dof
8‘000‘000 dof
InterPore 2026

## Slide 7: FDBF with Skewness
Displacement field:
+
=
Solve using Galerkin Method:
# Degrees of freedom for shearing = 2x number of fractures
InterPore 2026

## Slide 8: 33-Fracture Test Case – Shear Displacement
InterPore 2026

## Slide 9: 44-Fracture Test Case - Displacement
InterPore 2026
Splitting at intersections
  Example: 44 fractures  51 segmented fractures

## Slide 10: 4051 Fractures
5600 fractures after splitting at intersections
InterPore 2026

## Slide 11: „Same“ Method for Flow
Pressure
Basis function
  Assumption: all fractures have same distribution of sources and sinks
Weights
  found via the far field pressure drop over the fracture
basis function
weight
or
Daniel Stalder
MS03
Efficient Flow and Transport in Fractured Porous Media using the Basis Function Method
Friday 12:20 PM – 12:35 PM
InterPore 2026

## Slide 12: Results: Pressure Field
InterPore 2026

## Slide 13: Coupling
InterPore 2026
  Mechanics
  Criteria for shear slip
  Criteria for tensile opening
  Flow
  Criteria for pressure calculation
  Aperture from tensile opening and shear opening
Iterative coupling and checking the shear and tensile opening criteria at every iteration to determine mechanically active fractures

## Slide 14: Preliminary Results
InterPore 2026

## Slide 15: Summary
Mechanics and Flow calculation
Basis functions are calculated only once and then mapped
Only few dof per fracture  very efficient
Captures fracture interaction
Outlook:
Coupled simulations of highly fractured rock
Well injection test cases
InterPore 2026
Conti G., Matthai S., Jenny P., 2025, Fracture Displacement Basis Function (FDBF) Method for Efficient Geomechanical Calculations of Fractured Rock, Int. J. Rock Mech. Min. Sci.

## Slide 16: Coupled Flow and Mechanics Simulations using the Fracture Displacement-Pressure Basis Function Method for Highly Fractured Rock
Giulia Conti, Daniel Stalder, Patrick Jenny
Institute of Fluid Dynamics, ETH Zurich
Institute of Fluid Dynamics
InterPore 2026