## Slide 1
Physics-Preserving Enriched Galerkin Method for Fully-Coupled Thermo-Poroelasticity Model
Son-Young Yi
The University of Texas at El Paso
Collaborator: Sanghyun Lee (Florida State University)
InterPore 2026, May 21, 2026

## Slide 2: Outline
Background and Motivation
Enriched Galerkin Method
Numerical Examples
Summary and outlook
04
03
02
01

## Slide 3
Background & Motivation
01

## Slide 4: Thermo-Hydro-Mechanical (THM) Processes in Porous Media
THM processes refer to a complex interplay of heat transfer, fluid flow, and mechanical responses in natural and engineered porous media.
Applications:
Enhanced geothermal systems (EGS)
Carbon capture and storage (CCS)
Geological radioactive waste deposition
EGS
CCS

## Slide 5: Mathematical Model: Three Balance Equations
Governing Equations (Biot’s Thermo-Poroelasticity Model)
Primary Variables:
Functions
Momentum balance (Mechanics)
Mass conservation (Flow)
Energy conservation (Heat)
Notes: It is difficult to obtain analytical solutions for poroelasticity problems.
Therefore, solving poroelasticity problems relies mainly on numerical methods.

## Slide 6: Mathematical Model: Three Balance Equations
Governing Equations (Biot’s Thermo-Poroelasticity Model)
Parameters
Momentum balance (Mechanics)
Mass conservation (Flow)
Energy conservation (Heat)
Notes: It is difficult to obtain analytical solutions for poroelasticity problems.
Therefore, solving poroelasticity problems relies mainly on numerical methods.

## Slide 7: Numerical Trap for Each Subproblem
Near incompressibility can cause Poisson locking.
Engineering symptom:
Displacement becomes artificially stiff or inaccurate
Mechanics trap
Without local mass conservation, pressure and flux may be nonphysical near strong heterogeneity.
Engineering symptom:
Wrong injected/produced mass balance.
Flow trap
High K
Low K
(104 times lower)
Without local energy conservation, non-physical temperature and heat flux may be produced
Engineering symptom:
Temperature overshoots/undershoots, wrong thermal breakthrough time.
Heat trap
Goal: one discretization strategy that respects all three physics.

## Slide 8: Existing methods make trade-offs
Low Cost
Unified Analysis
CG
DG / MFEM
Mixed solvers
Physics-Preserving
Continuous Galerkin (standard FEM)
Efficient and familiar, but local conservation and locking robustness are not automatic
Discontinuous Galerkin / Mixed FEM
Excellent conservation and robustness, but many more degrees of freedom
Mix-and-match solvers (CG, DG, FVM, FDM)
Practical, but data transfer, coupling, implementation, and rigorous analysis become harder

## Slide 9: Research Goals
We want to develop numerical methods with the following properties:
Computationally robust
  Preserves underlying physical laws (e.g., mass conservation, energy conservation)
  Free of numerical instabilities (Poisson locking, overshoots/undershoots)
Computationally efficient
  Requires minimal number of degrees of freedom
  Existing codes or software utilization
Unified numerical framework
  Use the same type of method for the entire system for easier numerical analysis and implementation

## Slide 10
02

## Slide 11: Continuous Galerkin (CG) vs. Discontinuous Galerkin (DG)
CG
Discrete solution space
DG
Discrete solution space
Advantages: | Small number of DoFs Simple variational form
Disadvantages: | Can present some numerical instability issues (e.g., overshoot/undershoot, locking) Doesn’t satisfy local mass/energy conservation
Advantages: | Many nice properties (e.g., local mass conservation, good representation of discontinuous solution)
Disadvantages: | Large number of DoFs
Enriched Galerkin method sits between these two!

## Slide 12: Enriched Galerkin (EG) Method: Idea
Idea: Enrich the CG function space with a minimal set of discontinuous functions!
Advantages:
Computational cost: CG < EG << DG
Inherit many desirable properties from DG (e.g., local mass conservation, locking-free, etc)
Can utilize existing FEM codes for the CG and DG methods

## Slide 13: Locally-Conservative EG (LC-EG) Method
The LC-EG space: ℙ1CG + ℙ0DG
The discrete weak form is the same as the DG weak form.
Many nice properties from DG (e.g. local mass conservation) but with much lower computational costs.
Figure: Comparison of DOFs. A blue circle ( ) represents the enriched DOF.

## Slide 14: Locking-Free Enriched Galerkin (LF-EG) Method
The LF-EG space:
The LF-EG space contains non-trivial divergence-free vectors, allowing the EG method to be locking-free.
Figure: Comparison of DOFs. A red circle ( ) represents two DOFs and a blue triangle ( ) represents one DOF.
S.-Y. Yi, S. Lee, and L. Zikatanov, Locking-free enriched Galerkin method for linear elasticity, SIAM Journal on Numerical Analysis, vol. 60, no. 1, pp. 52--75, 2022.

## Slide 15: Coupled EG Method for Thermo-Poroelasticity
Mechanics
LF-EG displacement space
locking-free behavior
Flow
LC-EG pressure space
local mass conservation
Heat
LC-EG temperature space
local energy conservation
Fully discrete scheme = backward Euler in time + coupled EG in space
Key point: the subproblems communicate in the same finite-element language.
At each time step solve simultaneously for (u, p, θ)
mechanics residual 0 · mass residual 0 · energy residual 0
Key point: the subproblems communicate in the same finite-element language.

## Slide 16: Fully-Discrete EG Method for Thermo-Poroelasticity
Notation
: Average operator
: Jump operator

## Slide 17: What Was Proved Theoretically?
Lemma
Assume that
Then, the fully-coupled and fully-discrete EG method for solving the thermo-poroelasticity
problem has a unique solution at each time step, provided that the penalty parameters
and are large enough.
Well-posedness:
Optimal convergence:
S.-Y. Yi and S. Lee, Physics-preserving enriched Galerkin method for a fully-coupled thermo-poroelasticity, Numerische Mathematik, vol. 156, pp. 949 -978, 2024.
Notes: For this audience, the main takeaway is that the method is not only a practical discretization; it also has a rigorous stability and convergence foundation for the coupled THM system.

## Slide 18: Mass & Energy Conservation Properties

## Slide 19
Numerical Examples
03

## Slide 20: Ex.1: Convergence Tests with A Manufactured Solution

## Slide 21: Ex.1: Convergence Matches the Theory
Test 1 with Dirichlet boundary condition
Test 2 with mixed boundary condition
Takeaway: the observed convergence rates agree with the optimal-order error estimates.

## Slide 22: Ex 2. Coupled Response in Injection and Production
Setup
2D Homogeneous medium
Injection & production wells
Inj.
Prod.
Pressure (top) and temperature (bottom) & their cross-sections evolve consistently with sources/sinks
Displacement field

## Slide 23: Ex.3: Simulations in a Layered Medium
Simulation Setup:
2D layered medium
Injection & production well
Higher permeability
& heat conductivity
Pressure
Temperature
Displacement
What to notice
Layered/discontinuous coefficients are exactly where non-conservative methods can produce nonphysical behavior near interfaces.

## Slide 24: Ex.3: Local Conservation Residuals
Local mass conservation
residual:
Local energy conservation residual:
EG residual CG residual
Residual over time

## Slide 25
04
Summary

## Slide 26: Summary
THM simulations need robustness, conservation, and efficiency at the same time.
The coupled EG method uses LF-EG for mechanics and LC-EG for flow and heat.
The method is well-posed, optimally convergent, locally conservative, and computationally cheap (low DOF) for these properties.
Takeaways
Acknowledgements:
U.S. National Science Foundation (Grants DMS-2208402, DMS-2208426)
U.S. Department of Energy, Office of Science, Energy Earthshots Initiatives
(Award Number DE-SC-00240703)