## Slide 1
Luminescence Thermometry for Dynamic Imaging of Temperature distribution in Porous Media
Arwa Rashed1, Benoît Fond2, Sergey M. Borisov3, Yves Méheust1,4, Maria Klepikova1
1 Univ. Rennes, CNRS, Géosciences Rennes - UMR 6118, F-35000 Rennes, France 2 ONERA - The French Aerospace Lab, Department of Aerodynamics, Aeroelasticity and Acoustics (DAAA), Paris-Saclay University, Meudon, France 3 Institute of Analytical Chemistry and Food Chemistry, Graz University of Technology, Stremayrgasse 9, Graz 8010, Austria 4 Institut Universitaire de France (IUF)
Notes: Today I’ll present our work on applying luminescence thermometry for dynamic imaging of temperature distribution in porous media.
This work focuses on resolving how heat is transported at the pore scale under flowing conditions.

## Slide 2
Why pore-scale temperature imaging matters
The subsurface is inherently heterogenous, shaping how heat is transported
Non-intrusive
Geothermal energy
Water–groundwater interactions
Formation of microbial hotspots
Thermocouples
high temporal resolution
× no spatial context
Infrared Thermography (IRT)
Non invasive
× limited in water-saturated systems
Current experimental limitations
Non invasive
High spatial resolution
High temporal resolution
Novel application
Luminescence thermometry
Notes: This work is motivated by the importance of understanding heat transport in the subsurface.
Heat transport plays a major role in geothermal systems, groundwater–surface water interactions, subsurface energy storage, and also biogeochemical activity.
However, the subsurface is inherently heterogeneous, and this heterogeneity strongly influences how heat propagates through porous media. It can generate preferential flow pathways, uneven temperature distributions, localized thermal anomalies, and regions with limited thermal mixing. “Experimentally, studying these processes remains challenging.
Thermocouples provide high temporal resolution, but they are invasive and only provide point measurements without spatial information.
Infrared thermography is non-invasive, but water strongly absorbs infrared radiation, which limits its use in saturated porous systems.”
here we explore luminescence thermometry as an alternative approach.
This technique is already used in fields such as aerodynamics and microfluidics, but to our knowledge has not yet been applied to porous media heat transport.”
“And importantly, it allows non-invasive measurements with both high spatial and temporal resolution.

## Slide 3
[Russegger, et al., Adv. Optical Mater., 2023]
Recording time (frames)
Io
Luminescence (emission)
Intensity (I)
Excitation signal
Time (t)
LED excitation
Luminescence emission
PRINCIPLE
: Initial and maximum intensity before decay 𝜏: lifetime
How temperature is measured: Luminescence thermometry
Experimental setup
3
Notes: When excited by a pulsed LED, they emit luminescence whose intensity decays over time.”
This decay follows approximately a mono-exponential behavior, characterized by the luminescence lifetime tau.
The key point is that this lifetime decreases systematically with increasing temperature.
…by recording the emission decay using a high-speed camera and fitting the decay at each pixel, we can reconstruct a two-dimensional temperature field.
The experimental setup:
A blue LED provides excitation, while a Phantom high-speed camera records the emission.
The acquisition and LED excitation are synchronized using a signal generator.
The flow cell contains a synthetic porous medium connected to two syringes: one at room temperature and one heated using a heating jacket.
And temperature evolution is then monitored dynamically during injection. ..Before applying the method in flow experiments, we first calibrated the temperature response.

## Slide 4
Linking Luminescence Lifetime to Temperature
Calibration setup
0.5 mg/ml of Zr complex nanoparticles
Jacketed beaker and a thermostatic bath
T range: 18 – 45 oC
Temperature dependence on lifetime
Thermocouple reference temperature
4
Notes: For calibration, the nanoparticle suspension was placed in a jacketed beaker connected to a thermostatic bath.
A thermocouple was used as the reference temperature measurement while the lifetime was extracted at each temperature step.
The investigated range was between approximately 18 and 45 degrees Celsius.
As expected, the lifetime decreases smoothly with increasing temperature.
The calibration showed a relative sensitivity of approximately 2 percent per Kelvin, which is relatively good for optical thermometry measurements in this temperature range.
…Using this calibration, we then performed a proof-of-concept hot-water injection experiment.

## Slide 5
Hot-water injection into a synthetic porous medium
  Porosity 0.36
  Grain diameter range 6 – 8.5 mm
  Thickness 2 mm
  Thermal conductivity 2.72 W/m.K
Injected fluid | Dye-preheated water to 32 °C
Flow rate | 6.67 mL/min (Darcy velocity: 80 m/d)
Flow regime | Laminar (Re ≈ 1.33)
Thermal Péclet number | ~ 18 (convection-dominated)
Proof-of-concept experiment
Experimental conditions
Thermocouple junction
flow direction
0.5 mg/ml of dye in water at RT
Thermally conductive silicone
5
6 cm
Notes: The experimental flow cell used in this study:
The field of view contains a thermocouple junction positioned near the inlet region for independent validation measurements.
The porous structure was fabricated from a thermally conductive silicone with a conductivity of approximately 2.7 watts per meter Kelvin, within the range reported for geological materials.”
The medium has a porosity of 0.36, with heterogeneous grain diameters ranging between 6 and 8.5 millimeters.
The pore space was initially saturated with room-temperature water containing a low concentration of luminescent nanoparticles.
Then hot water at 45 degrees Celsius was injected upward through the medium.
The experiment was conducted under laminar flow conditions, with a thermal Péclet number around 18, indicating convection-dominated transport. …. the resulting temperature evolution.

## Slide 6
Pore-scale spatiotemporal temperature evolution
Flow direction: bottom → top
Field of view: 26.5 × 31.5 mm2
Image “snapshot” every 2.5 s
Snapshot at t = 45 s
Most rapid thermal front progression observed here
“Cold” zones
Temperature gradients persistent
over time
6
Notes: These are selected snapshots extracted during the injection experiment.
The flow direction is from bottom to top.
As soon as the hot fluid enters the field of view, we observe strongly heterogeneous temperature evolution.
“A preferential thermal front propagation is clearly visible along the left side of the domain, indicating preferential flow pathways through the pore space.”
“In contrast, some regions remain persistently colder because they are partially shielded from the dominant flow direction.”
We also observe localized temperature gradients near grain surfaces, reflecting the coupling between flow structure and heat transport.
The important point here is that these features are spatially resolved dynamically and non-invasively.
To evaluate whether the measured temperatures are quantitatively reliable, we compared them with independent thermocouple measurements.

## Slide 7
Validation Against Independent Temperature Measurements
  Mean temperature difference: 0.02 K
  Maximum absolute difference: 0.49 K
.
Spatial resolution: 0.25 mm/pixel
Temporal resolution: 130 ms
Pixel-to-pixel standard deviation of temperature: 0.1 K
Temperature precision
×
×
×
Validation Against Independent Temperature Measurements
7
Notes: The thermocouple measurements are shown here in black, while the blue points correspond to the temperature inferred optically from the surrounding pixels.
The shaded region represents the manufacturer uncertainty of the type-T thermocouple, which is approximately plus or minus 0.5 Kelvin.
As shown, the optical measurements follow the thermocouple evolution very closely throughout the injection experiment.
“The mean temperature difference was only 0.02 Kelvin, while the maximum absolute difference remained below 0.5 Kelvin.”
PRECISION: In addition to agreement with the thermocouple measurements, we also evaluated the intrinsic precision of the method under isothermal conditions. The pixel-to-pixel standard deviation was approximately 0.1 Kelvin at room temperature.
And the measurements were obtained with a spatial resolution of 0.25 millimeters per pixel and an effective temporal resolution of 130 milliseconds.
“So finally, we compared the experimental observations with numerical simulations.”

## Slide 8
Number of elements ≈ 90,000
Mesh size ≥ 6.64 µm, Timestep ≥ 0.075 s
FOV-Experiment
FOV-Model
FOV-Model
FOV-Experiment
Experimental and simulated temperature fields at t = 72.5 s
Observed agreement
Preferential thermal front propagation reproduced experimentally
Similar spatial thermal structures and localized cold zones observed
Discrepancy Thermocouple fitting and junction perturbation
Validation Against Independent Temperature Measurements
Comparison with pore-scale numerical simulation
8
Notes: The left side shows the experimental flow cell geometry and the corresponding numerical representation of the porous structure.
The right side compares the simulated and experimental temperature fields at 72.5 seconds.
The comparison shows strong qualitative agreement.
In both cases, the preferential thermal front progression is reproduced along the left side of the domain.
We also observe similar spatial thermal structures and localized colder regions associated with flow shielding and limited thermal mixing.
The main discrepancy occurs near the center of the experimental field. “Overall, the comparison suggests that the experimentally observed thermal structures are physically consistent with the coupled flow and heat transport processes.
This is caused by the thermocouple fitting and junction, which locally perturb the flow and temperature field but are not represented in the numerical model.

## Slide 9
Thank you for your attention
  — Full-field temperature analysis of the synthetic porous medium
  — Effect of flow rate on thermal transport dynamics — Influence of porous geometry on thermal transport
  — Experimental investigation of pore-scale thermal averaging scales (REV)
  Perspectives
  Conclusion
  First pore-scale application of lifetime thermometry for dynamic 2D temperature imaging in saturated porous media.
Notes: To conclude, this work demonstrates that lifetime-based luminescence thermometry can resolve transient pore-scale temperature fields in saturated porous media with high spatial and temporal resolution.”
In the coming work, we plan to extend the analysis to larger regions of the porous medium, investigate the effect of flow rate on thermal transport dynamics, and explore the influence of porous geometry.