## Slide 1: Improved Invasion Percolation Algorithm with Trapping for Pore Network Modeling
Homam Khatirzad Baboli1, Hans Janssen2, Stefan Vandewalle1
1 Department of Computer Science, Numerical Analysis and Applied Mathematics
2 Department of Civil Engineering, Building Physics and Sustainable Design

## Slide 2: Introduction: pore network modeling (PNM)
XCT 3D imaging
Pore network extraction
Invasion simulation
Objective: Using static PNM to study hygric properties of building materials
Permeability simulation
Moisture content calculation
Permeability calculation

## Slide 3: Introduction: invasion percolation with trapping
Invasion: through the lowest entry pressure path
Step 2: Identifying the trapped pores
Step 1: Fully saturated network
Inlet
Outlet
Trapped pores: disconnected from air pathway

## Slide 4: Introduction: importance of trapping
Trapping affects network properties.
 | Runtime
Invasion without Trapping | 42 min
Invasion with Trapping | 7 hours
Computationally expensive
# Pore bodies: ~190K
# Pore throats: ~250K
Trapping: 90% of IP

## Slide 5: Methodology: classical trapping
Classical trapping algorithm:
Start from the first invaded pore
Check the entire network for the outlet connectivity
Trapped pore → no outlet path exists
Invasion step: i+1
Invaded
Trapped
Connected to outlet
Inlet
Outlet
Impermeable
Impermeable
Invasion step: i
Disadvantage:
Going through entire network in each iteration
O(M.N)
Invasion step: i+2

## Slide 6: Methodology: backward trapping
Invasion step: j-1
Invasion step: j
Invaded
Trapped
Connected to outlet
Inlet
Outlet
Impermeable
Impermeable
Invasion step: j-2
Masson, Y. (2016). A fast two-step algorithm for invasion percolation with trapping. Computers & Geosciences.
O(M.N) → O(N)
Benefits:
Avoid full network searches
Check local neighbors' connectivity

## Slide 7: Methodology: trapping algorithm
Masson (2016)​
Pore trapping
Pore body + throat trapping
Structured lattice
Unstructured network
Separated invasion
Simultaneous invasion
This work
Algorithm customization:

## Slide 8: Methodology: implementation
Pore network
Node-based network

## Slide 9: Results: moisture content and permeability
Network size | Runtime (old algorithm) | Runtime (new algorithm) | Efficiency
# Pore bodies: ~72K # Pore throats: ~78K | ~ 25 min | 4 sec | 99.7%

## Slide 10: Results: moisture content and permeability
Network size | Runtime (old algorithm) | Runtime (new algorithm) | Efficiency
# Pore bodies: ~72K # Pore throats: ~78K | ~ 25 min | 4 sec | 99.7%
# Pore bodies: ~132K # Pore throats: ~114K | ~ 44 min | 5 sec | 99.8%

## Slide 11: Results: moisture content and permeability
Network size | Runtime (old algorithm) | Runtime (new algorithm) | Efficiency
# Pore bodies: ~72K # Pore throats: ~78K | ~ 25 min | 4 sec | 99.7%
# Pore bodies: ~132K # Pore throats: ~114K | ~ 44 min | 5 sec | 99.8%
# Pore bodies: ~190K # Pore throats: ~250K | ~ 5 h | 22 sec | 99.9%

## Slide 12: Results: moisture content and permeability
Network size | Runtime (old algorithm) | Runtime (new algorithm) | Efficiency
# Pore bodies: ~72K # Pore throats: ~78K | ~ 25 min | 4 sec | 99.7%
# Pore bodies: ~132K # Pore throats: ~114K | ~ 44 min | 5 sec | 99.8%
# Pore bodies: ~190K # Pore throats: ~250K | ~ 5 h | 22 sec | 99.9%
# Pore bodies: ~260K # Pore throats: ~330K | ~ 11 h | 44 secs | 99.9%

## Slide 13: Conclusion
Trapping in a PN is important in obtaining accurate result.
The classical trapping, is not efficient.
The backward algorithm only checks the neighbors.
A backward trapping algorithm is applied which resulted in >99% runtime reduction.

## Slide 14
Thank you for your attention!