## Slide 1
Mechanical behavior of dense suspensions in porous media: A pore-scale model
Nassim Cheikh1, Emmanuel Le Trong1, Cyprien Soulaine1
1Orléans Institute of Earth Sciences, France
InterPore 2026 meeting
May 21, 2026
nassim.cheikh@cnrs-orleans.fr

## Slide 2
Mechanical behavior of dense suspensions in porous media: A pore-scale model
May 21, 2026
InterPore 2026 Meeting
2
Context – Pore clogging
Sieving, bridging and aggregation
Lagrangian approaches: accurate but computationally expensive
Move into Euler-Euler approaches
Modified from Dressaire and Sauret (2017)
Sieving
Bridging
Aggregation

## Slide 3
Euler-Lagrange simulations
Simulation of the permeability reduction test on a complex geometry (Maya Fogouang 2025).
Euler-Lagrange simulation of particle transport and retention at pore scale
Accurate but very costly in terms of time and resources
This simulation ~ 1 week
The same in Euler-Euler ~ 4 hours
Mechanical behavior of dense suspensions in porous media: A pore-scale model
InterPore 2026 Meeting
3
May 21, 2026

## Slide 4
Euler-Euler model
Mass conservation
Momentum equation
+ Boundary Conditions
Mechanical behavior of dense suspensions in porous media: A pore-scale model
InterPore 2026 Meeting
4
May 21, 2026
Euler-Lagrange
Euler-Euler
Volume Averaging Method
Particles
Fluid

## Slide 5
Particle pressure
Particles interactions in shear stress flow (Guazzelli and Pouliquen, 2025)
Particle pressure : normal stress applied on the wall by particles
Suspension is incompressible so the particle pressure is balanced by fluid pressure
Mechanical behavior of dense suspensions in porous media: A pore-scale model
InterPore 2026 Meeting
5
May 21, 2026

## Slide 6
Particle pressure & viscosity
Mechanical behavior of dense suspensions in porous media: A pore-scale model
InterPore 2026 Meeting
6
May 21, 2026
Particle pressure
Shear effective viscosity
Gidaspow and Ettehadieh / Krieger
Boyer et al. / Boyer et al.

## Slide 7
Compression in a single pore
Gidaspow and Ettehadieh solid pressure
Nondeformable particles
Solid phase cannot go out: it will compress
Comparison with analytical solution (Hewitt et al., 2016)
Water flow
ΔP
Mechanical behavior of dense suspensions in porous media: A pore-scale model
InterPore 2026 Meeting
7
May 21, 2026

## Slide 8
Compression in a single pore
Mechanical behavior of dense suspensions in porous media: A pore-scale model
InterPore 2026 Meeting
8
May 21, 2026

## Slide 9
Clogging in a single pore
W
D
Mechanical behavior of dense suspensions in porous media: A pore-scale model
InterPore 2026 Meeting
9
May 21, 2026
Injection of solid phase in constricted channel
Boyer et al. solid pressure
Important parameters: W/D, solid volume fraction

## Slide 10
Clogging in a single pore
Mechanical behavior of dense suspensions in porous media: A pore-scale model
InterPore 2026 Meeting
May 21, 2026
10

## Slide 11
Clogging in a single pore
Mechanical behavior of dense suspensions in porous media: A pore-scale model
InterPore 2026 Meeting
11
May 21, 2026

## Slide 12
Solid Flux analyses
Mechanical behavior of dense suspensions in porous media: A pore-scale model
InterPore 2026 Meeting
12
May 21, 2026
Maximum flux
Final flux

## Slide 13
Heat map of clogging
Mechanical behavior of dense suspensions in porous media: A pore-scale model
InterPore 2026 Meeting
13
May 21, 2026
121 simulations in constricted channels
Solid pressure and effective viscosity from Boyer model
varying from 0.3 to 0.6 and varying from 3.5 to 0.8
Ratio of maximum flux to final flux as clogging factor

## Slide 14
Clogging in a complex geometry
Mechanical behavior of dense suspensions in porous media: A pore-scale model
InterPore 2026 Meeting
14
May 21, 2026

## Slide 15
Clogging in a complex geometry
Mechanical behavior of dense suspensions in porous media: A pore-scale model
InterPore 2026 Meeting
15
May 21, 2026

## Slide 16
Clogging in a complex geometry
Mechanical behavior of dense suspensions in porous media: A pore-scale model
InterPore 2026 Meeting
16
May 21, 2026

## Slide 17
Conclusion
A pore-scale Euler-Euler model developed to simulate the transport and retention of dense suspensions
Considering proper rheology for dense suspension according Boyer et al.
Ability of simulating clogging by sieving or bridging in constricted channel and complex geometry (test done on over 120 simulations)
Perspectives: Adapt the model to dilute suspensions by considering other rheological models. Add clogging by aggregation in the model.
Mechanical behavior of dense suspensions in porous media: A pore-scale model
InterPore 2026 Meeting
17
May 21, 2026

## Slide 18
Acknowledgement
We would like to acknowledge European Union for funding this project
(ERC COCONUT n°101043288)
nassim.cheikh@cnrs-orleans.fr
Mechanical behavior of dense suspensions in porous media: A pore-scale model
InterPore 2026 Meeting
18
May 21, 2026

## Slide 19
Clogging in a complex geometry
Mechanical behavior of dense suspensions in porous media: A pore-scale model
InterPore 2026 Meeting
19
May 21, 2026

## Slide 20
Permeability reduction test
Mechanical behavior of dense suspensions in porous media: A pore-scale model
InterPore 2026 Meeting
20
May 21, 2026

## Slide 21
Permeability reduction test
Mechanical behavior of dense suspensions in porous media: A pore-scale model
InterPore 2026 Meeting
21
May 21, 2026

## Slide 22
Context - NAPL pollution
Generalized Conceptual Site Model (CSM) with Nonaqueous Phase Liquid (NAPL) Release into the Subsurface (Ford et al., 2014)
Non-aqueous phase liquids (NAPL) : water-immiscible pollutants
Two types : Light NAPL and Dense NAPL
Long-term source of pollution
Trapping of NAPL droplets by capillarity
Mechanical behavior of dense suspensions in porous media: A pore-scale model
InterPore 2026 Meeting
22
May 21, 2026

## Slide 23
Volume Averaging Method
Macroscopic region and local averaging volume (Whitaker, 1997)
Note that :
Intrinsic average
Superficial average
Mechanical behavior of dense suspensions in porous media: A pore-scale model
InterPore 2026 Meeting
23
May 21, 2026