## Slide 1: Unravelling Reactive Transport in Subsurface Rocks: Can We Predict What We Measure?
Jacqueline Mifsud1*, Hannah Menke1, Florian Doster1, Callum Robinson2, Sam Shaw2, Katherine Morris2, Jingyue Hao3, Lin Ma3, Aislinn Boylan4, Liam Abrahamsen-Mills4, Vasileios Tsitsopoulos4, Keith Bateman5, Julien Maes1
1 Institute of GeoEnergy Engineering, Heriot-Watt University, Edinburgh, EH14 4AS, UK
2 Department of Earth and Environmental Sciences, The University of Manchester, Manchester, M13 9PL, UK
3 Department of Chemical Engineering, The University of Manchester, Manchester M13 9PL, UK
4 United Kingdom National Nuclear Laboratory, Warrington, Cheshire WA3 6AE, UK
5 British Geological Survey, Environmental Science Centre, Keyworth, Nottingham, NG12 5GG, UK
*Email: J.Mifsud@hw.ac.uk
Interpore 2026, MS09 – Pore-Scale Physics and Modelling
19th May 2026
The
GeoChemFoam
Project
In collaboration with:
Funded by:
Notes: Good afternoon everyone, I’m Jacqui, I’m a post-doc at Heriot-Watt working on the GeoSafe project. I will speak to you today about some of the work that I have been doing since joining the university, and specifically my talk today will look at “Unravelling Reactive Transport in Subsurface Rocks, and discuss whether we can reconcile some experimental data with numerical models.

## Slide 2
GeoSafe Project Overview
To undertake fundamental research that will advance our understanding related to hosting a Geological Disposal Facility (GDF) for radioactive waste within Lower Strength Sedimentary Rock formations.
3 challenge areas:
  Geological isolation
  Contaminant pathways
  Mathematical modelling
7 UK research organisations
  5 universities:
    Imperial College London
    University of Manchester
    University of Liverpool
    University of Leeds
    Heriot-Watt University
  2 institutions:
    United Kingdom National Nuclear Laboratory
    British Geological Survey
Project website now live: https://geosafeproject.co.uk/
Underground tunnels and vaults of a GDF in an inshore location.
Up to 1000m underground. Source: https://www.nuclearwasteservices.uk/disposal/geological-disposal/
Notes: My work at Heriot-Watt is part of the GeoSafe project so I thought it would be good to introduce the scope of the project. The aim of the GeoSafe project is to conduct fundamental research that will advance our understanding related to hosting a Geological Disposal Facility (GDF), for radioactive waste, within Lower Strength Sedimentary Rock formations in the UK. We are predominantly looking at 3 challenge areas, Geological isolation, contaminant pathways, and mathematical modelling. The project is between 7 UK research organisations, 5 universities, Imperial, Manchester, Liverpool, Leeds, Heriot-Watt and two institutions, the UK National Nuclear Laboratory and the British Geological Survey.
If you are interested in more detail on the project, the project website is now live. ** Geological isolation challenges: characterisation and conceptualisation of geological complexity and heterogeneity at multiple length and time scales within LSSRs
Contaminant pathways: developing a mechanistic understanding of retention and/or transport within LSSRs
Mathematical models: development of system level mathematical models of key sedimentary systems.

## Slide 3
Biogeochemistry
Radiochemistry
Hydro-Mechanical Modelling
Reactive Transport Modelling
Rock Characterisation
Multi-scale Imaging
GeoSafe Project Overview
Notes: It is a highly collaborative effort between the various institutions, and brings together experts from all over the UK. The following schematic gives an overview of the different bits of research being conducted and where, so we have people working on rock characterisation, multi-scale imaging, radiochemistry etc, and you can see that here at Heriot-Watt in Edinburgh we are predominantly concerned with the reactive transport modelling and specifically we are looking at pore-scale reactive transport modelling.
(We are also mainly working with colleagues working on multi-scale imaging and radiochemistry.)

## Slide 4
How is pore-scale reactive transport modelling relevant to GeoSafe?
Relevance to Geological Disposal Facility (GDF) programme
  Geochemistry impacts fate of radionuclides in the subsurface
  Small scale characterisation will lead to better modelling at the larger scale
  This work investigates subsurface rocks targeted by GeoSafe
  Experimental parameters can affect reactive constants:
    Simulations facilitate relatively inexpensive parametric studies to quantify effects (e.g. different flowrates)
INSERT GDF figure
U6+
Quartz
Quartz
Quartz
Clay
UO2
U6+
adsorption
Precipitation
Notes: So how is our work at Heriot-Watt relevant to the GDF programme?
Many of you will know that geochemistry impacts the fate of radionuclides in the subsurface. What we are concerned with in our work is the pore-scale which might not seem immediately relevant to the large-scale of a GDF. Yet this small-scale characterisation will lead to better modelling at the larger scale.
Also although the workflow I will show today can be applied to any rock, we are specifically investigating subsurface rocks targeted by GeoSafe.
Finally, one of the benefits of modelling is that we can perform parametric studies fairly quickly in comparison to experiments, and this helps us understand effects e.g. how does a higher or lower flowrate impact radionuclide transport?
And more broadly, output parameters from our simulations will output directly to reactive transport upscaling.
(Refer to comments from Julien’s talk in March meeting.)

## Slide 5
University of Manchester: Flow-through & batch experiments on pellet sample
University of Manchester: Image pellet sample in 3D
Heriot-Watt & UKNNL: Simulate (radionuclide) transport using 3D images and experimental parameters
Modelling results
and
experimental data
validation
Overview of GeoSafe Collaboration
Notes: So hopefully by this point you have a better idea of the capabilities of GeoChemFoam, now in the next part of my talk I will discuss how we apply this open-source code and leverage some of its capabilities in our GeoSafe project.
(A few slides back I introduced the concept of Digital Rock Physics and how we can perform simulations on the exact pore-space.) In this part of our GeoSafe work we are working closely with the University of Manchester, and the UK National Nuclear Laboratory. So first our collaborators are running some experiments on this flow through cell, so it’s a sample of crushed rock pressed into this perspex slide, then this same sample is sent to another group at Manchester which performs the imaging, and finally that experimental data and images come to us at Heriot Watt where we plug them into our simulator.

## Slide 6
Overview of GeoSafe Collaboration
University of Manchester: Flow-through & batch experiments on pellet sample
University of Manchester: Image pellet sample in 3D
Heriot-Watt & UK NNL: Simulate (radionuclide) transport using 3D images and experimental parameters
Modelling results
and
experimental data
validation

## Slide 7
Experiments: Advective Flow Column
Flow experiment on reaggregated pressed pellet of rock
Performed by colleagues at the University of Manchester (UoM)
Flow cells developed by British Geological Survey (BGS)1
Breakthrough curve with fluorescein:
  Flowrate: 0.55 ml/hr
  Porosity: 40%
1Bateman, K. et al. Evolution of the Reaction and Alteration of Granite with Ordinary Portland Cement Leachates: Sequential Flow Experiments and Reactive Transport Modelling. Minerals 2022, 12 (7).
Pressed pellet of rock. Sample size (cylindrical), 2cm diameter, 1cm length.
2 cm
Flow cells developed by BGS1

## Slide 8
University of Manchester: Flow-through & batch experiments on pellet sample
University of Manchester: Image pellet sample in 3D
Heriot-Watt & UK NNL: Simulate (radionuclide) transport using 3D images and experimental parameters
Modelling results
and
experimental data
validation
Overview of GeoSafe Collaboration

## Slide 9
Voxel size 5.5, 3442 x 3442 x 1609 voxels.
Segmented CT image of pressed column of clay-rich rock.
CT-Image Analysis: Pressed Pellet
Several CT scans at voxel resolution of performed by University of Manchester
CT-image chosen for computational domain is 3442 x 3442 x 1609 voxels
  Computational domain is slightly smaller than in experiments (1.89cm x 1.89cm x 0.88cm in image vs. 2cm x 2cm x 1cm in experiments)
Sample is clay-rich rock that has been crushed
  hence may not resemble typical clay microstructure (layers etc.)
Grains
Pores

## Slide 10
University of Manchester: Flow-through & batch experiments on pellet sample
University of Manchester: Image pellet sample in 3D
Heriot-Watt & UK NNL: Simulate (radionuclide) transport using 3D images and experimental parameters
Modelling results
and
experimental data
validation
Overview of GeoSafe Collaboration

## Slide 11
Simulations: From CT-image to computational model
Computational model of segmented CT-image built in GeoChemFoam
GitHub page: www.github.com/GeoChemFoam
Model requires porosity, , & permeability, , specified for each voxel:
  solid grains,
  pores,
Illustrative examples of tracer evolution in simulations below,
  injecting at experimental flowrate
  for different Pe regimes
Computational domain: porosity & permeability specified per voxel.
flow direction
Velocity streamlines show tracer concentration T against time for different pore-scale Peclet numbers . Concentration of T: Purple = 1; Green = 0. Side view.
CT image
In GeoChemFoam model:
The
GeoChemFoam
Project
Notes: Note that these animations assume the porosity is 10%, i.e. microporosity is fully non-porous.
Different Peclet numbers modelled by changing value of diffusion coefficient
The core-scale Peclet number tells us what is going to arrive first at the outlet, and if this flow reaching the outlet would be advection or diffusion dominated. In this case, we see that 𝑃𝑒_𝑐𝑜𝑟𝑒 is always greater than 1, so the flow at the core-scale is advection dominated. In contrast, the pore-scale Peclet number tells us whether the flow will be advection or diffusion dominated to the NEXT PORE, rather than at the core-scale. Note that the results for Tout were obtained using the processScalarOutlet utility but without the gSum option implemented by Julien
The simulations are located on HWLX0048 here: ~/works/breakthroughPellet/crop_not_distort/newimages/sims_for_pres/Pellet_vdev_crop_half_Pdrop_00015_200_crop1_devscripts_newimg_Pe_0_1 ; Pe_1; Pe_10

## Slide 12
Experimental breakthrough curve of fluorescein in reaggregated pellet
Our initial attempts at matching tracer transport simulations with the experimental results revealed that our timescales are dissimilar, and breakthrough happens much faster in simulations…
Preliminary results: Validation with Experiments
flowrate
time
porosity
volume
2 important features will help improve our agreement with the experiments:
1. Sorption
2. Dispersivity
Notes: These preliminary results show that in our simulations, the outlet is reach after around, 2-3 PV_injected. Yet, in the experiments, this takes over 15 pore-volumes injected, so having consulted our colleagues on this the first suspicion is that there is some sorption going on in the experiments, which was not anticipated.

## Slide 13
1g disaggregated rock and 30ppm fluorescein in 10ml of groundwater.
After an equilibration period, the amount of fluorescein sorbed is measured.
Distribution coefficient,
ml/g;
initial concentration, final concentration, volume (), mass ().
Batch sorption experiments: Fluorescein
Rock sample
Rock minerals
Water
Fluorescein
Fluorescein
7 days
Notes: So, in order to determine how much sorption there is, they perform some batch sorption experiments, so the idea is to take 1g of disaggregated rock and 30ppm fluorescein in 10ml of groundwater, then after an equilibration period of one week they measure the amount of fluorescein sorbed, and we have this value of distribution coefficient Kd here which is equal to 1.96ml/g.
(i.e. we assume that after 7 days that fluorescein has equilibrated).
https://taylorandfrancis.com/knowledge/Medicine_and_healthcare/Pharmaceutical_medicine/Distribution_coefficient/

## Slide 14
Linear sorption model,
,
where sorbed concentration,
concentration in solution,
ml/g (from batch experiments).
1D Reactive Transport Modelling in PHREEQC
*2025, PHREEQC Version 3, Software release, https://www.usgs.gov/software/phreeqc-version-3.
inlet
outlet
Example TRANSPORT block in PHREEQC model:
TRANSPORT
-cells 10
-shifts 219
-time_step 822.5 s
-boundary_conditions constant flux
-lengths 10*1e-3
-dispersivities 0.001 #initial guess
-punch_cells 10
-print_cells 10
1D RT model in PHREEQC (code developed by US Geological Survey)
Transport model developed by UKNNL

## Slide 15
The longitudinal dispersion () is related to the dispersivity (), pore-velocity () and molecular diffusion () in the porous medium
Influence of diffusion & dispersivity Comparing experimental data & PHREEQC 1D model
Phreeqc 1D model with:
  for fluorescein (blue line) and experimentally measured
15
pore-scale velocity variations + molecular diffusion = solute spreading at continuum scale (dispersion)
Dispersion is important for modelling & predicting contaminant and radionuclide transport in the subsurface
yet correct value to use is geometry-specific & unknown a priori!
Discrepancy attributed to lack of dispersion in model
Notes: So even by implementing the linear sorption model in the 1D Phreeqc model we see a huge improvement in the match with the experiments, however there is still some deviation between the experiments and the Phreeqc model, which we want to try and improve if we can. We attribute this to dispersion, but we do not know how much dispersion we have in our geometry.

## Slide 16
dispersionFoam* solver in GeoChemFoam accurately quantifies dispersion on a micro-CT image of the rock sample – solves a closure problem
Calculating dispersivity in GeoChemFoam
Computational domain: porosity & permeability specified per voxel.
CT image
In GeoChemFoam model:
*Maes & Menke, Journal of Environmental Chemical Engineering (2024)
GeoChemFoam links flow experiments & PHREEQC model, eliminating the need to guess dispersivity (or use as a fitting parameter)
GeoChemFoam computes
  (fluorescein) 
  Feedback DRP-informed value of dispersion to Phreeqc 1D (orange line) – excellent agreement with experiments.
inclusion of dispersion in model yields better agreement with experiments

## Slide 17
Simulations facilitate parametric studies on CT image
  e.g. How does dispersivity vary for higher/lower flowrates?
Dispersivity normalised with diffusion coefficient
vs
Deduced a fit of the following form:
  where is the tortuosity, and are fitting coefficients
Best fit
Increasing flowrate
Dispersivity predictions vs Peclet number (flowrate)
Experiments,
Expressed in terms of Peclet number
varying (flowrate),
where – porosity, – characteristic pore-size
Simulations complement experimental dataset by simulating different conditions (e.g. flowrates)

## Slide 18
Conclusions & Future work
Conclusions
  Developing a tool that simplifies upscaling, complementing experiments.
  Digital Rock Physics (DRP) in GeoChemFoam eliminates the need to guess dispersivity to fit experiments.
  Similar DRP-informed workflow can be applied to other rock-types and reactions, if a CT-image is available to input in GeoChemFoam.
  DRP enables relatively inexpensive parametric studies to quantify behaviour, e.g. higher/lower flowrates.
Future work
  Next steps:
    Benchmark simulations with experimental measurements of inert tracer transport
  In the meantime, we developed a new reactive transport solver:
    Previous model too slow and too memory hungry  limited to images
    New model allows much larger domains > 1000 voxels
    Ready to start running reactive transport model on the pellet geometry
Numerical simulation of Strontium adsorption (illustrated on Estaillades image)
Numerical simulation of non-reactive transport in reaggregated oxford clay sample

## Slide 19
Acknowledgements
Collaborators:
  DigiPorFlow Group at Heriot-Watt https://digiporflow.site.hw.ac.uk/
  GeoSafe colleagues https://geosafeproject.co.uk/:
    Heriot-Watt: Julien Maes, Hannah Menke, Florian Doster
    University of Manchester: Jingyue Hao, Lin Ma, Kevin Taylor Callum Robinson, Sam Shaw, Katherine Morris
    UK National Nuclear Laboratory: Vasileios Tsitsopoulos, Aislinn Boylan, Liam Abrahamsen-Mills
    British Geological Survey Keith Bateman, Ruth Delina-Agillon
Funding:
  NERC Grant: NE/Y002504/1 (PI: Florian Doster) Towards Safe Geological Disposal of Radioactive Waste in Lower-Strength Sedimentary Rocks (GeoSafe)
  Nuclear Waste Services https://www.nuclearwasteservices.uk/
HPC facilities and associated support services:
  UK national supercomputing facility ARCHER2 https://www.archer2.ac.uk. Beckett, G., Beech-Brandt, J., Leach, K., Payne, Z., Simpson, A., Smith, L., Turner, A., & Whiting, A. (2024). ARCHER2 Service Description. Zenodo. https://doi.org/10.5281/zenodo.14507040
The
GeoChemFoam
Project
DigiPorFlow group, 2025.
  Scan to be directed to the 9th Annual UK Interpore Chapter Conference 2026 website for details! 1-2 September 2026, Heriot-Watt University, Edinburgh, United Kingdom

## Slide 20: Thank you for your attention!
The
GeoChemFoam
Project
In collaboration with:
Funded by:
Any questions?