## Slide 1
Pore-scale dynamics of salt precipitation during brine-CO₂ displacement in micromodels
Lijuan Shi & Alexander Shapiro
CERE – Center for Energy Resources Engineering
Chemical and Biochemical Engineering,
Technical University of Denmark
1

## Slide 2
2
Why do we care?
Salt precipitation controls injectivity in subsurface applications
Where does salt precipitate?
What controls the precipitation dynamics at the pore scale?
How fast does salt grow?
What controls the growth dynamics at the pore scale?
How does injection rate matter?
How does injection pressure influence breakthrough, dry-out, and salt distribution?
Ai generated

## Slide 3
3
Experimental Strategy
Micromodel experiments with dual imaging systems
1. Chip Cleaning and Drying
2. Brine Saturation
3. CO₂ Injection and Imaging
4. Cleaning and Reuse
Chip type uniform
Pore volume 2.08 µL
Size (L×W) 20×10 mm
Chanel Depth 20 µm
Permeability 8.43-10.14 D
Porosity 52%
Dual Imaging Systems
MIS (pore-scale)
FFIS (chip-scale)
Field of view:
2.5 × 1.7 cm
Resolution:
8192 × 5464
3.05 µm/pixel
Field of view:
782 × 521 µm
Resolution:
4752 × 3168
0.165 µm/pixel
Water flushing, followed by CO₂ injection removes residual moisture
150 g/L NaCl brine injected until full saturation
Continuous imaging during displacement and dry-out
Water flushing followed by CO₂ drying
inlet
outlet

## Slide 4
Microscopic image
A : salt-affected region;
: average grayscale value at the reference
phase (gas or liquid);
: average grayscale value at time t.
Brine (green)
Salt (yellow)
Full-view image
4
Image analysis
Salt Precipitation Index (SPI)
Quantifies salt accumulation based on the salt-covered area and grayscale evolution
OpenCV-based segmentation

## Slide 5
5
Two distinct salt morphologies emerge
Transparent crystals
(liquid-rich regions)
Form near water–gas interfaces
Slow and localized growth
Well-defined crystal structure
Dark porous aggregates
(gas-dominated regions)
Form in gas-filled pores with residual brine nearby
Rapid accumulation
Irregular porous structure
Aggregate growth is
~6× faster
than crystal growth
Different local conditions lead to fundamentally different salt structures and growth rates.

## Slide 6
6
Dry-out Dynamics: CO₂-driven dry-out proceeds through three stages
Stage 1
Stage 2
Stage 3
29min
54min
79min
3min
64min
44min
Stage 1
Slow displacement
Stage 2
Rapid displacement
and salt onset
Stage 3
Slow-down and
final salt precipitation
Salt precipitation fundamentally alters the displacement dynamics during CO₂-driven dry-out.

## Slide 7
7
Injection Rate Effect
Higher injection rates may result in instable displacement
130 mBar
170 mBar
300 mBar
Before breakthrough
After breakthrough
1. Breakthrough time decreases (black line)
2. Brine saturation decline rate increases (red line)
3. Residual brine saturation first increases then decreases (blue line)
4. Residual brine saturation at the onset of salt precipitation
Brine saturation decreases linearly
2.26%/s at 130mBar, 10.24%/s at 170 mBar, 37.24%/s at 300 mBar.

## Slide 8
8
Mechanisms
Salt onset is governed by the competition between evaporation and displacement
pressure (mBar) | saturation at breakthrough (%) | saturation at salt onset (%) | The actual reduction (%) | water loss due to evaporation (%)
130 | 23.4 | 11.4 | 12.0 | 12.7
170 | 37.6 | 7.6 | 30.0 | 20.4
300 | 32.1 | 4.7 | 27.4 | 17.4
Low pressure (~130 mbar)
Displacement is relatively uniform and stable
Evaporation dominates after breakthrough
CO₂ invasion becomes weaker
Salt forms at higher residual brine saturation
High pressure (~300 mbar)
Displacement is finger-like (unstable)
CO₂ continues displacing brine after breakthrough
Fingering persists
Salt onset occurs at much lower brine saturation
Pressure shifts the balance : evaporation-dominated →displacement dominated

## Slide 9
9
Stochasticity
Dry-out dynamics are highly stochastic even under identical conditions
Large variation in dry-out time
60-160 min
After-breakthrough brine saturation varies
12% - 16%
The process is inherently unstable and stochastic
Small pore-scale differences amplify into large-scale variability.

## Slide 10
10
Take-home Messages
1
2
3
Two distinct salt morphologies
Crystals in liquid-rich zones; aggregates in gas-dominated regions. Aggregates grow ~6× faster.
Pressure controls the dry-out pathway
Higher pressure accelerates breakthrough and shifts the balance from evaporation to continued displacement.
The process is inherently unstable
Large run-to-run variability makes salt precipitation difficult to predict.