## Slide 1: Salt Precipitation Dynamics in Carbon Dioxide Storage: A Pore-Network Modelling Study
Yuxi Liang
Department of Earth Science & Engineering
Supervisors: Prof. Martin Blunt, Dr. Branko Bijeljic
22/05/2026

## Slide 2: Section 1. Introduction & Motivation
2
Physical Process
Dry CO₂ injection into saline aquifers:
Brine evaporation into CO₂
Increasing local salinity
Salt precipitation in pores / throats
Why it Matters
Salt precipitation may:
Block pores & throats
Reduce permeability & injectivity
Affect long-term storage performance
Why Pore-Scale Modelling?
Process is strongly pore-scale dependent:
Multiphase transport
Evaporation & precipitation coupling
Strong heterogeneity effects
Pore-network modelling:
Captures pore-scale physics
Computationally efficient
Bridges micro-CT and continuum behaviour
Why Salt Precipitation Matters During CO2 Storage
1
2
3
Dry CO2 Injection into Saline Aquifer
Similar Precipitation Phenomena in Other Environments
Pore-Scale Heterogeneity & Modeling
Micro-CT of Porous Rock
Salt Damage in Infrastructure
Soil salinization (Agriculture)
Pore-Network Model
Adapted from Zhang et al., J. Cleaner Production (2025)

## Slide 3
3D Visualization of Salt Precipitation Evolution in Bentheimer Sandstone
Section 1. Introduction & Motivation
Dry CO2
injection
Dry CO2 enters from the inlet boundary (not explicitly visualised)
Drying initiates near the inlet boundary
The precipitation region propagates through the network
Precipitated salt becomes spatially heterogeneous over time
What is shown in the video
Visualisation of precipitation evolution during dry CO2 injection (Video shows cumulative salt precipitation only).
Salt precipitation evolves as a highly heterogenous pore-scale process.
NaCl (solid)

## Slide 4
Dry CO2
Section 2. Salt Precipitation Framework
Pore-Scale Evolution During Dry CO2 Injection
Drainage
Dry CO2 invades the pore network.
CO2 (gas)
Brine (liquid)
Water vapour(gas)
NaCl (solid)
Evaporation
Water evaporates from connected brine layers into the CO2 phase.
Concentration increase
Salt concentration rises in remaining brine.
Precipitation
Salt precipitates in pores and throats.
Dry CO2 injection drives coupled evaporation and salt precipitation, leading to pore structure evolution and flow alteration.
Evaporation increases brine salinity, leading to pore-scale salt precipitation.
1
2
3
4

## Slide 5
Section 2. Salt Precipitation Framework
Coupled Evaporation-Precipitation Modelling Framework
Evaporation of Water
      = equilibrium concentration of water in CO₂
Salt Precipitation
= salt concentration in brine
= saturation concentration of NaCl
Water vapour transport in the CO₂ phase
Advection-diffusion transport of water vapour in CO2
= concentration of water vapour in CO2 phase
We solve coupled transport, evaporation and precipitation processes sequentially at each time step.
B. Key Model Relations
A. Numerical Coupling Loop (per time step)
Gas core
Salt layer
Corner water
Solve vapour transport
Advection-diffusion of water vapor in the CO2 phase
Compute local evaporation
Evaporation occurs where CO2 is undersaturated
Update brine salinity
Salt concentration increases in remaining brine
Initialise post-drainage brine configuration
Residual brine distribution after CO2 drainage
Check precipitation criterion
Salt precipitates where brine is locally oversaturated
This is a coupled transport-evaporation-precipitation framework prior to hydraulic feedback (e.g. permeability evolution).

## Slide 6: 1-D Validation: Drying-Front Propagation
1 2 3 4 5 6 7 8
  Gas-phase removal of water (moles)
  Water initially stored in the porous medium
  Definition of dry front
  Mass balance
Section 3. Validation & Results
Excellent agreement between analytical prediction and numerical dry-front propagation validates the evaporation-driven transport framework.
Salt precipitation initiates after local brine concentration reaches supersaturation
1. Analytical Derivation
2. Numerical Results
3. Salt Precipitation
Dry CO2 injection

## Slide 7: 1D vs 3D Evaporation-Precipitation Dynamics
Key Takeaway
Section 3. Validation & Results
Both 1D and 3D models capture the same evaporation-driven transport trend, while 3D networks exhibit broader fronts and heterogeneous salt accumulation due to pore-scale connectivity effects.
Vapour Concentration (Cv/Cv,eq) Water Volume (Vw/Vw0) Salt Precipitation (np, mole)
3D
Pore Network
1D Chain Network
··· ···
1D Chain Network 3D Bentheimer Pore Network

## Slide 8
Permeability update
Permeability Reduction & Flow Redistribution
Section 3. Validation & Results
Mechanism: Salt-Induced Throat Constriction
Key Relations
Results: Local Conductance & Permeability Evolution
Conductance reduction
Only modest permeability reduction (~1%)
Spatially heterogeneous conductance changes
g0: initial throat conductance
g: current throat conductance
fs: local precipitated salt fraction (cross-sectional area ratio)
k0: initial permeability
rold: original pore / throat radius
rnew: updated effective radius
Salt precipitation
Salt accumulates on pore / throat surfaces
Conductance reduction & flow update
Lower conductance g
Recompute flow field
Radius reduction
Effective radius rnew
( <r0 )
Clean pore-throat
Initial radius r0
Conductance g0
This motivates the next step: capillary-driven re-imbibition
Local throat
constriction
Conductance reduction
g
Flow redistribution
Permeability reduction
k
Radius reduction
r
Without re-imbibition, salt precipitation alone leads to only modest permeability reduction (~1%) under dry-CO₂ conditions.
Key Takeaway
Brine
Salt

## Slide 9
Section 4. Re-imbibition Physics
Why Re-imbibition Matters
Dry CO2
CO2
Remaining corner water (thin films)
Film swelling (capillary-driven)
Enhanced wetting connectivity
Salt precipitation changes pore geometry
Salt deposits reduce radius of pores & throats and alter capillary entry conditions.
Remaining corner water creates capillary suction
Thinning layers in corners generate higher capillary pressure.
Corner brine can flow back into dried/partially dried regions
Capillary-driven backflow occurs spontaneously without external brine injection.
This may enhance local salt redistribution and blockage
Salt can dissolve, transport and re-precipitate, further modifying geometry and flow.
Outcome
Enhanced wetting-phase connectivity.
Salt redistribution and possible re-precipitation.
Potential hydraulic feedback on pore transport and connectivity.
Corner water in a pore
Salt layer
Corner water
1
2
3
4
CO2 (gas)
Brine (liquid)
Water vapour (gas)
NaCl (solid)
New physics after salt precipitation during dry CO2 injection.
Gas core

## Slide 10
Section 4. Re-imbibition Physics
Numerical Re-imbibition Workflow
  Salt transport update
  Salt concentration
Corner-water redistribution
Numerical update sequence (per time step)
Corner-water flux between elements
Geometry and flow field feedback
Salt transport
Advective transport of salt
Water flux
Compute fluxes
Wetting layer growth
Update corner water volume
Corner-film expansion
Update wetting-layer connectivity
Precipitation / dissolution
Check Ci vs. Csat
Compute pressures
compute Pc,i and water pressure Pw,i
Geometry & conductance
Update and
Salt precipitation
Radius reduction
Updated flow field
Conductance reduction
If , precipitate

## Slide 11
Section 5. Conclusions & Outlook
Conclusions & Outlook
CO2
Pore-scale evaporation and salt precipitation influence transport and hydraulic evolution during dry CO2 injection into saline aquifers.
Key Findings
Dry CO2 injection drives evaporation-induced salt precipitation at pore scale.
The 1D analytical solution shows excellent agreement with numerical dry-front propagation, validating the evaporation-driven transport framework.
3D pore networks exhibit broader drying fronts and stronger spatial heterogeneity than 1D systems.
Salt precipitation alters local geometry and flow, but re-imbibition should be included to capture the full hydraulic feedback
··· ···
Outlook: Re-imbibition
Salt redistribution and re-precipitation may further modify pore geometry and flow connectivity.
Remaining corner water may generate capillary-driven backflow after precipitation.
A numerical re-imbibition algorithm has been developed and will be coupled with the evaporation-precipitation framework.
Why it Matters
Re-imbibition introduces potential feedback on pore connectivity, salt transport and long-term storage performance.
Questions?
Thank you!
Take-Home Message
Pore-scale heterogeneity, salt-precipitation and re-imbibition jointly control hydraulic evolution during dry CO2 injection into saline aquifers.