## Slide 1
Modelling the Drying Process of CO₂-Water in Porous Media with a Novel Volume-of-Fluid Lattice Boltzmann Model
INTERPORE 2026
¹ University of Manchester · ² TU Delft · ³ Shell Global Solutions International
Published in Water Resources Research, 2026
Saleh Mohammadrezaei¹ · Rouhi Farajzadeh²,³ · Vahid Niasar¹

## Slide 2: Why Drying In Porous Media Matters
Agriculture Affects soil moisture balance, influencing yield and root health
Or et al., 2013
Food and pharmaceutical industries
Determines shelf life, drying uniformity, and product stability Prawiranto et al. 2019
Buildings Leads to salt efflorescence, causing damage and reducing durability Qazi et al, 2019
Notes: Agriculture, drying influences the soil moisture distribution, which directly affects crop yield and soil health {*or2013advances}

## Slide 3: Carbon Capture and Storage (CCS)
Two phase displacement
  Flooding front
  Residual brine
  Capillary flow
Up to an 80% decrease in permeability
Evaporation
  Drying front
  Increase salt saturation in brine
  Salt precipitation
  Injectivity Loss
© Prof. Vahid Niasar
THE CHALLENGE

## Slide 4
Analysis of water redistribution due to drying
Mass balance for a group of pores in fine and coarse domains
Hagen-Poiseuille equation
Since water flux is induced by capillarity and pressure drop is neglected in the gas phase:
Compares the impact of evaporation to capillary forces:
High Γ: Evaporation dominates, resulting in steady and uniform drying.
Low Γ: Capillary forces dominate, leading to complex, nonlinear saturation patterns.
4

## Slide 5
2D case studies
Key parameters and schematic views for the three case studies.
5

## Slide 6
Geometry of the rock sample derived from micro-CT scans, showing the dimensions and boundary conditions used in the 3D simulations.
3D case studies
Micro-CT scans of actual rock samples from three overlying sandstone layers exposed in Lower Cretaceous fluviatile sands on Mount Carmel, Northern.
Simulation Size:
0.6 × 0.6 × 0.6 mm3
6
Case 4:
Case 5:

## Slide 7
Validation
7
Height of the capillary interface in the capillary tubes over time
Two interconnected vertical capillary tubes
Co-current channel
Two-layer flow, ρ-ratio 10⁻³ ν-ratio 10
Micromodel experiment
Yan et al. 2025

## Slide 8
2D case studies
Case 1
Case 2
Case 3
8
Fluid distribution across each scenario over time
Case 1 Γ = 7.5 × 10⁻⁷
Capillarity dominates. Coarse drains first; fine retains water → non-linear front.
Case 2 Γ = 2.5 × 10⁻⁵
Evaporation dominates. Uniform front recession; linear saturation curve.
Case 3 Δr_p = 0 (Γ → ∞)
Homogeneous medium. No capillary gradient; front controlled by J alone.

## Slide 9
2D case studies
9
CO₂–water distribution in 2D simulations at four water saturations, with corresponding time intervals and the overall saturation evolution during drying.
Case 1 Γ = 7.5 × 10⁻⁷
Capillarity dominates. Coarse drains first; fine retains water → non-linear front.
Case 2 Γ = 2.5 × 10⁻⁵
Evaporation dominates. Uniform front recession; linear saturation curve.
Case 3 Δr_p = 0 (Γ → ∞)
Homogeneous medium. No capillary gradient; front controlled by J alone.

## Slide 10
3D case studies
Case 4 (Slow)
Case 5 (fast)
Fluid distribution across each scenario over time
10
Temporal evolution of water saturation across the entire domain.
Why 3D matters
Corner flow and thin films sustain water connectivity through narrow throats that don't exist in 2D. 3D = stronger capillary pumping than 2D for the same pore-size heterogeneity. Implication: 2D models systematically underestimate salt-precipitation risk in CCS.

## Slide 11
3D case studies
Snapshots of fluid distribution at different saturation levels and time intervals during the drying process in the 3D simulations
11
Distribution of the spatially averaged difference between saturation-matched frames.

## Slide 12
Historical heat map of water velocity magnitude for 2D case studies.
Statistical distribution of water velocity magnitude at three saturations for Cases 1-3.
Water redistribution
Capillary head vs Sw · Skjæveland fits

## Slide 13
Developed an advanced Lattice Boltzmann (LB) model:
  Handles extreme density and viscosity contrasts with sharp interfaces.
  Validated against analytical model for interconnected capillary tubes.
Introduced a dimensionless parameter (Γ) to quantify evaporation vs. capillary-driven flow.
Drying interface morphology strongly influenced by the interplay of evaporation rate and capillary pressure gradients:
  High evaporation flux: stable, linear drying front.
  High capillary gradient: uneven, nonlinear drying front with notable water redistribution.
Pore size heterogeneity critically affects water redistribution:
  Prolonged liquid retention in finer pores, potentially increasing localized salt precipitation.
3D vs. 2D simulations:
  Increased connectivity of water phase in 3D significantly enhances capillary effects, emphasizing importance of corner flow.
Conclusions and key insights

## Slide 14: THANK YOU