## Slide 1
Pore-scale CFD simulations to investigate transport phenomena in packed-bed reactors
D. Fida, M. Icardi, G. Pipitone, A. Buffo, G. Boccardo,
D. Marchisio, S. Bensaid

## Slide 2
1
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Results | Conclusion
Introduction to
Aqueous
Phase Reforming
Industrial APR Aim:
produce renewable Hydrogen from industrial wastewater
cat
APR Reactor
Pt over activated carbon
Zoppi G. et al. Catal. Today 2022

## Slide 3
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Results | Conclusion
Goals & Challenges
9 mm
1.40 mm
Goals for CFD:
Analyse unwanted fluid dynamic behavior influence
Study the complex geometry influence
Geometry optimization
21 mm
Challenges:
Irregular pellet shape
Side-reactions consume the products
Multiphase system
2

## Slide 4
3D
Digital reactor
Geometry Reconstruction
2D image
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Results | Conclusion
3

## Slide 5
Mean Age Theory
Liu M., Tilton J.N., AIChE J. 2010
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Results | Conclusion
Mean Age is the average time that the fluid spends in the system before crossing a specific location.
4

## Slide 6
Delay
5.4%
0.3%
Stagnant zones
By-pass
paths
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Results | Conclusion
5

## Slide 7
Chart: Carbon Selectivity
| 0 | 0.75 | 1.5 | 3 | 18
Acetol | 0.0462 | 0.025136 | 0.021908 | 0.028229 | 0.027735
Ethylene glycol | 0.02918 | 0.027835 | 0.034264 | 0.035301 | 0.039963
1-Propanol | 0 | 0.0054594 | 0.014163 | 0.030561 | 0.14386
MeOH | 0 | 0 | 0.013406 | 0.015222 | 0.040724
CH4 | 0.018761 | 0.020395 | 0.021247 | 0.020253 | 0.017129
C2H6 | 0 | 0.0077516 | 0.0093925 | 0.013121 | 0.032916
EtOH | 0 | 0.019839 | 0.032198 | 0.038611 | 0.044972
Propilen glycol | 0.49263 | 0.39151 | 0.47232 | 0.45725 | 0.25619
CO2 | 0.16221 | 0.15498 | 0.13388 | 0.12604 | 0.14607
Operating condition:
Pt/C
5% glycerol
240°C
Kinetic model
from
experimental data
(1)
(2)
Range of campaign:
Pt/C
5% - 15% glycerol
240°C - 270 °C
0h-3h
Shabaker J.W. et al., J. Catal. 2003
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Results | Conclusion
6

## Slide 8
Kinetic model
results
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Results | Conclusion
5% Glyc. 270°C
5% Glyc. 240°C
Highlight:
Nonlinear kinetics
Hydrogen is consumed by the secondary reaction
7

## Slide 9
Reactive transport
in
Reactions implemented as a Boundary Condition
A
C
B
Reactions implemented as a volumetric source
A
C
B
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Results | Conclusion
8

## Slide 10
Method comparison
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Results | Conclusion
9

## Slide 11
Method comparison
Inside the catalyst the diffusion transport changes the interplay between transport and reaction
A
C
B
Catalyst effectiveness
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Results | Conclusion
10

## Slide 12
Results
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Results | Conclusion
11

## Slide 13
Glycerol concentration
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Results | Conclusion
12

## Slide 14
Hydrogen concentration
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Results | Conclusion
13

## Slide 15: Conclusion
Kinetic model:
Build a kinetic model based on experimental data and adapt it to the CFD models
Non-reactive flow:
Upscaling parameters estimation
Abnormal residence time zones identification
Multiphase model:
Under development: an easy and general reactive mixture transport model
Reactive transport:
Two models are developed
A
C
B
Volumetric source model can consider internal diffusion
Boundary condition model is faster and more stable
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Results | Conclusion
14

## Slide 16
Thank you for your kind attention!
Diego’s contact:
diego.fida@polito.it

## Slide 17
Supplementary

## Slide 18
Mean Age Theory
Mean Age is the average time that the fluid spends in the system before crossing a specific location.
Liu M., Tilton J.N., AIChE J. 2010
6/28
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Multiphase | Conclusion

## Slide 19
Mean Age for Upscaling
Advection-Dispersion
6/24
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Multiphase | Conclusion

## Slide 20
Catalyst effectiveness
We can calculate the catalyst effectiveness for arbitrary shape and kinetics
In literature, mathematical correlations exist but:
simplified shapes
limiting chemical species
simple chemical kinetics
Meenakshi Sundaram K. M., Chem. Eng. Commun., 1982
Aris R., Oxford University Press, 1975
Roberts G.W., Satterfield C.N., Chemical Kinetics and Chain Reactions, Clarendon Press, 1954
Aris R., Chem. Eng. Sci. 6 (1957)
13/24
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Multiphase | Conclusion
Chart: conversion %
| 5.405405405405405E-2 | 0.54054054054054046 | 5.4054054054054053 | 54.054054054054042 | 540.54054054054052 | 5405.405405405405 | 54054.054054054046 | 540540.54054054047
Vol method | 0.0812 | 0.080892 | 0.076845 | 0.054664 | 0.025268 | 0.01009 | 0.0050432 | 0.0038509
BC method | 0.080848 | 0.080848 | 0.080848 | 0.080848 | 0.080848 | 0.080848 | 0.080848 | 0.080848 | 0.080848
Chart: Effectiveness
| 5.405405405405405E-2 | 0.54054054054054046 | 5.4054054054054053 | 54.054054054054042 | 540.54054054054052 | 5405.405405405405 | 54054.054054054046 | 540540.54054054047
CFD | 1.0044 | 1.0006 | 0.9505 | 0.67613 | 0.31254 | 0.1248 | 0.062379 | 0.047631
Numerical solution | 0.9995 | 0.99502 | 0.95278 | 0.68652 | 0.25785 | 0.081609 | 0.025807 | 0.0081609

## Slide 21
Open challege
We can calculate the catalyst effectiveness for arbitrary shape and kinetics
Chart: conversion %
| 5.405405405405405E-2 | 0.54054054054054046 | 5.4054054054054053 | 54.054054054054042 | 540.54054054054052 | 5405.405405405405 | 54054.054054054046 | 540540.54054054047
Vol method | 0.0812 | 0.080892 | 0.076845 | 0.054664 | 0.025268 | 0.01009 | 0.0050432 | 0.0038509
BC method | 0.080848 | 0.080848 | 0.080848 | 0.080848 | 0.080848 | 0.080848 | 0.080848 | 0.080848 | 0.080848
Chart: Relative computational time t_vol/t_BC
| 5.405405405405405E-2 | 0.54054054054054046 | 5.4054054054054053 | 54.054054054054042 | 540.54054054054052 | 5405.405405405405 | 54054.054054054053 | 540540.54054054047
 | 186.1427 | 31.9617 | 4.6459 | 1.3957 | 0.55832 | 0.78182 | 0.62546 | 1.032
The computational time rise when the diffusion is the relevant phenomena
// * * * * * * * * * * * * * fvSchemes* * * * * * * * * * * * //
laplacianSchemes
{
default Gauss linear corrected
}
14/24
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Multiphase | Conclusion

## Slide 22
Multiphase

## Slide 23
Multiphase Reactive Mixture Model
Solid fraction
Liquid fraction
Gas fraction
Flow field resolution
𝜕(ρ_𝑚 𝐮_𝑚 )/𝜕t+∇⋅(ρ_𝑚 𝐮_𝑚⊗𝐮_𝑚 )=∇⋅σ_𝑚−∇⋅𝜏+𝜑_𝑚 𝜌_𝑚 𝒈−f_(𝑠,𝑚)
Calculate slip velocity
𝐮_ℓ=φ_ℓ (𝐮_𝑚+φ_g ρ_g κ_gℓ/μ_𝑚 𝒈)
Species transport
𝐮_g=φ_g (𝐮_𝑚−φ_ℓ ρ_ℓ κ_gℓ/μ_𝑚 𝒈)
Flow field resolution
Calculate slip velocity
Species transport
18/24
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Multiphase | Conclusion

## Slide 24
Momentum conservation
Summation
19/24
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Multiphase | Conclusion

## Slide 25
Slip velocity
Constraints:
Where is a function that must take in account the extra forces between the phases
We assume that is the gravity acceleration
20/24
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Multiphase | Conclusion

## Slide 26
Liquid & Gas governing equations
: Reactions rate
: Condensation-Evaporation term
: Nucleation term
21/24
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Multiphase | Conclusion

## Slide 27
Update fluid state properties
22/24
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Multiphase | Conclusion

## Slide 28
Other

## Slide 29
3/28
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Multiphase | Conclusion
Analysis of Experimental Data
Morphological & Dimensional characterization
Geometry reconstruction

## Slide 30
SET-UP & FRAGMENTS GENERATION
COMPARISON WITH EXPERIMENTAL DATA
PACKING SIMULATION
by RIGID-BODIES SIMULATION
OPTIMUM CHOICE
NOISE
Geometric Reconstruction
Frequence
Circularity
Equivalent diameter, mm
Frequence
3D (Digital)
2D (Real)
3D (Digital)
2D (Real)
BEST FITTING
NUMBER OF FRAGMENTS
4/28
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Multiphase | Conclusion
×3000 sets of (noise, num. fragment)

## Slide 31
Open challenge
2D image
5/28
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Multiphase | Conclusion
There may be better parameters to describe the pellets
3D
Digital reactor

## Slide 32
Delay
9/28
Introduction | Non-reactive flow | Eperimental kinetic model | Reactive transport | Multiphase | Conclusion

## Slide 33
Different geometry
 | Porosity
Fragment | 0.415
Cylinder | 0.394
Sphere | 0.439
Trilobe | 0.411
8/28
Introduction | Non-reactive flow | Eperimental kinetic model | Reactive transport | Multiphase | Conclusion

## Slide 34
Experimental test
Global optimization
Local optimization
Arrhenius plot
Workflow
12/28
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Multiphase | Conclusion

## Slide 35
Kinetic model
results
5% Glyc. 240°C
15% Glyc. 240°C
10% Glyc. 240°C
--- Glycerol
--- Hydrogen
--- Carbon dioxide
--- Propylene Glicol
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Multiphase | Conclusion
13/28

## Slide 36
Kinetic model
results
5% Glyc. 240°C
5% Glyc. 260°C
5% Glyc. 250°C
--- Glycerol
--- Hydrogen
--- Carbon dioxide
--- Propylene Glicol
Introduction | Non-reactive flow | Experimental kinetic model | Reactive transport | Multiphase | Conclusion
5% Glyc. 270°C
14/28

## Slide 37
Kinetic model
definition
assumed negligible due to low conc. at the end of experiment
Present in very low amount
experimentally proven
Shabaker J.W. et al., J. Catal. 2003

## Slide 38
Kinetic model
definition

## Slide 39
Reactions: boundary condition
First order Taylor expasion
Robin boundary condition

## Slide 40
Reactions: volumetric source