## Slide 1
Quantifying Mass Transfer Between Partially-Soluble Fluids in Multiphase Systems
Anna L. Herring1, Christopher Allison1, Joe-Sam Nkuah1
1Civil and Environmental Engineering; University of Tennessee, Knoxville
2University of Sydney
Presented to Interpore 2026

## Slide 2: Goals:
Transport of Partially-Soluble Fluids
CO2, H2, NAPLs….
Many multiphase imaging experiments are conducted with fluids pre-mixed to ensure mutual solubility and immiscible displacements
  better imaging quality
In the field, observe significant mass transfer between liquid/gas/supercritical phase and water (both dissolution and evaporation)
Subsequent movement by advection, diffusion, density-driven convection
How to quantify transport in both “pure” phase and in aqueous phase?
Interpore 2026

## Slide 3: Two approaches we are pursuing
X-ray μCT Studies
  Colorimetric Methods

## Slide 4: X-ray μCT
Key positive aspects
3D
Compatible with reservoir conditions
Opaque Samples
Key drawbacks
Most solutes of interest do not produce X-ray contrast
Aqueous concentration must be inferred

## Slide 5: Calculating Mass Transfer Coefficient and Aqueous Concentration from X-ray μCT Data
Key Assumption- What is aqueous phase concentration C?
Measure directly from image sequences
Assume constant or estimate
m = mass
ρ = density
V = volume
t = time
k = mass transfer coefficient
A = interfacial area
Csol = aqueous concentration at the solubility limit
C = aqueous concentration

## Slide 6: Quantifying the Effect of Assumptions
Allison et al. Quantifying Injection-Driven Mass Transfer within Porous Media via Time-Elapsed X-ray micro-Computed Tomography. under review
arXiv:2604.07743 [physics.flu-dyn]
Key Assumption- What is aqueous phase concentration C?
Huang et al. (2023) identify clusters where safe to assume C=0; calculate k based on those clusters only
Patmonoaji et al. (2017, 2021, 2023) Apply a 1D Advection-Dispersion model to estimate concentration as function of length along core

## Slide 7: Quantifying the Effect of Assumptions
kMT
three approaches investigated produce similar results
Aqueous Concentration Values
- Wide range depending on approach
- Cluster-based provides localized, physically relevant values
- Estimates!
Normalized H2(aq) Concentration [-]
Allison et al. “Quantifying Injection-Driven Mass Transfer within Porous Media via Time-Elapsed X-ray micro-Computed Tomography.” under review arXiv:2604.07743 [physics.flu-dyn]

## Slide 8: Surprising impact of cluster remobilization
Multiple systems evidence cluster mobilization during flow
  Huang et al., Investigation of Supercritical CO2 Mass Transfer in Porous Media Using X-Ray Micro-Computed Tomography, Adv. Water Resour. 171, 104338 (2023).
  Lv et al., CO2-Brine Mass Transfer Patterns and Interface Dynamics under Geological Storage Conditions, Int. J. Heat Mass Transf. 222, (2024).
  Now: Patmonoaji et al., Dissolution Mass Transfer of Trapped Gases in Porous Media: A Correlation of Sherwood, Reynolds, and Schmidt Numbers, Int. J. Heat Mass Transf. 205, 123860 (2023).
  Mobilization can bias estimates of
  Mass Transfer
Allison et al. “Quantifying Injection-Driven Mass Transfer within Porous Media via Time-Elapsed X-ray micro-Computed Tomography.” under review arXiv:2604.07743 [physics.flu-dyn]

## Slide 9: Surprising impact of cluster remobilization
Excludes Data with Mobilization
Includes Data with Mobilization
Includes Data with Mobilization
Positive mass transfer at bottom balanced by negative mass transfer at top – mathematically works out (in this case)
Allison et al. “Quantifying Injection-Driven Mass Transfer within Porous Media via Time-Elapsed X-ray micro-Computed Tomography.” under review arXiv:2604.07743 [physics.flu-dyn]

## Slide 10: Aqueous concentration estimates do not agree
Allison et al. “Quantifying Injection-Driven Mass Transfer within Porous Media via Time-Elapsed X-ray micro-Computed Tomography.” under review arXiv:2604.07743 [physics.flu-dyn]
Huang et al. (2023) Concentrations directly adjacent to gas bubbles
Patmonoaji et al.
(2017, 2021, 2023)
1D Advection-Dispersion
Cross sectional average

## Slide 11: Colorimetric Quantification
Key positive aspects
Accessible
“Direct” measurement of concentration
Key drawbacks
2D or quasi-2D
Color is a vector rather than a scalar – quantification is tricky
Nkuah et al. “Spatial Colorimetric Mapping of pH and Dissolved Carbon during Convective Dissolution of CO₂: Constraints from Domain, Geometry, and Indicator Mix on Measurement Reliability”. In prep.

## Slide 12: Choice of quantification scheme can impact results Errors propagate to concentration estimates
Nkuah et al. “Spatial Colorimetric Mapping of pH and Dissolved Carbon during Convective Dissolution of CO₂: Constraints from Domain, Geometry, and Indicator Mix on Measurement Reliability”. In prep.

## Slide 13: Conclusions
X-ray µCT provides relatively robust estimates of mass transfer coefficient k in 3D
  Regardless of quantitative approach
  Ganglia / bubble remobilization impacts statistics- interpret with care
Aqueous concentrations still a challenge
  Other methods – colorimetric – promising
    Require precise calibration + quantification
This material is based upon work supported by the U.S. Department of Energy, Office of Science, Office of Basic Energy Sciences, Geosciences program under Award Number DE-SC0025400.
Allison et al. “Quantifying Injection-Driven Mass Transfer within Porous Media via Time-Elapsed X-ray micro-Computed Tomography.” under review arXiv:2604.07743 [physics.flu-dyn]
How is CO2 invasion into heterogeneities affected by partial solubility?
R. Huang, A. Herring, M. Saadatfar, and A. Sheppard, Impact of Heterogeneity and Miscibility on ScCO2 Drainage Flow Patterns and Implications for Experimental Interpretation, Water Resour. Res. 61, (2025).
Thank You!

## Slide 14: Colorimetric Quantification
Different Color Quantification Schemes
Y. Xu, M. Moura, E. G. Flekkøy, and K. J. Måløy, Advances in Water Resources A Comparison of Different Image Analysis Techniques for Mapping Spatiotemporal PH and Carbon Dissolution in Density-Driven Convection of CO2 in Water, Adv. Water Resour. 212, 105296 (2026).
Notes: [1]