## Slide 1
May 13, 2026
Decoupling the Non-linear Influence of Pore Structure on CO2 Saturation:
An Explainable Data-Driven Approach based on Microfluidic Experiments
Han Ge,
Associate Professor,
Ocean College, Zhejiang University

## Slide 2
01.点击加入标题
Background & Limitations
Background
CO2 transport is influenced not only by pore structure, but also by fluid properties and flow conditions
Multiple parameters may interact with each other, leading to complex effects on CO2 behavior
Existing studies mainly focus on individual parameters, lacking a unified framework
Challenges & limitations
CO2
Micro-mechanism:
Microfluidic experiment
*Image source: https://www.thorntontomasetti.com/project/carbon-capture-storage
Macro-scale: Gigaton-scale offshore CO2 storage*
Flow patterns, trapping behavior, storage efficiency and security are controlled by pore structures
Geological CO2 sequestration is a key pathway for long-term carbon mitigation
Simulation
Micro-scale: Capillary capture

## Slide 3
1
Microfluidic experiments platform
2
Multi-parameters experiment
Geometry heterogeneity:
porosity, pore size probability density function (PDF)
Topology properties:
pore-throat ratio, coordination number
Fluid properties:
viscosity, surface tension
3
4
Interpretable analysis
01.点击加入标题
Technical Route
Machine learning model
Multi-modal feature fusion (data + image)
Initial & residual saturation perdition (Si & Sr)
Dataset
Feature importance analysis (SHAP)
Identify main control parameters & influence
Displacement-imbibition process
Microscopic imaging & saturation characterization
Notes: About data pre-processing, exp_type, one hot encoding
Other parameters, to exclude the influence of the unit, use Max-min normalization

## Slide 4
01.点击加入标题
Experiment 1: General Heterogeneity Variation
A1
A2
B2
φ=0.3926
φ=0.5403
Same porosity
Similar pore size distribution
pore size
PDF
A narrow pore size distribution with a sharp peak
A broader pore size distribution dominated by small pores
Binarized
Pore
Area
equivalent
circle
pore size
PDF

## Slide 5
01.点击加入标题
Experiment 2: Topology Variation
dcir
wrec1
wrec2
wrec3
wrec4
Coordination number (Nc )=4
(rec1, rec2, rec3,rec4)
Pore-throat ratio (Rp/t )=
avg (dcir/wrec)
N0R0
N0RH
NHRH
NHR0
Rp/t↑
Nc↑
Rp/t↑
Nc↑
Nc↑
Rp/t↑
Model | Coordination Number (Nc) | Pore-Throat Ratio (Rp/t)
N0R0 | 2.25 | 1.78
N0RH | 2.25 | 2.51 (↑)
NHR0 | 2.75 (↑) | 1.78
NHRH | 2.75 (↑) | 2.51 (↑)

## Slide 6
01.点击加入标题
Machine Learning
Input
Image inputs
Registered image
Binary pathways
Binary CO2 distribution
Data inputs
Structural parameters
Fluid properties Experimental conditions
CNN
Feature concatenation
Feature extraction
Multi-task learning framework
Predict initial saturation Si
Logical mask (masking imbibition parameters Qre, Sr)
Predict residual saturation Sr
Prediction result
(High Accuracy & Stability)
Conv2D,3×3, 16
MaxPooling
Conv2D,3×3, 32
MaxPooling
Conv2D,3×3, 32
Global
Average Pooling
243×486×3
Notes: The register image to reflect the distribution of co2 and water in the pathways, including the interface between them.
The binary pathways to reflect the boundary conditions of the porous skeletons
The binary co2 distribution to reflect the distribution of CO2
All of the image data provide the spatial information by pixels to make complementary of the structured data, which can’t reflect the distribution differences.
The feature concatenation can couple all these information in different aspects and scales.
The displacement process, actually, Qre(re-imbibition flow rate) and Sr is unknow. To avoid leaking these information to the prediction of Si, here we add the logical mask.
We use multi-task learning framework to do this prediction to discover the potential relations between Si and Sr
The 5-fold cross-validation: we divided all the data to five groups( randomly?), and for each training round, select four groups in turn as the training set, and the other one as the validation set. Thus, we do 5-round training and validating. Using the 5-round coefficient of determination and standard deviation as the generalization target. Moreover, during the division of the data, we use make_key function to construct the ID of each group, i.e., use the structure parameters, fluid properties, experimental condition and the repeated rounds to seal to this ID, make sure the experimental results (displacement and reimbibition ) with the same experimental conditions to be split as a group into the training set or validation set. In this way, we can avoid information leaking and the accuracy oscillation due to the unbalance between the displacement data and reimbibiton data.

## Slide 7
01.点击加入标题
Optimization strategy
Prediction result
(High Accuracy & Stability)
Dataset splitting: 5-Fold cross-validation
Avoid data leakage
Increase the generalization of the model
Dataset
Group-based split
(Group ID: Structure + Fluid + Flow Rate + Repeated rounds)
Fold 1
Fold 2
Fold 3
Fold 4
Fold 5
Iteration 1: Test = Fold 1 (20%) Train/Validation = Fold 2-5 (80%)
└─ Train: 72%; Validation: 8%
Iteration 2: Test = Fold 2 Train/Validation = Fold 1, 3-5
…
Iteration 5
Training strategy: Bayesian optimization
Hyperparameters (Learning rate, Dropout, Weight decay)
R2 evaluation
Target = mean(R2)-1.5×std(R2)
Optuna
update
Notes: The displacement process, actually, Qre(re-imbibition flow rate) and Sr is unknow. To avoid leaking these information to the prediction of Si, here we add the logical mask.
We use multi-task learning framework to do this prediction to discover the potential relations between Si and Sr
The 5-fold cross-validation: we divided all the data to five groups( randomly?), and for each training round, select four groups in turn as the training set, and the other one as the validation set. Thus, we do 5-round training and validating. Using the 5-round coefficient of determination and standard deviation as the generalization target. Moreover, during the division of the data, we use make_key function to construct the ID of each group, i.e., use the structure parameters, fluid properties, experimental condition and the repeated rounds to seal to this ID, make sure the experimental results (displacement and reimbibition ) with the same experimental conditions to be split as a group into the training set or validation set. In this way, we can avoid information leaking and the accuracy oscillation due to the unbalance between the displacement data and reimbibiton data.

## Slide 8
01.点击加入标题
Machine Learning
Optimization result
(high accuracy & stability)
R2 | fold1 | fold2 | fold3 | fold4 | fold5 | Average ± std
Si | 0.930 | 0.935 | 0.917 | 0.951 | 0.933 | 0.933 ± 0.0109
Sr | 0.876 | 0.921 | 0.722 | 0.931 | 0.908 | 0.872 ± 0.0771
Optimization target = mean(R2)-1.5×std(R2)
(accuracy & robustness)
Before optimization
Optimal learning rate, dropout rate and weight decay
R2 | fold1 | fold2 | fold3 | fold4 | fold5 | Average ± std
Si | 0.978 | 0.918 | 0.968 | 0.968 | 0.945 | 0.955 ± 0.0216
Sr | 0.953 | 0.946 | 0.954 | 0.941 | 0.975 | 0.954 ± 0.0116
After Optimization
Bayesian optimization

## Slide 9
01.点击加入标题
Interpretable Analysis by SHAP
Symmetry: If two features contribute identically to all possible subsets, their Shapley values are equal.
Dummy: A feature that does not change the prediction in any context receives a Shapley value of zero.
SHAP (SHapley Additive exPlanations) refers to an explanation model that uses an additive model to represent the relationship between input features and their coefficients, providing importance values to each feature based on their effect on the model prediction[1].
Huang, X., Kroening, D., Ruan, W., Sharp, J., Sun, Y., Thamo, E., Wu, M. and Yi, X., 2020. A survey of safety and trustworthiness of deep neural networks: Verification, testing, adversarial attack and defence, and interpretability. Computer Science Review, 37, p.100270.
Lundberg, S.M. and Lee, S.I., 2017. A unified approach to interpreting model predictions. Advances in neural information processing systems, 30.
Notes: The model is a black box, so we use SHAP (SHapley Additive exPlanations)
SHAP (SHapley Additive exPlanations) is a unified, game-theoretic framework used to interpret the predictions of complex machine learning models (often treated as "black boxes").
It frames feature attribution as a cooperative game where input features act as "players" collaborating to produce a prediction output.
SHAP calculates the exact marginal contribution of each feature, ensuring a theoretically sound distribution of credit.

## Slide 10
01.点击加入标题
Interpretable Analysis by SHAP
exp_type_imb
exp_type_disp
interfacial_tension
fluid_SW
porosity
viscosity
fluid_DI
pore_throat_ratio
PDF_strength
PDF_peak_density
PDF_peak_radius
Nc_Rp/t
coordination_number
Qi
Si
Qre
Feature value
High
Low
fluid properties structural parameters experiment conditions coupling terms
High
Low
coordination_number
exp_type_imb
exp_type_disp
interfacial_tension
fluid_SW
porosity
viscosity
fluid_DI
pore_throat_ratio
PDF_strength
PDF_peak_density
PDF_peak_radius
Nc_Rp/t
Qi
SHAP value (impact on model output)
Si
Sr
positive
negative
positive
negative
Feature value
SHAP value
Beeswarm Plot: Summarizes feature importance, showing how higher/lower values impact the prediction.
Notes: Positive value means the increase of this feature will increase the output, while negative value means it will lower the output

## Slide 11
01.点击加入标题
Interpretable Analysis by SHAP
fluid properties structural parameters experiment conditions coupling terms
Fluid properties ＞ Structural parameters ＞ Injection rate (Qi, Qre).
Coupling terms occupy a moderate position in importance ranking.
Within the experimental regime of this study, fluid properties primarily govern the overall flow pattern, while pore structure further modulates CO2 distribution and residual behavior through local geometric constraints, with injection rate providing local corrections within this framework.
High
Low
coordination_number
interfacial_tension
porosity
viscosity
pore_throat_ratio
PDF_strength
PDF_peak_density
PDF_peak_radius
Nc_Rp/t
Qi
Feature value
Si
positive
negative
interfacial_tension
pore_throat_ratio
PDF_strength
PDF_peak_radius
Nc_Rp/t
Si
Feature value
High
Low
Sr
porosity
viscosity
coordination_number
Qre
Qi
PDF_peak_density
positive
negative
Notes: If the red dot located in the Positive half, it means the increase of this feature will increase the output, while negative half means it will lower the output

## Slide 12
01.点击加入标题
Interpretable Analysis by SHAP
Porosity ↑ → earlier breakthrough → Si ↓
Topological parameters > General heterogeneity parameters
Heterogeneity: more homogenous & larger pores → Si ↑;
Tropology:
  Nc↑ → Si ↓ , Rp/t ↑ → Si ↑ ,
  Nc _Rp/t ↑ → Si ↓
N0R0
NHR0
N0RH
NHRH
Experimental Results
SHAP value
coordination_number
porosity
pore_throat_ratio
PDF_strength
PDF_peak_density
PDF_peak_radius
Nc_Rp/t
Qi
Si
High
Low
positive
negative
Notes: Positive value means the increase of this feature will increase the output, while negative value means it will lower the output

## Slide 13
01.点击加入标题
Mechanism Analysis
Heterogeneous structure
Si ↓
Pronounced fingering during displacement, with bypass areas (framed) formed due to high resistance in small pores
Increasing injection rate
1-1
A1
A2
1-2
B2
MA2-1
MA2-2
KA2-1
KA2-2
MB2-1
MB2-2
KB2-2
KB2-1
KB2-3
KB2-4
Capillary-Connectivity balance
⟹ Flow pattern & Sweet spot (CF-transition turning spot)
Chen, X., Ge, H.*, Chen, J., & Wang, C. (2026). Pore-Network Topology Impact on CO2 Sequestration via Capillary-Connectivity Mechanism. Energy & Fuels, 40, 668-674.
Chen, X., Ge, H.*, Chen, J., & Wang, C. (2025). Impact of Pore Heterogeneity on CO2 Capture Efficiency in Porous Media. Chemical Engineering Research and Design, 215, 77-82.

## Slide 14
01.点击加入标题
Interpretable Analysis by SHAP
Si is much more important: Si ↑ → Sr ↑
Topological parameters > General heterogeneity parameters
Heterogeneity
  small pores enhance trapping, larger pores provide trapping space.
Tropology:
  Nc↑ → Sr ↓ , Rp/t ↑ → Sr ↑
  Nc _Rp/t ↑ → Sr ↓/ ↑
Sr
pore_throat_ratio
PDF_strength
PDF_peak_radius
Nc_Rp/t
Si
SHAP value
High
Low
porosity
coordination_number
Qre
Qi
PDF_peak_density
positive
negative
N0R0
NHR0
N0RH
NHRH
Experimental Results
Notes: Positive value means the increase of this feature will increase the output, while negative value means it will lower the output

## Slide 15
01.点击加入标题
Conclusion
Interpretable AI for Micro-Mechanics
Experimental & Predictive Alignment
  The framework demonstrated robust qualitative agreement with microfluidic visual proofs, accurately capturing complex displacement boundaries.
Opening the Black Box via SHAP
  By integrating SHAP analysis, we successfully achieved a rigorous unification of high-precision saturation prediction and interpretable mechanistic analysis.
Decoupling Non-Linear Complexity:
  SHAP dependence models successfully isolated and quantified the highly non-linear weights of individual topological parameters (e.g., coordination number, pore-throat ratio) driving capillary snap-off.
Notes: To conclude, our work builds a rigorous bridge between physical micro-mechanisms and data-driven scalability.
As you can see from the SHAP analysis on the screen, our predictive models do not just output numbers—they align perfectly with our experimental visual proofs. More importantly, by utilizing SHAP, we have successfully opened the 'black box' of neural networks, achieving a true unification of high-precision prediction and interpretable mechanistic analysis. This proves that explainable AI is an essential key to decoupling highly complicated, non-linear multiphase flow dynamics driven by pore topology.

## Slide 16
Our Core Capabilities :
Multiphase Flow & Cavitation: Deep expertise in acoustic cavitation dynamics and physical blockage removal in porous media.
High-Fidelity Visualization: Customized microfluidic platforms capturing transient, pore-scale displacement mechanisms.
Explainable AI (XAI): Integrating experimental physics with machine learning (PIML) to decode non-linear flow complexity.
IMPACT Group @ Zhejiang University
Intelligent Multiphase Porous media & Acoustic Cavitation Transport
Han Ge (PI)| ✉ gehan@zju.edu.cn
Notes: Before I conclude, I want to take a brief moment to introduce myself and share what my group at Zhejiang University can bring to the table.
My name is Han Ge, and my research fundamentally focuses on acoustic cavitation, multiphase flow visualization, and integrating explainable AI into porous media. We have built highly cost-effective, high-precision microfluidic pipelines that generate rich, structured datasets—which are exactly what large-scale AI models and simulators need for ground-truth validation.
Currently, we are actively expanding our international footprint and looking for funding synergies. If you are building a consortium for major collaborative grants, or if your macroscopic simulators need robust pore-scale physical constraints for CCUS and EOR applications, let's partner. We bring the high-fidelity experimental proof and the explainable AI engines; we are looking for the macro-scale validation and joint proposal opportunities.
Please catch me during the coffee break. I would be absolutely honored to discuss how we can build high-impact projects together. Thank you!"

## Slide 17
Thank you for your attention
13 May 2026
Questions?