## Slide 1: Residual-Based Physical Informed Neural Network Modelling for Coupled Transport Phenomena in Porous Gas Diffusion Layers
Hui Zhang, Dr.Bo Li, EEMG, 16/05/2026

## Slide 2
INTRODUCTION
METHODOLOGY
RESULTS
CONCLUSIONS
INTRODUCTION
Decarbonization has become a priority for nations worldwide.
3% of global CO2 emissions and 12% of transport emissions [1]
High-Temperature Proton Exchange Membrane Fuel Cells (HT-PEMFCs)
Reactant transport, water management, pressure distribution, electron conduction [2-4]
Fig.1 ZeroAvia Hydrogen-electric regional aircraft​
Fig.2 Gas diffusion layer (GDL) structure
Experiments cannot fully capture in-situ multi-physics behaviour. [5]
CFD is accurate but too computationally expensive.
AI models struggle with generalization, physics consistency, and convergence. [6, 7]
How to rapidly predict coupled physical fields inside the GDL while maintaining physical consistency and convergency efficiency?
Notes: Aviation today contributes around 3% of global CO₂ and 12% of transport emissions, and without intervention these could triple by 2050. PEMFCs are one of the most credible candidates to decarbonise this sector — and inside a PEMFC, the gas diffusion layer is the component that governs how reactants, water, electrons, and pressure are distributed across the cell.
快，但不物理"与"物理，但不快

## Slide 3
INTRODUCTION
METHODOLOGY
RESULTS
CONCLUSIONS
INTRODUCTION
Fig.3 Structural comparison of black-box model (BBM), pure physics-informed neural network model (PPM) and residual-based physics-informed neural network model (RPM)
Research Objectives:
Develop a fast, accurate, and generalizable multi-physics prediction model for the PEMFC hydrogen-side GDL.
Compare RPM with PPM and BBM in accuracy, generalization, and efficiency.
Innovations：
Residual connections improve PINN convergence under multi-physics coupling.
Learnable scaling coefficient α stabilizes training.
Coupled output architecture explicitly encodes pressure–concentration physics.

## Slide 4
INTRODUCTION
METHODOLOGY
RESULTS
CONCLUSIONS
METHODOLOGY
Fig.4 CFD Geometry and computational domain for the hydrogen-side GDL
COMSOL Application Gallery Case 38 (“Species Transport in the Gas Diffusion Layers of a PEM”).
Geometry dimensions:
AB = EF = 0.5 mm CD = 1 mm GH = 2 mm AH = FG = 0.35 mm BC = DE = 0.1 mm
Boundary conditions:
AB & EF: gas inlets (specified mole fraction and pressure)
CD: reference potential boundary (V = 0)
GH: GDL–catalyst layer interface
This model couples charge, mass, and momentum transport in the PEMFC：
( )
The dataset includes 700 steady-state operating conditions, with set between 0.500–0.950 V , between 101825–106775 Pa, between 0.500 and 0.800.
Notes: The geometry of the reference case is shown in Figure 1, where the blue region represents the hydrogen-side GDL domain considered in this study.

## Slide 5
INTRODUCTION
METHODOLOGY
RESULTS
CONCLUSIONS
METHODOLOGY
Black-Box Model (BBM): A purely data-driven model without physical constraints.
Pure Physics-Informed Neural Network Model (PPM): A PINN model embedding governing physics into training.
Residual-based Physics-Informed Neural Network Model (RPM): A residual-enhanced PINN with improved convergence and stability.
()
()
Loss Function：
BBM
PPM
RPM
Introduce the residual structure based on the PPM loss

## Slide 6
INTRODUCTION
METHODOLOGY
RESULTS
CONCLUSIONS
METHODOLOGY
Fig.5 Detail training workflow for residual-based physics-informed neural network model (RPM)

## Slide 7
INTRODUCTION
METHODOLOGY
RESULTS
CONCLUSIONS
RESULTS
Six operating conditions were selected for validation, comprising three interpolated conditions within the training domain and three extrapolated conditions beyond it, see Table 1.
Conditions | Parameters [Vcell, pa,in,xH2,in]
1 | [0.525, 104000, 0.650]
2 | [0.575, 104250, 0.675]
3 | [0.625, 105250, 0.725]
4 | [0.400, 104000, 0.800]
5 | [0.500, 107000, 0.600]
6 | [0.480, 107200, 0.870]
Table 1 New test combinations for model performance analysis

## Slide 8
INTRODUCTION
METHODOLOGY
RESULTS
CONCLUSIONS
RESULTS
1
2
3
4
5
6
Fig.6 Predicted spatial distributions of physical fields under six conditions

## Slide 9
INTRODUCTION
METHODOLOGY
RESULTS
CONCLUSIONS
RESULTS
1
6
Figure 7 Comparison of predicted profiles along selected cross-sections under representative conditions
Y-direction cross-section
X-direction cross-section

## Slide 10
INTRODUCTION
METHODOLOGY
RESULTS
CONCLUSIONS
RESULTS
Figure 8 Comparison of Computational Speeds for models
The single-case computation times for RPM, PPM, and BBM were 3.65 ± 1.02 ms, 3.16 ± 0.95 ms, and 2.35 ± 0.80 ms, respectively, achieving approximately 2000 to 3000 times faster processing compared to COMSOL.

## Slide 11
INTRODUCTION
METHODOLOGY
RESULTS
CONCLUSIONS
CONCLUSIONS
RPM embeds governing equations into the loss function, providing stronger physical constraints than BBM.
RPM improves convergence stability and efficiency over PPM via residual connections.
RPM is the only model that maintains positive R2 across all test cases and all three physical fields.
RPM enables millisecond-level full-field prediction, supporting real-time monitoring, online optimisation, and rapid control.
2D
3D
Notes: RPM effectively overcomes the high computational cost of CFD and the poor extrapolation reliability of BBM, providing a viable framework for real-time, physics-consistent prediction of PEMFC GDL behaviour.

## Slide 12
INTRODUCTION
METHODOLOGY
RESULTS
CONCLUSIONS
REFERENCES
CO2 Emissions in 2023. https://www.iea.org/reports/co2-emissions-in-2023 (2024).
Taheri, H. R., Shakeri, M. & Zahedi, S. A. Enhancing electrical conductivity and mechanical strength of gas diffusion layers through multi-objective optimization. J. Power Sources 658, 238358 (2025).
Zhu, Y. & Chen, Z. Improvement the performance of PEMFC by the cathode right-angled trapezoidal baffle for aviation applications. Aerosp. Sci. Technol. 168, 111196 (2026).
10. Mi, S., Wei, Z., Cai, L., Xi, X. & Zang, Z. The prediction of the optimal 2D porosity distribution of gas diffusion layer for enhancing PEM fuel cell performance based on convolutional neural network image learning. Int. J. Hydrog. Energy 146, 149971 (2025).
Lian, Y., Zheng, W., Yue, C., Han, S. & Ming, P. Mass transfer capacity degradation of gas diffusion layer under 1000 hours real-world heavy duty load cycles. Int. J. Heat Mass Transf. 223, 125239 (2024).
Sun, J. et al. Artificial-intelligence-guided design of ordered gas diffusion layers for high-performing fuel cells via Bayesian machine learning. Nat. Commun. 16, 6528 (2025).
Tan, S. et al. A Physics-Informed Neural Network framework with strong robustness to low-accuracy physical models for predicting adhesive wear of self-made BNNC milling tool. J. Manuf. Process. 160, 285–301 (2026).

## Slide 13: Thanks!
Hui Zhang, Dr.Bo Li, EEMG, 16/05/2026