## Slide 1
Transparent on-demand neural approximation of EOS-based thermodynamics for pore-scale gas–condensate flow
InterPore - May 20, 2026
G. S. Gerlero, P. Calderano, B. Costa, S. Ribeiro, M. H. Caeiro, G. Ferreira,
J. Casacão, H. Althoff, M. Carvalho

## Slide 2
The flash bottleneck
<number>
Flash at every pore (grid cell), every timestep/nonlinear iteration
Flash calculations are very numerically expensive
Cost grows with component count and worsens near the critical point
Thermodynamics can easily be the bottleneck of a compositional simulation
Pore network model (PNM)

## Slide 3
<number>
Prior ML approaches
Potential for flash acceleration via machine learning techniques already known
  C.f. Gaganis & Varotsis (2012), Wang K. et al. (2019), Wang S. et al. (2022)
Existing work trains the models offline
Gap: workflow friction
  Precomputed datasets -> no runtime flexibility
Goal: solve for speed, accuracy & deployment at the same time

## Slide 4
<number>
The on-demand framework
Caller picks EOS and fluid components
Caller chooses P and/or T ranges and/or known composition
Serve predictions
Check cache
Train neural networks
Save networks to cache
Hit
Miss
Transparent caching of trained networks
Hash covers component properties + EOS + ranges/composition
Resolution order: configurable env variable→__pycache__→OS user cache dir
Needs to be fast!

## Slide 5
<number>
Neural architecture: overview
T (normalized)
Composition
(except last)
P
(normalized)
Gas fraction (as logit)
Equilibrium constants (except last, as logarithms)
Probability of single-phase (as logit)
Probability of gas if single-phase
(as logit)
Phase classifier
hidden width = 32
hidden depth = 4
GELU activation
~3.5k learnable params
Equilibrium regressor
hidden width = 32
hidden depth = 4
GELU activation
~3.5k learnable params
[Same inputs]
Only if classifier indicates two-phase
Always

## Slide 6
<number>
Test fluids & training criteria
Fixed composition: 95% C1 + 5% C16
  T ∈ [250 K, 350 K]
  P ∈ [6.9 kPa, 58.6 MPa]
Variable composition: C1 + C16
  T = 360 K
  P ∈ [6.9 kPa, 58.6 MPa]
C1: methane
C16: hexadecane
Default training targets
Classifier: 99.5% accuracy single- vs. two-phase, 95% for single-phase ID
Regressor: avg. 0.005 error (weighted by gas fraction for phase compositions)

## Slide 7
<number>
Accuracy I
Classical numerical
Neural
Fixed composition: showing gas fraction β

## Slide 8
<number>
Speedup
Training time: ~10 s in all cases
Prediction time: ~0.6 μs in all cases (architecture-bound)
Thermodynamic speedup
Fixed composition A: 147x
Fixed composition B: 110x
Variable composition: 129x
One-time training break-even cost: ~100,000 flash evaluations
Notes: Now the other key part: performance. Training took roughly 10 seconds in all cases. Prediction time is 0.6 microseconds, essentially bounded by network sizing. This leads to flash speedups above 100 times, and up to roughly 150x in some cases. Even if it’s the first time we run a mixture and neural training needs to be done, this one-time training cost is recovered after a hundred thousand flash calls, which in realistic compositional simulations is a threshold that can be reached very quickly.

## Slide 9
<number>
Effect on a PNM simulation
6.5x overall speedup
Classical numerical thermo
Neural thermo
Cubic test pore network (1k pores): showing gas fraction β
flow
flow

## Slide 10
<number>
Wrap-up
On-demand training + caching = high transparency
>100x flash speedups with errors within engineering tolerances
Relatively small training dataset (5000 x dof)
Bonus: full differentiability (can help nonlinear flow solvers)
Forward look
  Improved training/early-stopping criteria
  Adaptive operating range expansion
  Automatic network resizing (for high component counts)

## Slide 11
G.S. Gerlero

## Slide 12
<number>
Classical flash implementation
Two-phase flash
1. Successive substitution
2. BFGS Gibbs fallback
Rachford–Rice equation
Newton–bisection hybrid
P
T
Equilibrium constants
Gas fraction
Composition
Single-phase
Gas fraction & liquid and gas compositions
Single-phase stability test
1. Successive substitution
2. BFGS Gibbs fallback
Phase identification
1. Gibbs energy 2. Phase labeling heuristic
Predicted single phase
(liquid or gas)
Two-phase
<number>
Classical EOS-based numerical flash
Our own implementation of a numerical flash within the JAX computational framework for Python
Produces training data for the neural networks
Also usable on its own
Very competitive performance!

## Slide 13
<number>
Neural architecture: details
Implemented within the JAX framework
Choice of output variables of regression (gas fraction & equilibrium constants) is critical
Can work with known composition and/or P and/or T
Independent neural networks can be trained concurrently
Last equilibrium constant can be recovered via Rachford–Rice:
(Closed-form expression!)

## Slide 14
<number>
Accuracy II
Another fixed composition
Variable composition
Errors at specific evaluations
Training targets
Classifier: 99.5% accuracy single- vs. two-phase, 95% for single-phase ID
Regressor: avg. 0.005 error (weighted by gas fraction for phase compositions)