## Slide 1: A Graph Neural Network Framework for Upscaling the Pore Network Modeling Calculations
Mehdi Mahdaviara
Amir Raoof
Hydrogeology group, Department of Earth Sciences, Utrecht University

## Slide 2: Introduction
Modeling of transport phenomena is a key step in any underground development study.
Advances in micro-CT imaging have significantly helped to cope with this challenge.
To create the geometry of porous media:
  A 3D X-ray image of the sample is prepared.
  The image is segmented to recognize the pore and grain spaces.
Modeling is implemented through:
  Direct Numerical Simulation (DNS)
  Pore Network Modeling (PNM)
PNM
DNS
Image segmentation
CT Scanning
0: grains
1: pores
0
0
0
0
1
1
1
0
0
0
1
0
0
1
1
1
1
0
0
0
1
0
0
0
0
0
1
0
0
0
0
1
1
0
0
1
0
1
1
0
0
1
Dimensionless pressure distributions in different rocks obtained by LBM and PNM [2].

## Slide 3
Node (pore) data
Edge (throat) data
Connection data
Stokes equation (incompressible, steady-state):
-∇p + μ ∇²u = 0
Yaung-Laplace equation:
Pc = (2 * γ * cos(θ)) / r
Dynamic modeling
Graph-structured data

## Slide 4: Challenge
  The calculations for small samples are not necessarily representative of the larger scales.
  The PNM computational cost increases significantly with the sample dimension.
Bentheimer sandstone

## Slide 5
  We trained a U-Net autoencoder-decoder for the extraction of the skeleton and distance map directly from the grayscale images [2].

## Slide 6: Modeling Pore pressure and entry pressure

## Slide 7
Why did we utilize GNNs?
Why GNNs?
Graph-structured pore networks
Size-invariant learning
Works on variable network sizes
Upscaling

## Slide 8: Modeling
Bentheimer
The modeling was carried out for various GNN models, including:
  GCN
  GAT
  GIN
  GraphSAGE
  NNConv
The samples from 3 sandstones were used for modeling and evaluation.
Berea
CastleGate
Notes: GCN: Uses a fixed normalized neighbor averaging. GAT: Lears attention weights for neighbors. GIN: Uses sum aggregation + MLP, strong for graph structure discrimination. GraphSAGE: Samples/aggregates neighbors efficiently for large graphs. NNConv (your model): Edge attributes dynamically generate the message weights via an MLP. Very good when edge features are important.

## Slide 9: Evaluation Training performance
Pore pressure training performance – R-squared
Invasion pressure training performance – R-squared
Are GNN models able to be trained for pore-level prediction?
Pore pressure
Entry pressure
Framework performance for Castle Gate sandstone
PNM calculated
PNM calculated
GNN predicted
GNN predicted

## Slide 10: Evaluation Upscaling performance
Can the models trained on small samples be used for prediction of large samples?
Train sample size: 6003
Prediction sample size: 10003
Prediction sample size
10003
Train sample size
Pore pressure upscaling
Entry pressure upscaling
Framework performance for Bentheimer sandstone
Pore pressure upscaling
Entry pressure upscaling

## Slide 11
Can the models trained on a sample be used for prediction in another samples?
Evaluation Generalization capability
Train sample
Prediction sample
Bentheimer
Train sample: Bentheimer
Prediction sample: Berea
Pore pressure prediction
Entry pressure prediction
Pore pressure
Entry pressure
Framework performance transfer learning

## Slide 12: Evaluation How much time does the prediction take?
Pore pressure
Entry pressure

## Slide 13
Future work - Relative permeability upscaling
Train sample size:
200
Retrain sample size:
600
Prediction sample size:
1000

## Slide 14: Conclusions
This study demonstrates that GNNs can effectively learn the weighted relationships between pores, while accurately predicting pore pressure, entry pressure, and relative permeability.
The trained models show strong potential for upscaling pore-network simulation results, enabling more efficient analysis of complex porous media systems.
In addition, the models exhibit good generalization capability, highlighting their flexibility and reliability in predicting previously unseen data.

## Slide 15: Thank you for your attention! Any questions?

## Slide 16: References
Zhao, J., Qin, F., Derome, D., Kang, Q., & Carmeliet, J. (2020). Improved pore network models to simulate single-phase flow in porous media by coupling with lattice Boltzmann method. Advances in Water Resources, 145, 103738.
Mahdaviara, M., Sharifi, M., & Raoof, A. (2023). PoreSkel: Skeletonization of grayscale micro-CT images of porous media using deep learning techniques. Advances in Water Resources, 180, 104544.