## Slide 1: Machine learning-based permeability estimation in heterogeneous porous media
Hongkyu Yoon
Sandia National Laboratories, Albuquerque, NM
Contributors: P. Roy, S. Bhattacharjee (UTEP)
This work was supported by a DOE Science Foundations for Energy Earthshots project, Advanced Multi-Physics Machine Learning for Subsurface Energy Systems Across Scales.
InterPore 2026, Nantes, France
SAND2026-21040C

## Slide 2: Heterogeneous Porous Media
Sandstone & pore networks
(pores: 10’s-100’s m)
Shale
(1 nm - microns)
PN from FIB-SEM image
Heterogeneity: Complexity in geometry, size, scale, and compositions
Multiphysics processes are complicated in heterogeneous porous media
Xtlas.pergeos.com
Chemically Altered zone
Chemically unaltered zone
Magnesite
Calcite
Mg-rich Calcite/
Dolomite
Carbonate chalk under chemo-mechanical processes (pores: 10’s nm – 10’s m)
Chemically Unaltered sample
Chemically altered sample
Unflooded sample

## Slide 3: Permeability Estimation (Anisotropy)
2D synthetic data (circular, elliptic shapes) & microCT images of sandstone
As the first step, directional permeabilities are estimated for various porous media
Directional permeabilities were computed by lattice Boltzmann Modeling

## Slide 4: AnisONet: Directional Permeability Estimator
  Overall workflow
Bhattacharjee et al. Physics of Fluid (2026)
  Note: SWIN Transformer has been retrained (Geng et al., 2024)
Input images
1. Classifier
2. Baseline permeability estimator (horizontal)
3. Directional permeability estimator
(any arbitrary angle)

## Slide 5: AnisONet – DeepONet architecture
Three separate inputs are used for deepONet architecture
A zero-degree (i.e., horizontal) permeability is taken as the reference
Bhattacharjee et al. Physics of Fluid (2026)

## Slide 6: AnisONet: Directional Permeability Estimator
  LBM results (blue) vs. linear transformation (red)
Bhattacharjee et al. Physics of Fluid (2026)
  True (LBM, blue) vs. AnisONet results
Note: AnisONET results
LBM-based baseline perm (red)
SWIN-based baseline perm (green)

## Slide 7: Upscaling: Permeability Tensor Derivation
Bhattacharjee et al. Physics of Fluid (2026)
  Elliptical grains oriented at 45º
  Elliptical grains with 3 perm zones
FLSF: Full least squares fit
FPV: Fixed principal values
KPV: Known principal values from AnisONet
BIP: Boundary Informed permeability
Each upscaling method performs differently in different configurations

## Slide 8: Complex porous media case (3 permeability zones)
Bhattacharjee et al. Physics of Fluid (2026)
BIP matches the pressure profile relative well compared to the LBM result at x=0.5
All methods have relatively high errors upstream and downstream at y=0.5
All methods can’t match the characteristics of preferential flow path
along the diagonal direction on pressure drops very well, but
BIP and partially KPV perform better

## Slide 9: AnisONet vs. Fourier Neural Operator
Bhattacharjee et al. Physics of Fluid (2026)
Comparison reveals geometry-dependent performance trend
Only for the circular case, FNO marginally outperforms AnisONet
For the more complex geometries (Elliptical, Sandstone), AnisONet performs better
  FNO architecture

## Slide 10: Pore scale modeling with precipitation and dissolution
Step 1: Velocity field (u) at pore scale (Lattice Boltzmann Method)
Step 2: Reactive transport at pore scale
(Finite Volume Method)
Step 3: Update of CaCO3 volumetric content (Vm)
on reactive surface (heterogeneous reaction)
Chemical equilibrium in bulk fluid (e.g., H+, HCO3-, …)
Extended Debye-Hückel Equation for activity coefficients
Volumetric CaCO3 content
Navier-Stokes equation => Stokes equation with constant viscosity (independent of the species conc.) and at low Reynolds number
Yoon et al. (RiMG, 2015)
Phreeqc, GEMS
Charge balance equation can be added
Fracture aperture can be updated with mechanical coupling
Crystal growth: Cellular automata algorithm
Zhang et al. (EST, 2010), Yoon et al. (WRR, 2012), Fanizza et al. (WRR, 2013), Boyd et al. (GCA, 2014), Singh et al. (EST, 2015), Yoon et al. (2015, 2017, EST 2019)

## Slide 11: Upscaled permeability and porosity relationships
A
B
Pore scale reactive transport modeling
Upscaled relationship
Velocity profile
Calcite precipitation
(Normalized) Permeability vs. porosity
Yoon et al. JPSE 2017
high permeable conduit
Solid grain
Volumetric fraction of precipitates
  Pore scale reactive transport modeling to derive permeability-porosity relationships during cementation for various Peclet and Damköhler numbers

## Slide 12: Heterogeneous vs. homogeneous reactive surfaces
Velocity profile
(pressure gradient)
Non-reactive grain
Reactive calcite
{Ca2+} x {CO32-}
Concentrations
Inlet concentrations
[Ca2+]T=
[CO32-] T
=50mM
{Ca2+} x {CO32-}
Concentrations
All reactive grains

## Slide 13: Heterogeneous vs. homogeneous reactive surfaces
Concretion from
reactive grains
Concretion from
all reactive grains
Non-reactive grain
Reactive calcite
All reactive grains
Inlet concentrations
[Ca2+]T=
[CO32-] T
=50mM
Velocity profile
(pressure gradient)

## Slide 14: Reactive Transport Modeling
Influent
[Ca2+]T= 20mM
[CO32-] T=20mM
pH=7.4
Calcite

## Slide 15: Deep learning methods
  CNN (+MLP) as a baseline model
  Improved neural operator (DeepONet-based model, e.g., PRT-DeepONet)
  Variables: Peclet and Damköhler numbers to evaluate transport and reaction dominant cases (low, medium, and high cases)
  Test case: ~150 training data (snapshot of concentraions)
Yoon et al. (2020, AAAI workshop)
Kadeethum, T., Verzi, S.J. and Yoon, H., 2024. An improved neural operator framework for large-scale CO2 storage operations. Geoenergy Science and Engineering, 240, p.213007.
Concentrations
(Ca2+, CO32-, pH)
Reaction rates

## Slide 16
ML prediction: preliminary results
True
(ML pred)
Notes: Why this is a real challenging problem?
Subsurface
  uncertain materials
  uncertain structures
Multiple scales
  time, space
  multi-scale analysis (e.g. homogenization) attempts to exploit any scale separation
  may not have scale separation → scale embedding with ‘mortars’
  fracture is inherently multi-scale
Multiple physics
  geomechanics, geochemistry, biology
  solid mechanics, porous flow, chemical and biological reactions
  phase changes, localization, fracture
Dynamic, highly nonlinear
  instabilities, bifurcation phenomena, limit cycles
  emergent phenomena
Multiphase flows in highly permeable structures, such as coarse sands or distillation columns, requires
a specific treatment due to the fact that, when the pore size becomes very large, Reynolds
number, capillary number and Bond number attached to the flow can no longer be considered small,
as it is assumed for the quasi-static assumption, i.e., the system can no longer be described as mainly
controlled by capillarity. As a consequence, the classical generalized Darcy’s law model must be
adapted. While this is largely an open question, experimental and theoretical evidence suggest that,
at least, terms representing the drag force between the two phases must be added to the generalized
Darcy’s law. This has been emphasized in recent studies showing, for instance, a deviation from
the hydrostatic pressure drop in water observed in a vertical column subject to an upward gas flow
Chikhi, N., Clavier, R., Laurent, J. P., Fichot, F., & Quintard, M. (2016). Pressure drop and average void
fraction measurements for two-phase flow through highly permeable porous media. Annals of Nuclear
Energy, 94, 422-432.
Davit, Y., & Quintard, M. (2018). One-Phase and Two-Phase Flow in Highly Permeable Porous Media.
Heat Transfer Engineering, 1-19.

## Slide 17: Summary
AnisONet can predict directional permeabilities for images and can be used for upscaled model properties
AnisONet (with Jax-based LBM) is being applied for 3D porous media
Pore scale reactive transport enables us to improve fundamental understanding of physical-chemical processes involved in various subsurface energy systems
Improved neural operator was able to predict chemical concentrations reasonably well (in progress)
An adaptive strategy to couple pore- and continuum scale using machine/deep learning methods will be tested against more realistic cases