## Slide 1: Data-Driven Prediction of Relative Permeability: Applications to CO₂ and Hydrogen Storage
Abdolali (Ali) Mosallanezhad1, Amir Jahanbakhsh1,2, and M. Mercedes Maroto-Valer1,2
1 The Research Centre for Carbon Solutions (RCCS), School of Engineering and Physical Sciences, Heriot-Watt University, Edinburgh, UK
2 Industrial Decarbonisation Research and Innovation Centre (IDRIC), Heriot-Watt University, Edinburgh, UK
May 2026

## Slide 2
2
CO2/Hydrogen Storage in Porous Media
Relative permeability curves are essential inputs for multiphase reservoir simulation.
Reservoir Simulation
Predict storage capacity
Support safe CO₂/H₂ storage design
Identify key uncertainties
Plan injection/withdrawal rates
Convert lab data into field-scale forecasts
Optimise well placement
Important INPUT:

## Slide 3
3
Relative Permeability in Porous Media
Relative permeability controls gas–brine mobility, which affects:
Gas plume migration
Residual trapping
Pressure response
Simulation forecast reliability
Gas Plume
Porous Media Saturated with Water
Trapped Gas
Experimental Bottleneck:
Experiments are:
Expensive
Time-consuming
Dependent on core availability
Limited in pressure, temperature, and rock coverage
Insufficient to capture full reservoir heterogeneity

## Slide 4
4
Research Objectives
Develop a machine-learning workflow to predict water and gas relative permeability (krw and krg) for gas–brine systems in Sandstones.
Data Acquisition
Data
Curation
End Point Prediction
Curve
Prediction
Temperature, Pressure, Fluid Viscosities, Salinity, Brine Composition, IFT, Wettability, Rock Mineralogy, Pore size, Sw, Krw, Krg
Physics-Aware Transformation For Training, and Normalising them between [0,1] by their Max and Min values for better Consistency
Selecting the best ML Model based on the number of data points and the workflow

## Slide 5
5
Data Acquisition and Curation
Data Acquisition on H2 and CO2 Relative Permeability and their Corresponding Conditions via LLMs:
Features to look for:
Temperature, Pressure, Porosity, Permeability, Rock Type, Brine Salinity, Brine Composition, Pore Size, Contact Angle, Gas Viscosity, Brine Viscosity, IFT, Capillary Pressure
Transformation Based on Rock/Fluid (Porous Media) Physics
 | Temperature (K) | Pressure (Mpa) | Porosity | Permeability (mD) | Pore throat size (µm) | Mean Pore size (µm) | Contact Angle | Calcite % | Feldspar % | Mica% | Clay % | Quartz % | Gas Viscosity (cp) | Brine Viscosity (cp) | IFT (mN/m) | Brine Salinity (mol/kg) | MCM (mol/kg) | BCM (mol/kg)
Min | 293.15 | 1.38 | 0.039 | 2.94E-06 | 0.1 | 0.006 | 1.19 | 0 | 0 | 0 | 0 | 0 | 0.014 | 0.25 | 19.8 | 0 | 0 | 0
Max | 395.15 | 34.47 | 0.383 | 1810 | 25 | 150 | 86.93 | 100 | 24.1 | 7 | 49.2 | 99.5 | 0.083 | 1.12 | 57 | 9.36 | 3.83 | 0.65
Features Ranges:

## Slide 6
6
Endpoint Prediction
Why predict Swirr and Krg0 first?
Transferability
Reconstruction
Saturation Window
Curve Boundaries
Why
How?

## Slide 7
7
Endpoint Results (Swirr)
Dataset | RMSE | MSE | MAE | R2 | Bias | AAPRE | STD Error | Coverage_90
Test | 0.09 | 0.008 | 0.075 | 0.75 | -0.0016 | 16.84 | 0.093 | 0.89
Train | 0.05 | 0.0009 | 0.017 | 0.85 | -0.0007 | 5.73 | 0.029 | 1
Predicted vs Measured Swirr
Predicted Values: Swirr_hat
Notes: The OOF result is genuinely encouraging:
That means the model is learning meaningful structure for Swirr. An 𝑅^2of about 0.75 for a core-level endpoint with only ~65 cores is respectable. Swirr is controlled by pore structure, wettability, capillary scale, and experimental protocol; it is not a trivial target. So this is not a weak result.
The bias is almost zero:
𝐵𝑖𝑎𝑠≈−0.00166
That is good. The model is not systematically overpredicting or underpredicting Swirr overall. The remaining error is mostly scatter, not directional bias.
The coverage is excellent:
𝐶𝑜𝑣𝑒𝑟𝑎𝑔𝑒_90=0.892
That is almost exactly nominal 90% coverage. So the uncertainty intervals are behaving honestly, at least under the OOF setup.

## Slide 8
8
Endpoint Results (Swirr)

## Slide 9
8
Endpoint Results (Swirr)

## Slide 10
9
Endpoint Results (krg0)
Dataset | RMSE | MSE | MAE | R2 | Bias | APRE | STD_Error | Coverage_90
Test | 0.179 | 0.015 | 0.149 | 0.60 | 0.0073 | 44.34 | 0.179 | 0.83
Train | 0.127 | 0.005 | 0.058 | 0.79 | 0.003 | 29.15 | 0.077 | 1
Predicted vs Measured krg0
Predicted Values: krg0_hat

## Slide 11
10
Endpoint Results (krg0)
Notes: The residuals are not randomly scattered around zero. At low predicted Krg0, the errors are relatively small. But as predicted Krg0 increases, the residual spread becomes much wider, ranging from roughly 0.5 to +0.4. That means the model becomes much less reliable for moderate-to-high predicted Krg0.
This is heteroscedastic behaviour: the error magnitude depends on the predicted value. The model is more confident-looking in low-Krg0 regions and much less stable in high-Krg0 regions. That is physically plausible because high gas endpoint permeability depends on connected gas pathways, pore-throat structure, and the exact definition of Swirr. These are hard to infer from limited core descriptors.
The SHAP ranking says the model uses the features in this approximate order:
"Swirr\_hat">〖log⁡ 〗_10 𝐾>𝑃>〖log⁡ 〗_10 𝑟_𝑚>𝐼𝐹𝑇>𝜙>𝑇
The most important feature is Swirr_hat, which is physically sensible. High Swirr_hat values mostly push Krg0 downward, while low Swirr_hat values push Krg0 upward. That makes sense: if more water remains irreducibly trapped, the gas phase has less connected pore space available at the endpoint, so gas relative permeability at Swirr tends to be lower.
IFT also matters. Higher IFT seems to push Krg0 downward, while lower IFT often pushes it upward. This can be interpreted as the IFT decrease, gas and water viscosity will get closer to each other and as a result, gas will flow through the pores more easily, but again I would be cautious because IFT is probably correlated with pressure, temperature, and CO₂ state.

## Slide 12
10
Endpoint Results (krg0)
Notes: The residuals are not randomly scattered around zero. At low predicted Krg0, the errors are relatively small. But as predicted Krg0 increases, the residual spread becomes much wider, ranging from roughly 0.5 to +0.4. That means the model becomes much less reliable for moderate-to-high predicted Krg0.
This is heteroscedastic behaviour: the error magnitude depends on the predicted value. The model is more confident-looking in low-Krg0 regions and much less stable in high-Krg0 regions. That is physically plausible because high gas endpoint permeability depends on connected gas pathways, pore-throat structure, and the exact definition of Swirr. These are hard to infer from limited core descriptors.
The SHAP ranking says the model uses the features in this approximate order:
"Swirr\_hat">〖log⁡ 〗_10 𝐾>𝑃>〖log⁡ 〗_10 𝑟_𝑚>𝐼𝐹𝑇>𝜙>𝑇
The most important feature is Swirr_hat, which is physically sensible. High Swirr_hat values mostly push Krg0 downward, while low Swirr_hat values push Krg0 upward. That makes sense: if more water remains irreducibly trapped, the gas phase has less connected pore space available at the endpoint, so gas relative permeability at Swirr tends to be lower.
IFT also matters. Higher IFT seems to push Krg0 downward, while lower IFT often pushes it upward. This can be interpreted as the IFT decrease, gas and water viscosity will get closer to each other and as a result, gas will flow through the pores more easily, but again I would be cautious because IFT is probably correlated with pressure, temperature, and CO₂ state.

## Slide 13
11
Curve Results (krw & krg)
Target | Phase | Model Name | Value Space | Test RMSE | Test R2 | Test MAE | Test MSE | Train RMSE | Train R2 | Pi_coverage_90
krg | gas | catboost | absolute | 0.100 | 0.805 | 0.065 | 0.010 | 0.098 | 0.813 | 0.878
krg_norm | gas | catboost | normalized | 0.171 | 0.820 | 0.129 | 0.029 | 0.168 | 0.829 | 0.896
krw | water | catboost | absolute | 0.111 | 0.869 | 0.080 | 0.012 | 0.104 | 0.884 | 0.879
krw_norm | water | catboost | normalized | 0.111 | 0.869 | 0.080 | 0.012 | 0.104 | 0.884 | 0.879
How did we do it with the Endpoints?
Recalculated the normalised water saturation using the predicted endpoints:
Trained the model on the new normalised values
The predicted krg0_hat was used to reconstruct the relative permeability
Notes: The residuals are not randomly scattered around zero. At low predicted Krg0, the errors are relatively small. But as predicted Krg0 increases, the residual spread becomes much wider, ranging from roughly 0.5 to +0.4. That means the model becomes much less reliable for moderate-to-high predicted Krg0.
This is heteroscedastic behaviour: the error magnitude depends on the predicted value. The model is more confident-looking in low-Krg0 regions and much less stable in high-Krg0 regions. That is physically plausible because high gas endpoint permeability depends on connected gas pathways, pore-throat structure, and the exact definition of Swirr. These are hard to infer from limited core descriptors.
The SHAP ranking says the model uses the features in this approximate order:
"Swirr\_hat">〖log⁡ 〗_10 𝐾>𝑃>〖log⁡ 〗_10 𝑟_𝑚>𝐼𝐹𝑇>𝜙>𝑇
The most important feature is Swirr_hat, which is physically sensible. High Swirr_hat values mostly push Krg0 downward, while low Swirr_hat values push Krg0 upward. That makes sense: if more water remains irreducibly trapped, the gas phase has less connected pore space available at the endpoint, so gas relative permeability at Swirr tends to be lower.
IFT also matters. Higher IFT seems to push Krg0 downward, while lower IFT often pushes it upward. This can be interpreted as the IFT decrease, gas and water viscosity will get closer to each other and as a result, gas will flow through the pores more easily, but again I would be cautious because IFT is probably correlated with pressure, temperature, and CO₂ state.

## Slide 14
12
Curve Results (krw & krg)
Three Permeability Regimes
Low Permeability: 0.356 mD
High Permeability: 430 mD
Medium Permeability: 74.4 mD

## Slide 15
13
Curve Results (krw & krg)
Worst Case Scenario
Why?
We went back and checked the study:
They stated that the core plugs were Highly Heterogeneous

## Slide 16
14
Key Points
ML captures the main physical trends in relative permeability endpoints and curves from a small dataset of ~70 core plugs.
The workflow is diagnostic, not cosmetic: noisy experiments were not removed just to improve metrics; residuals and SHAP were used to identify possible experimental or metadata issues.
Current limitations include hidden core heterogeneity such as microfractures, fissures, laminations, vugs, and unresolved pore-throat connectivity.
The model can support screening-level reservoir simulation when SCAL/relative permeability data are scarce or incomplete.
Predictions should be used with uncertainty intervals, not as absolute laboratory replacements.
Swirr is predicted more reliably than Krg0, because krg0 is more sensitive to gas connectivity, endpoint definition, and experimental uncertainty.

## Slide 17
Dr. Amir Jahanbakhsh
Research Fellow/Programme Manager
School of Engineering & Physical Sciences, Institute of Mechanical, Process & Energy Engineering, Heriot-Watt University
Prof. Mercedes Maroto-Valer
Director
School of Engineering & Physical Sciences, Institute of Mechanical, Process & Energy Engineering, Heriot-Watt University
Abdolali (Ali) Mosallanezhad
PhD Researcher
School of Engineering & Physical Sciences, Institute of Mechanical, Process & Energy Engineering, Heriot-Watt University
Thank You for Your Attention