## Slide 1: ML-Assisted Topology Optimization of Thermochemical Heat Storage Reactors
Torben Prill, Thomas Jahnke

## Slide 2: Thermochemical Heat Storage in the SrBr-System
Thermochemical heat storage in the SrBr-System
Storage and release of heat energy in a chemical reaction
  Reaction:
  Enthalpy of Reaction:
SrBr/H2O-System
  Charge:
    Dehydration reaction at ca. 1,3 kPa and T=168 °C
  Discharge:
    Hydration reaction at ca. 67 kPa and T=208 °C
Used as a fixed bed at temperatures between 150°C and 250°C

## Slide 3: Wall Detachment as a Bottleneck in Heat Transport
Problem:
  Fill expands/contracts during cycling
  Detachment of the fill from the heat conducting structure during cycling, impairs heat transfer.
Solution:
  Integration of heat transfer structures (HTS) into reaction bed to improve thermal contact.
Project THEMSE 2
  Optimization of heat transfer in reactors for the SrBr/H2O system.
  Build simulation model for reactor
  Optimize fins with numerical topology optimization
  Using AI for surrogate modeling!

## Slide 4: Physical Model Based on Porous Media Theory
Pressure equation
Energy equation
Conservation of solid mass
Darcy’s law
Heat Transfer Resistance
Reaction kinetics
Model based on: Jana Stengler, Inga Bürger, Marc Linder, "Performance analysis of a gas-solid thermochemical energy storage using numerical and experimental methods", International Journal of Heat and Mass Transfer, Volume 167, 2021, 120797
Powder bed
HTF
Gas port

## Slide 5: Topology optimization

## Slide 6: Numerical Topology Optimization
Optimization
  Find optimal geometry for fin structure
  State of Charge variable SOC
  where is full charge
Target: Total discharge at time
Maximizes energy output at time
Constraints:
  Minimal volume fraction of fins
    Baked into functional
    in fins counts as
  Fins must be connected to HTF
  Powder bed must be connected to gas port

## Slide 7: ML Surrogate Model
Network Architectures
  Autoencoder
  CNN-Autoencoder
  Variational Autoencoder
  MSNet
  Time Dependent
    Autoregressive MSNet [1]
    Autoregressive SinGAN [2]
Setup
  Dataset with 100 geometries (as few as possible)
    Training: 80 geometries
    Testing: 20 geometries
  Validation with 50 geometries
    For testing generalization!
  6 Timesteps each ()
Features
  SOC in preceeding timestep
  Phase function
  Euclidian Distance Transform (EDT) wrt. fins
  EDT to gas-port
EDT fins
EDT gas-port
Prediction
SOC at t
SOC at t+dt

## Slide 8: Synthetic Training Data
Generation of ca. 150 random HTS
Constraints:
  Bed must have access to gas boundary
  Fin must be connected to HTF
  6-fold symmetry
Generation of training data
  Generate symmetric and concentric lines in domain
  Compute Skeleton
  Thicken skeleton
  Insert into geometry
Maximum number of branches can be controlled with parameter
Parameters:

## Slide 9: Autoregressive sinGAN
  Last time:
    Best model aMSNet
    Error range 1-2% in SOC
    Samll problems at the Boundary!
  New model SinGAN:
    Removes masking from the learning
    Slightly better results
  Reasons:
    Both methods are essentially non-linear kernel methods
      Explains low data requirement
    Removing masking improves info at thin structures
  Still problems in full field prediction!
aSinGAN
aMSNet
aMSNet
aSinGAN

## Slide 10: Topology Optimization With Level-Sets
Parametrization of geometry with Level-Set function
Sets:
  Powder bed and fin structure:
Evolution with Hamilton-Jacobi equation
Velocity given by shape derivative
Evolution until optimum\stationarity is reached!

## Slide 11: Learning the Shape Derivative
Computation
  Can be computed with Firedrake adjoint solver
  Hilbertian regularization of the shape derivative extending it to the whole domain
NN Input:
  Current timestep
  EDT Features

## Slide 12: Topology Optimization
Results:
  Optimization loop gets stuck in local minima
  Numerically unstable
  Violates constraints
Possible Reasons
  Surrogate model does not “learn” fin conductivity and thickness
    Small temperature variations
    L2-Error
Possible Solutions
  Combine learned gradient with equality or inequality constraints via KKT equation
  Combine Level-Set solver with stochastic gradient algorithms
However this is a long shot!

## Slide 13: Brute Force Parametric Optimization
Resulting optimization problem in parameters
Optimization problem is non-convex and not smooth
Surrogate modeling enables ‚brute-force‘ optimization of reactor performance
  Find global minimum in parameter space
Vary line radii in 15 steps
  For
    Evaluation of 3.3k combinations takes ca. 2 min.
  For
    Evaluation of 3.3k combinations takes ca. 30 min.
  For
    Evaluation of 50k combinations takes ca. 7 h

## Slide 14: Topology Optimization With Genetic Algorithms
Method
  Downsampling to 64x64
  Global optimization of functional with genetic algorithm pyGAD [3]
  Rejection of non-conneted fins
Results after 3k generations with 20 function calls per generation:
  Very fine grained structure
  Not suitable for prediction
  Not even with 3D printing
  Need to introduce regularization!
Regularization with surface area penalty term
Penalty reduces complexity!
However:
  Model cannot predict heat transport in fins.
  Overly complex solutions!
Pure Heat Conduction (SIMP)
Surrogate Reactor Model
No reg.
Regularized

## Slide 15: Optimization of Contact Problems
Work ongoing!
Solving for geometrically linear and constitutively non-linear elasticity
Momentum equation:
Stress-tensor
Strain-tensor
Non-linear , :
  Boundary layer soft in tension, but hard in compression
Results:
  Detachment happens with convex shape
  NN only trained with convex shapes
    Too bad!
  Would need regularization like shape derivative

## Slide 16: Conclusion & Outlook
Summary
  Optimization of heat transfer structures
  Surrogate modeling of reactor possible with suitable machine learning algorithms
    SinGAN performs best
  Enables brute-force and stochastic optimization of non-convex, non-smooth problems.
  However need additional constraints
  Level-Set not working so far! 
Outlook
  Modeling
    Looking for even better surrogate models for heat transfer in fins
    Based in Model Order Reduction Techniques
      Difficult with low data req.
  Optimization of heat transfer structures
    Use current parameterized model to “cue in” more general topology optimization methods looking for local minimum
      Level-Set implemented in simulation
        Stability?
    Explore different objective functions
      Regularization Techniques
    Find optima for different requirements
      Optimize for Power, Capacity etc.
      Explore Pareto Front between objectives
References:
[1] Agnese Marcato, Javier E. Santos, Chaoyue Liu, Gianluca Boccardo, Daniele Marchisio, Alejandro A. Franco, (2023) Modeling the 4D discharge of lithium-ion batteries with a multiscale time-dependent deep learning framework, Energy Storage Materials 63, 102927
[2] Shaham, Tamar Rott, Tali Dekel, and Tomer Michaeli. "SinGAN: Learning a Generative Model from a Single Natural Image." arXiv preprint arXiv:1905.01164 (2019)
[3] Gad, A.F. PyGAD: an intuitive genetic algorithm Python library. Multimed Tools Appl 83, 58029–58042 (2024)