## Slide 1
Haoyuan Dou (China University of Petroleum (Beijing), Beijing China)
Bing Hou (China University of Petroleum (Beijing) at Karamay, Xinjiang, China)
Study on Leakage Mechanisms in Vesicular Volcanic Rocks Dominated by Fine‑to‑Microscopic Pore Structures

## Slide 2
Ⅲ
Part3. Conclusions and discussions
Part2. Methodology
Ⅱ
Ⅲ
Ⅱ
Part1. Introduction
Ⅰ

## Slide 3
The Mabei Feng-1 Member reservoir is located in the Wuxia fault belt on the western uplift of the Junggar Basin. The reservoir primarily develops high‑porosity volcanic and clastic reservoirs. It exhibits high rock mechanical strength and high in‑situ stress.
Moreover, dissolution pores are widely developed as the reservoir space, resulting in high fracturing fluid leak‑off, narrow hydraulic fractures, and a high risk associated with large‑scale proppant placement.
Geological background
Introduction
microscopic dissolution pores

## Slide 4
Ⅲ
Part3. Conclusions and discussions
Part2. Methodology
Ⅱ
Ⅲ
Ⅱ
Part1. Introduction
Ⅰ

## Slide 5
Microscale Characterization Method — Scanning Electron Microscopy (SEM)
Using the FEI Quanta200F SEM, the development of micro-cracks, dissolution pores, and mineral distribution characteristics on rock cross-sections can be observed with high precision, allowing for the microscopic-scale characterization of pore structures in dissolution pore-type Igneous rocks.
Cuttings for Laboratory Testing
SEM analysis results
Microscopic dissolution pores
Methodology

## Slide 6
three-dimensional digital core
Methodology
Using a high-precision CT scanner, a three-dimensional digital core is reconstructed to finely characterize, from a mesoscale scale, complex structures such as natural fracture networks and joints within Igneous rocks.
Mesoscale Characterization Method—3D Digital Core Reconstruction

## Slide 7
Study on Leakage Mechanisms in Vesicular Volcanic Rocks
Methodology
By integrating the microscopic results from SEM analysis and the mesoscopic results from 3D digital core reconstruction, the distribution characteristics of dissolution pores and fractures in micro‑mesoscale igneous rocks are characterized.
Furthermore, the lost circulation mechanism and the analysis of influencing factors for dissolution‑pore type volcanic rocks dominated by micro‑mesoscale pore structures are investigated.

## Slide 8
Ⅲ
Part3. Conclusions and discussions
Part2. Methodology
Ⅱ
Ⅲ
Ⅱ
Part1. Introduction
Ⅰ

## Slide 9
Micro‑Mesoscale Experimental Results— low dissolution pore content(1#)
Sample 1# is characterized by a low content of dissolution pores and generally poor pore development. Dissolution pores are mostly distributed near the boundary, with two irregular dissolution pores larger than 4 mm in radius developed in the upper to middle part, and the maximum dissolution pore radius is 7.49 mm.
The microscopic pores inside Sample 1# are mainly strip‑shaped intergranular pores, among which the largest micropore has a diameter of 551.7 μm. This micropore is filled with organic matter, lacks communication via micro‑fractures, and exhibits poor interconnection with each other.
Conclusions and discussions
large dissolution pores
middle dissolution pores
Oil droplet
Dissolution pore zone
Intergranular pore zone
3
2D grayscale image
3D digital core image
SEM micrograph
30
Large
volume
Middle
volume
Small
volume
V/mm3

## Slide 10
Samples 2# and 3# are dominated by small‑sized dissolution pores that are uniformly distributed within the core. The dissolution pore volumes account for approximately 9% and 14% of the sample volume, respectively. Micro‑fractures connect the small pores in the middle part, forming a relatively large storage space.
Sample 2# develops more micro‑fractures with good connectivity, but dissolution pores are poorly developed. Sample 3# develops both dissolution pores and micro‑fractures; the dissolution pores are polygonal in shape, and the pore connectivity is relatively good.
Conclusions and discussions
Micro-crack
30
50
Micro‑Mesoscale Experimental Results— middle dissolution pore content(2#/3#)
Experimental image of Core 2#
Experimental image of Core 3#
Large
volume
Middle
volume
Small
volume
Large
volume
Middle
volume
Small
volume
Dissolution pore zone
Dissolution pore zone
Intergranular pore zone
middle dissolution pores

## Slide 11
Samples 4# and 5# exhibit relatively high and uniformly distributed dissolution pore contents. The dissolution pore volume of Sample 4# accounts for approximately 40% of the sample volume, with no micro‑fractures connecting the pores. Sample 5# develops larger dissolution pores throughout the sample.
SEM results show that micro‑ and nano‑scale dissolution pores are mostly polygonal or circular, while intergranular pores are mostly triangular or strip‑shaped. The well‑developed micro‑vug and micro‑fracture assemblages inside the cuttings with high dissolution pore content are favorable for hydrocarbon storage and migration, resulting in a high degree of hydrocarbon enrichment and good connectivity.
Conclusions and discussions
Organic matter filling
30
Micro‑Mesoscale Experimental Results— high dissolution pore content(4#/5#)
30
Experimental image of Core 4#
Experimental image of Core 5#
Large
volume
Middle
volume
Small
volume
Large
volume
Middle
volume
Small
volume
Dissolution pore zone
Intergranular pore zone
Dissolution pore zone
Dissolution pore zone
Intergranular pore zone
middle dissolution pores

## Slide 12
Lost Circulation Mechanism Dominated by Meso-microscale Pore Structures
The dissolution pore-type igneous reservoir in the Mabei Feng-1 Member has an average pore volume fraction of 26.7%. The dissolution pores exhibit irregular ellipsoidal structures u'jwith a wide range of sizes. Within a single standard core plug, the dissolution pore volumes range from 4 mm to 30 mm. The distribution of dissolution pore structures is highly heterogeneous, with pore volume fractions varying from 3% to 33%.
In samples with low dissolution pore content, the pores are isolated and distributed near the boundary. In samples with medium dissolution pore content, the pores are uniformly distributed, and micro-fractures together with dissolution pores form a directional three-dimensional fracture‑vug network. In samples with high dissolution pore content, large pores dominate, the proportion of isolated pores is high.
Conclusions and discussions
Sample | Depth/m | Maximum dissolution pore radius/mm | Dissolution pore volume fraction | Pore-fracture connectivity
Low dissolution pore content | 4920.0 | 7.49 | 1%-4% | Locally networked fracture-vug structures with poor inter-connectivity
Middle dissolution pore content | 4904.2/ 4932.0 | 10.78-11.83 | 9%-20% | Micro-fractures connecting small pores in the middle create considerable storage space
High dissolution pore content | 4907.8/ 4935.6 | 11.42-11.60 | >20% | Large pores are isolated with few micro-fractures connecting them

## Slide 13
Polygonal dissolution pores account for 43% of the micropores, while strip-shaped intergranular pores account for 52%. Approximately 24 micropores with diameters larger than 50nm are developed per square micrometer. The interiors of dissolution pores are mostly filled with organic matter, and some are partially cemented by inorganic cements. Micro-fractures extend in a lightning-like pattern from low-dissolution-pore-density areas to high-density areas.
The dominant lost circulation type is pore-fracture composite loss. The loss amount and loss rate are synergistically controlled by the content and density of dissolution pores. The connection between micron-scale micro-fractures and dissolution pores significantly enhances the complexity of loss pathways, whereas cements inhibit loss by blocking throats.
Conclusions and discussions
Sample | Depth/m | Lithology | Characteristics of natural micro-fractures
Low dissolution pore content | 4920.0 | Basalt/ Ignimbrite | No obvious fractures observed
Middle dissolution pore content | 4904.2/ 4932.0 | Ignimbrite | Dissolution pores and micro-fractures developed
High dissolution pore content | 4907.8/ 4935.6 | Ignimbrite /Welded breccia | Micro-fractures poorly developed, with locally distinct network fracture-vug structures
Lost Circulation Mechanism Dominated by Meso-microscale Pore Structures

## Slide 14
During drilling of the igneous reservoir in the Fengcheng Formation, the average drilling fluid density was 1.24 g/cm³, the average lost circulation rate was 22.3 m³/h, and the average lost circulation volume was 148.2 m³.
Losses were mainly concentrated in the middle-upper part of the Feng-1 Member (at depths of 4800–5000 m), where dissolution pores and fractures are relatively well developed, and the loss frequency accounted for more than 80% of total loss events.
Lithology influences lost circulation behavior. As a pyroclastic rock, tuff contains pores and joint fractures and is prone to forming wide fractures (0.5–3 mm) after fracturing, resulting in a relatively high lost circulation rate. The average loss rate is 28 m³/h, and the loss frequency accounts for 45% of total loss events, mainly occurring in the upper to middle intervals.
In the interval of 4896–4910 m, which has a relatively high dissolution pore content, the average loss rate was 26 m³/h, which is 16.6% higher than the overall average, and the average loss volume was 179.7 m³, which is 21.2% higher than the overall average.
Conclusions and discussions
Statistics of lost circulation in dissolution pore-type igneous rocks
Number | Depth /m | Lithology | drilling fluid density /g/cm3 | lost circulation rate/ m3/h | lost circulation volume /m3
1 | 4896 | Ignimbrite | 1.23 | 30 | 230
2 | 4906 | Volcanic breccia | 1.23 | 19-33 | 124
3 | 4910 | Ignimbrite | 1.25 | 26 | 185
4 | 4913 | Volcanic breccia | 1.24 | 22 | 132
5 | 4921 | Vesicular basalt | 1.24 | 13 | 70

## Slide 15
Conclusions
The igneous formation of the Mabei Feng-1 Member is dominated by pore-fracture composite lost circulation, with losses concentrated in the middle-upper interval at depths of 4800–5000m within the Wuxia fault belt of the western uplift.
For samples with low dissolution pore content, pores are isolated and distributed near the boundary, exhibiting poor connectivity.
For samples with medium dissolution pore content, pores are uniformly distributed, and micro-fractures together with dissolution pores form a three-dimensional fracture-vug network, resulting in a high risk of lost circulation.
For samples with high dissolution pore content, large pores dominate and the proportion of isolated pores is high, with permeability limited by the lack of fractures. However, induced fractures generated by pressure fluctuations during drilling can easily connect large dissolution pores, leading to severe lost circulation.
In reservoirs with high dissolution pore content, pressure fluctuations in the wellbore during drilling tend to connect large dissolution pores within the rock, forming high-rate lost circulation pathways.
For intervals with low to medium dissolution pore content, pore connectivity is relatively poor, and fluid loss occurs mainly along the fracture network, resulting in a low overall lost circulation rate.
The connection between micro-fractures and dissolution pores significantly enhances the complexity of loss pathways, whereas cements inhibit mud loss by plugging throats.
In the high dissolution pore interval (4896–4910 m), the average loss rate is 26 m³/h and the loss volume is 179.7 m³, which are 16.6% and 21.2% higher than the overall averages, respectively. In the low-to-medium dissolution pore interval (4913–4921 m), the loss rate and loss volume are 21.5% and 31.8% lower than the overall averages, respectively.
The difference in loss rate is controlled by drilling fluid properties (density, viscosity), drilling operation parameters (rate of penetration, flow rate), and the size differences of fractures and vugs.
Conclusions and discussions

## Slide 16
Thanks for listening！