## Slide 1: Modelling of the gas flow regimes in the anodic flow channels in Proton Exchange Membrane Water Electrolysis
Ahmed Elewaily, Gergely Schmidt & Insa Neuweiler

## Slide 2: 1. Introduction
Introduction
Methodology
Validation
Results
Conclusion
PEMWE splits water into hydrogen and oxygen.
In the Anode:
In the Cathode:
Anodic channels
PEMWE: Proton Exchange Membrane Water Electrolysis needed for the production of clean hydrogen
The anodic channels carry water and gas (mainly ). Different flow regimes can develop.
We study these channels only

## Slide 3: 1. Introduction
Maier et al. (2022)
PEMWE is a promising technology , but efficiency losses still contribute to high cost.
Large slugs and annular flow are associated with poor performance
Flow regimes depend on operating conditions and flow-field design.
Objective: Modelling gas flow regimes in anodic PEMWE channels.
Introduction
Methodology
Validation
Results
Conclusion

## Slide 4: 2. Methodology
Introduction
Methodology
Validation
Results
Conclusion
Numerical framework:
Finite-volume method + VOF for two-phase flow
Implemented in OpenFOAM
Naiver-stokes equations:
Volume of fluid method (VOF):
Simulate the two phases as one phase using the phase indicator α
Surface tension force :
continuum surface force (CSF)

## Slide 5: 2. Methodology
Introduction
Methodology
Validation
Results
Conclusion
Main model inputs:
Reduced domain – only channels - Avoids explicit electrochemistry modelling
Gas flow rate  controlled by current density
Water flow rate in the channels inlet
Gas flow rate
Water flow rate

## Slide 6: 2. Methodology
Introduction
Methodology
Validation
Results
Conclusion
Main model inputs:
1. Gas injection through injectors
Key modelling assumptions
mimic gas detachment sites at the PTL–channel interface (Number based on Wang et al. (2021))
2. Fully wetted walls
One injector
Staggered injection
Reduced domain – only channels - Avoids explicit electrochemistry modelling
Gas flow rate  controlled by current density
Water flow rate in the channels inlet

## Slide 7: 3. Validation
Introduction
Methodology
Validation
Results
Conclusion
3.1 Bubble size from a single injector
Single-injector bubble size compared with Li et al. (2019)
Gas flow rate
Water flow rate
Model
Mean bubble diameter agrees well with experiments
Gas flow rate
Water flow rate
Experiments

## Slide 8: 3. Validation
Simulated bubble/slug sizes fall within the experimental range
Gas coverage agrees well across all current densities
Introduction
Methodology
Validation
Results
Conclusion
3.2 Validation at different current densities
Compared with experimental observations of Wu et al. (2024)

## Slide 9: 3. Validation
Introduction
Methodology
Validation
Results
Conclusion
3.2 Validation at different current densities
Compared with experimental observations of Wu et al. (2024)
Transition from bubbly to slug/annular flow is captured.
Simulations give a more uniform gas distribution and shorter slugs.
Likely related to uniform current density in the model.

## Slide 10: 3. Validation
Introduction
Methodology
Validation
Results
Conclusion
3.3 Validation with different flow rates
Gas flow rate fraction
Percentage of large slugs at monitoring cross section
Weak sensitivity to the specific combination at fixed
Experimental results show stronger separate effects of and ​
Higher ​→ shorter gas structures and lower gas coverage

## Slide 11: 4. Results
Introduction
Methodology
Validation
Results
Conclusion
Single Serpentine
Parallel
Pin
First results: Different flow-field designs
The pin design, followed by the parallel design, appears to distribute gas more evenly over time than the single-serpentine design
Analysis still ongoing
Goal
Identify the flow-field design with less gas blockage (potentially lower mass-transport losses)

## Slide 12: 5. Conclusion
A two-phase VOF-based CFD model was developed to resolve gas flow regimes in anodic PEMWE channels.
The proposed injector concept produces realistic gas generation behavior without explicitly resolving electrochemistry or porous layers.
The model captures key experimental trends:
realistic bubble/slug sizes,
regime transitions,
and regime change with different operating conditions .
Preliminary results suggest that the pin and parallel designs provide better gas distribution over time than the single-serpentine design (therefore probably lower mass-transport losses)
Introduction
Methodology
Validation
Results
Conclusion

## Slide 13
Thank you
Introduction
Methodology
Validation
Results
Conclusion