## Slide 1
An Integrated workflow for building digital rock model of multi-scale carbonate rocks
Zhenkai (Josh) Bo, Hannah P. Menke, Julien Maes, Ahmed H. Elsheikh, Tom Bultreys, Kamaljit Singh
Institute of GeoEnergy Engineering, Heriot-Watt University, Edinburgh, U.K.
Centre for X-ray Tomography (UGCT), Ghent University, Ghent, Belgium

## Slide 2
Content
Carbonate microporosity heterogeneity
    Multi-scale imaging
    Super-resolution
Propose ESMDA for microporosity
Forward: XPM simulation with Super-resolution
Conclusion

## Slide 3
Carbonate microporosity heterogeneity
0.5 mm
Resolved pore
(macropore)
Unresolved pore
(microporosity)
Multi-scale imaging
Resources-intensive, mechanically uncertain, unrepresentative
Deep learning neural network
2D training image
3D raw image
DL generator
SR image
Super-resolved images are too large for simulation

## Slide 4
Backward: ESMDA for microporosity
Ensembles
Observation
Forward model
Difference
Updated ensembles
Forward model
ESMDA workflow
Iterative update
Linear update
In carbonate characterization
Observation: drainage saturation map, porosity map, permeability, real perm, etc
Forward model: multi-scale simulation, invasion percolation, or even DL models!
Resources-intensive, mechanically uncertain, unrepresentative
Subsample drilling

## Slide 5
Case study: Estaillades microporosity inference
Observation: 6 steps drainage experimental image with increasing Pc
Forward model: Invasion percolation
Workflow input:
Porosity map
Pc curve of each microporosity phases
Inference target:
Pc curve of each microporosity phases
Initiate ensemble Pc values
Perform invasion percolation
Compare with observation
Linear update

## Slide 6
Validation against experimental results

## Slide 7
Forward: Super-resolution for microporosity
Solid
Microporosity phase
Resolved pores
7
eXtensive Pore Modeling (XPM)
Extract Resolved pores
1.98 mm
Cross connections
Super-resolution
Voxel size 0.196
Dimension: 12000 x 12000 x 40000
Voxel size 5.5
Dimension: 1000 x 1000 x 2000
Darcy cells
Input
Super-resolved images are too large for simulation

## Slide 8
XPM simulation
Image data from drainage experiments
Input
Validation
Input
Forward
Validate with experimental results
2D training image
3D raw image
SR image

## Slide 9
Conclusion
Focusing on the gap, we present and validate an integrated workflow characterizing carbonate microporosity
Both ESMDA and super-resolution are validated with multi-scale simulations (XPM)
These methods combined will enable more efficient carbonate characterization