## Slide 1: Uncertainty-Driven Screening and Optimisation of UK Depleted Reservoirs for Hydrogen Storage
Ehsan.vahabzadehasbaghi@Manchester.ac.uk
Ehsan Vahabzadeh1, Farzaneh Nazari1, Gabriel Patron2, Arash Pourakaberian1, Calvin Tsay2, Vahid Niasar1
1 Department of Chemical engineering, University of Manchester, Manchester, UK
2 Department of Computing, Imperial, London, UK

## Slide 2: Why UHS matters?
Net-zero shifts primary energy toward renewables (17% → 69%).
Weather-driven variability creates multi-week deficits (tens to hundreds of TWh).
Seasonal storage is required. Short-duration storage is not enough.
CB7
2025
2050
royalsociety

## Slide 3
Why UHS matters?
1
Storage Methods
Hours-Days
Days-Weeks
Weeks-Annual
royalsociety
Net-zero shifts primary energy toward renewables (17% → 69%).
Weather-driven variability creates multi-year deficits (tens to hundreds of TWh).
Seasonal storage is required. Short-duration storage is not enough.
CB7
Notes: I’ll start with the motivation. As the UK moves toward net zero, the energy system becomes more dependent on renewable electricity. That creates a storage problem, because wind and solar are weather-driven. The issue is not only short daily fluctuations, but extended periods where energy demand and renewable supply do not match. These gaps can reach tens to hundreds of terawatt hours. Batteries and other short-duration technologies are useful for hours to days, but they are not designed for seasonal-scale storage. That is where underground hydrogen storage becomes important, because geological storage can provide the scale needed for weeks to annual balancing.

## Slide 4: UHS in Depleted Gas Reservoirs
Existing wells and infrastructure.
Proven seal integrity
Very large storage volumes (TWh scale)
Mixing with Resident/Cushion Gas
Why gas reservoirs?
2
UK has more than 100 depleted gas fields suitable for storage.
Estimated capacity: ~1600 TWh H₂ (half capacity)

## Slide 5
How can UK depleted gas reservoirs be screened and operated to deliver hydrogen storage at the lowest cost while maintaining reliable H₂ recovery?

## Slide 6: Workflow
Compile UK depleted gas reservoir dataset
Simulate gas mixing and estimate recovery factor
Train surrogate model to predict hydrogen RF
Optimise reservoir portfolio to meet UK storage targets
4
Notes: To answer the research question, I built an end-to-end workflow. First, I compiled a UK depleted gas reservoir dataset, including reservoir properties, capacity indicators, and well counts. Then I used physics-based simulations to study gas mixing and hydrogen recovery under different reservoir and operating conditions. Because running full simulations for every optimisation scenario would be too expensive, I trained a surrogate model to predict recovery factor much faster. Finally, I used that surrogate inside a portfolio optimisation framework to identify reservoir combinations and operating strategies that meet UK storage targets at minimum cost.

## Slide 7: Reservoir Characterisation
1. Dataset
124 UK depleted gas reservoirs identified.
96 with complete rock properties, RGIIP, and well counts
2. Key Patterns
Permeability is strongly right-skewed.
Pressure and temperature show a clear positive trend.
3. Implication for modelling
Permeability distribution
Porosity–Permeability distribution
Permeability clustered before sampling to preserve low- and high-permeability groups.
Generated a representative reservoir parameter space.
Pressure-Temperature relationship
5
CO2Stored
Notes: The dataset started from 124 UK depleted gas reservoirs, with 96 having complete data for this study. The key modelling issue was heterogeneity, especially the strongly skewed permeability distribution. So I clustered permeability before sampling to preserve both low- and high-permeability groups and generate representative simulation cases.

## Slide 8: Simulation Setup
Domain and Inputs
Simulation Cases
1000 m
30 m
10 Cycles of I/W
Single Phase: Advection + Diffusion + Dispersion + Buoyancy
Saturated with: CH4 – N2 – CO2 – H2 (Analysed the CG ratio)
Repeated Injection/Withdrawal of H2 as working gas.
Combined the generated reservoir data points with Flow rate and Cycle Lengths (CL) from Latin Hypercube Sampling.
Cases Run: ~2,400 simulations across gas type, Q, CL, and rock/fluid combinations.
Recovery Factor (RF) =
Parameter | Lower Boundary | Upper Boundary
Q [sm3/day] | 1 105 | 1.5 106
CL [day] | 14 (Weekly) | 360 (Annual)
CG Ratio [-] | 0 | 5
Parameter | Lower Boundary | Upper Boundary
Q [sm3/day] |  | 
CL [day] | 14 (Weekly) | 360 (Annual)
CG Ratio [-] | 0 | 5
Cushion Gas Ratio = (only for H2)
6
Notes: For the simulation stage, I used a simplified 2D axisymmetric reservoir model in DuMuX. The model represents single-phase gas flow and transport in porous media, including advection, molecular diffusion, mechanical dispersion, and buoyancy effects. The reservoir was initially saturated with methane, nitrogen, carbon dioxide, or hydrogen, and then hydrogen was injected and withdrawn repeatedly as the working gas over 10 cycles. I combined the reservoir samples with operating variables such as flow rate and cycle length using Latin Hypercube Sampling. In total, I ran around 2,400 simulations, and the main output metric was hydrogen recovery factor, defined as cumulative withdrawn hydrogen divided by cumulative injected hydrogen.

## Slide 9: Physics-Based Simulation
Figure 1: Recovery factor after cycle 10 as a function of Péclet number and buoyancy number.
pore velocity [m/s] | 𝐿 Length of plume [m] | Effective Diffusion [m2/s] | plume height [m]
Spatial Covariance in lateral direction [m2/s] | vertical perm [md] | H2 viscosity [pa.s] | Density difference [kg m-3]
 | 𝐿 Length of plume [m] |  | 
Why Pe and Ng ?
Compact descriptors that collapse reservoir, operational and CG effects.
Pe ↑ ⇒ advection dominates spreading ⇒ RF ↑
Ng ↑ ⇒ buoyancy dominates flow ⇒ RF ↓
Dispersion + buoyancy still are there
7
Notes: “From the physics-based simulations, I did not want to only look at recovery factor as a black-box output. I reduced the behaviour into two dimensionless groups. The first is the Péclet number, which compares advective transport to diffusive and dispersive spreading. The second is the buoyancy number, which compares buoyancy-driven segregation to advective flow.”
“The trend is clear. When Pe increases, advection dominates the spreading mechanisms, and hydrogen recovery generally improves. When Ng increases, buoyancy becomes stronger relative to flow, which promotes vertical segregation and reduces recovery. So these two numbers helped explain why some reservoirs and operating conditions perform better than others.”
“The important point is that the dimensionless analysis connects the simulation results back to physical mechanisms, rather than treating the model as a black box.”
What pushes Pe up?
Higher rate/velocity, higher pressure, lower dispersion/diffusion
What pushes Ng up?
Larger density contrast, higher vertical permeability/connectivity, slower flow

## Slide 10: Surrogate Model
Figure 2: Parity plots for predicted vs. actual RF for both Training and Testing sets.
Goal: Fast surrogate of the physics simulator to predict cycle RF.
Inputs: [K, φ, P, T, Q, CL, ∆ρ, Cycle No., CG Ratio (H2)]
Preprocessing: Normalising features
Model: Artificial Neural Network (ANN)
Training: 80/20 train/test - 5-fold CV on train for hyper-params
Fit-for-purpose: Surrogate achieves simulation-grade accuracy but in milliseconds, enabling UK-scale optimisation.
alexlenail.me
Input layer
9 neurons
Hidden layer
36 neurons
Hidden layer
92 neurons
Hidden layer
108 neurons
Output layer
1 neurons
[Tanh]
[relu]
[sigmoid]
8

## Slide 11: Portfolio Optimisation
Reservoir
Database
Inputs: Reservoir Data + Recoverable Gas Initially in Place + Wells.
Scenario Generation
LHS over Q, CL, CG Ratio, Number of wells.
Surrogate RF ⇒ per-cycle delivered H₂ and PV-cost primitives.
CL [d] | Demand [TWh]
14 | 5
60 | 15
180 | 50
360 | 100-150-200
Optimisation
Framework
Optimal
Plan
CAPEX = f(well costs, H2 price, Compressor size, CG costs)
OPEX = f(electricity, cooling, water requirement, well O&M costs)
PV = Present Value (discount rate = 7 %)
Chosen fields & rates, PV-cost and LCOS.
Each target optimised separately over project horizon (Y = 10 / 20 / 30 Years).
LCOS = Levelised Cost of Storage
Obj = Min [CAPEX + PV (OPEX)]
Constraints:
Reservoir Capacity
Number of wells
Max injection pressure
Meet Demands
Includes wells, compression, H₂ production, CG injection and PSA purification.
9

## Slide 12: Optimal Design
Controlled by the number of I/W cycles achievable within a year.
Costs vary between $23–$38/MWh.
Figure 3: Box plot of LCOS across optimal reservoir combinations for all delivery targets.
Figure 4: Empirical cumulative distribution function of permeability.
Across all demand levels, the chosen reservoirs fall within a narrow range of permeabilities.
Permeability values consistently cluster between 10–30 [mD].
10
Notes: “Shorter cycle lengths allow more injection-withdrawal cycles per year, so the storage asset is used more frequently. That spreads fixed costs over more delivered hydrogen and lowers LCOS.

## Slide 13: When is H₂ cushion gas worth it?
Figure 5: Contour map showing the influence of the PCI and target demand on the CG ratio and resulting LCOS.
Uncertainty in hydrogen production and purification costs was explored by varying the hydrogen price between 3 and 5 $/kg and evaluating three PSA cost scenarios, base, Medium (×50), and High (×100).
Cushion gas becomes valuable when purification is expensive relative to hydrogen.
11
At low low demand, CG ratios rise to 2–4.
At 100 TWh, suggested CG ratio is between 0 and 1.
Notes: At high PCI, purification is cheaper → low cushion gas.
At low PCI and low demand, cushion gas ratios rise to 2–4.
At 100 TWh, high purification-cost cases favour ~1–2× working gas as H₂ cushion.

## Slide 14: Concluding Remarks
Reservoir quality sets the upper limit: poor reservoir properties cannot be fully compensated by optimisation.
1
2
3
H₂ cushion gas is only worth it when gas mixing makes purification expensive; in low-demand, short-cycle cases, optimal ratios can reach about 2–4× working gas.
An extendable end-to-end modelling workflow that connects reservoir physics, surrogate modelling, and optimisation to support hydrogen-storage deployment decisions.
12

## Slide 16
Thank You!
Department of Chemical Engineering, The University of Manchester
Ehsan.vahabzadehasbaghi@manchester.ac.uk
vahid.niasar@manchester.ac.uk

## Slide 17: Optimal Decision
spatial distribution and robustness of optimised UK reservoir fields across annual delivery targets under different PCI values.
Repeated selections cluster in the Southern North Sea, especially Ravenspurn, Clipper North, Indefatigable, Barque, and V-fields.
Optimisation identifies a robust east-coast core portfolio, not just isolated storage sites.
11

## Slide 18: Transport Model
Porosity [-]
Molar Density of phase [Mole/m3]
mole fraction of component k in phase [-]
Storage
Flux
Mass balance eq:
Darcy velocity of phase [m/s]
Hydrodynamic dispersion tensor [m2/s]
source/sink term [mol/m3]
Fugacity Coefficient [-]
Permeability [m2]
Relative Permeability [-]
= Dispersion + Diffusion
Darcy’s Law:
Scheidegger method
Dm from Maxwell-Stefan
Dispersivity [m]

## Slide 19: Cost Assumptions
Module | Parameter | Unit | Value / Expression
Gas cost | cost | USD | 3-5
 | CG ratio | [-] | 0-5
Wells | Retrofitting cost | USD/well | 
 | O & M cost | USD | 0.0545
Compressor | Compressor size |  | 2000
 | Capital cost | USD | 
 | O & M cost | USD | 0.318
Purification (PSA) | Low (Base) scenario capital | USD | 
 | Medium scenario capital | USD | 
 | High scenario capital | USD | 
 | O&M | USD | 
Module | Parameter | Unit | Value / Expression
Gas cost |  |  | 3-5
 | CG ratio | [-] | 0-5
Wells | Retrofitting cost | USD/well | 
 | O & M cost |  | 0.0545
Compressor | Compressor size |  | 2000
 | Capital cost | USD | 
 | O & M cost |  | 0.318
Purification (PSA) | Low (Base) scenario capital |  | 
 | Medium scenario capital |  | 
 | High scenario capital |  | 
 | O&M |  |