## Slide 1
X-ray Computed Tomography-informed models of preferential macropore flow in soils.
Hamza Chaif, François Lafolie, Chloé Caurel, Stéphane Sammartino, Nicolas Beudez,
Anne-Sophie Lissy, Stéphane Ruy, Nathalie Moitrier, Eric Michel
Funded in part by SmartFertiReuse ( ) and Département AgroEcoSystem ( )
Notes: Hi, I’m Eric,
The story I’m gonna tell you today is about preferential flow in soils
And how X-ray CT can help to test the models of preferential flow to their very limits

## Slide 2
Modified from Christophe Salin
Context
● contribute to regulation of water fluxes
● availability of nutriments
● stability of soil structure
● Earthworms and plants
Notes: In the soil, there are plants above ground and earthworms below
Both contribute to one of the services provided by soils,
Whic is the regulation of water fluxes by creating …

## Slide 3
Modified from Christophe Salin
Context
● Earthworms and plants
Macropores (> 300 µm)
● contribute to regulation of water fluxes
● availability of nutriments
● stability of soil structure
Notes: … MACROPORES …
In decayed root channels and earthworm b[eu]rrows

## Slide 4
Modified from Christophe Salin
Context
● Earthworms and plants
Macropores (> 300 µm)
Fast, gravity-driven, preferential flow
● contribute to regulation of water fluxes
● availability of nutriments
● stability of soil structure
Notes: Where water can flow very quickly
under the action of gravity and bypasses most of the soil matrix

## Slide 5
Context
Modified from Christophe Salin
Macropores (> 300 µm)
Fast, gravity-driven, preferential flow
● contribute to regulation of water fluxes
● availability of nutriments
● stability of soil structure
● Earthworms and plants
● Macropore – matrix exchanges
increasing macropore matrix transfers
van den Bogaert et al. Geoderma., 2016
Notes: Some exchanges of water between the macropores and the surrounding matrix are possible,
as evidenced by this blue dye that sorbs to soils
And by other studies in my group.

## Slide 6
● 1D compartment models “Double permeability”
Cey et al.
J. Cont. Hydrol., 2009
●matrix and macropore characterized by effective parameters
● Interface macropore—matrix not described explicitly
● Outputs of model:
in each compartment
● water content = f(z,t)
● flow rate q = f(z,t)
z
≈
matrix
macropores
Current operational models of macropore & matrix flow
Notes: This complicated macropore network is modeled with 1D compartment models

## Slide 7
● 1D compartment models “Double permeability”
●matrix and macropore characterized by effective parameters
● Interface macropore—matrix not described explicitly
matrix
● Outputs of model:
in each compartment
● water content = f(z,t)
● flow rate q = f(z,t)
z
Darcy-Richards: K(), (h)
macropores
Current operational models of macropore & matrix flow

## Slide 8
● 1D compartment models “Double permeability”
●matrix and macropore characterized by effective parameters
● Interface macropore—matrix not described explicitly
macropores
matrix
● Outputs of model:
in each compartment
● water content = f(z,t)
● flow rate q = f(z,t)
z
Darcy-Richards: K(), (h)
Kinematic (Dispersive) Wave
Germann & Beven, Water Resources Research, 1985.
Jarvis et al., Journal of Soil Science, 1991).
Di Pietro et al., Journal of Hydrology, 2003.
Current operational models of macropore & matrix flow
Notes: In the macropores, the Richards equation does not apply
And Germann at the begining of the eighties
popul[eu]rized the idea of using a Kinematic Wave to describe the fast preferential flow
This [eu]mounts to say that the flow rate out of the macropores is proportional to a power law of the of the macropore water content.

## Slide 9
Current operational models of macropore & matrix flow
● 1D compartment models “Double permeability”
●matrix and macropore characterized by effective parameters
● Interface macropore—matrix not described explicitly
matrix
● Outputs of model:
in each compartment
● water content = f(z,t)
● flow rate q = f(z,t)
Darcy-Richards: K(), (h)
Kinematic (Dispersive) Wave
Germann & Beven, Water Resources Research, 1985.
Jarvis et al., Journal of Soil Science, 1991).
Di Pietro et al., Journal of Hydrology, 2003.
z
with
wetted specific surface area of macropores, (m2 m−3).
Jarvis, Vadose Zone J., 2017
macropores
Notes: It is possible to show that this hypotesis implies that
The wettedspecific surface are of the macropores is also proportional to a power law — with a different exponent — of the macropore water content.
The two exponents are linked by this relationship.
We ‘ll come back to that later on.

## Slide 10
Current operational models of macropore & matrix flow
● 1D compartment models “Double permeability”
●matrix and macropore characterized by effective parameters
● Interface macropore—matrix not described explicitly
matrix
● Outputs of model:
in each compartment
● water content = f(z,t)
● flow rate q = f(z,t)
z
Darcy-Richards: K(), (h)
Kinematic (Dispersive) Wave
mean half distance between macropores (m)
exchange term
macropores
Notes: Simplified, physic based equations
In which characteristics of the macropore network are used as parameters :
One is the macropore volume by volume of soil;
The second is the mean half distance between macropores

## Slide 11
● Issue with “d ”
exchange term
“The initial "values of d for the different layers
based on visual observations of the soil structure were increased considerably to obtain a better fit” (Larsson & Jarvis, J. Hydrol., 1999)
“A value of 10 cm for d is considered large in relation to the size and scale of aggregation in the Lanna clay soil.” (Saxena, Jarvis, Bergström, J. Hydrol., 1994)
d has a physical meaning,
but is calibrated to fit experimental data.
Current operational models of macropore & matrix flow
mean half distance between macropores (m)

## Slide 12
Current coupled models of macropore & matrix flow
● Issue with “d”
“The initial "values of d for the different layers
based on visual observations of the soil structure were increased considerably to obtain a better fit” (Larsson & Jarvis, J. Hydrol., 1999)
“A value of 10 cm for d is considered large in relation to the size and scale of aggregation in the Lanna clay soil.” (Saxena, Jarvis, Bergström, J. Hydrol., 1994)
Why ? Can we fix that ?
d has a physical meaning,
but is calibrated to fit experimental data.
Notes: We wuld like in the near future model eathworms population dynamics
How they create macropore and
How that affets wayrt transferts

## Slide 13
Material and methods — simulated rainfall on undisturbed soil cores
4 undisturbed soil columns: 2 of a loamy calcisol,
2 of a silty calcaric luvisol.
2 initial conditions :
initially wet : matrix saturated, macropores empty,
initialy dry : all pores above ~ 8 µm are empty .
Rainfall of 20 mm h-1, duration 90 minutes
//////////////////////
soil
rain
15 cm
////////////////////////
Simulated
rainfalls
scale
scale
Effluent
Outflow rate (m s-1)
Water accumulated in the column (m)
12.5 cm
Notes: Parmi la biodiversité du sol, les vers de terre constituent 80% de la biomasse des sols.
Ils rendent aussi un certains nombre de fonctions et de services
Ils accroissent la DISPONIBILITE des nutriments pour les plantes et les autres organismes du sol, la stabilité de la structure
et ils contribuent à la régulation des flux d’eau
en creusant des galeries suffisamment larges…

## Slide 14
Material and methods — 3D X-ray CT: characterization of macropores
400
horizontal
slices
Voxel size 400 µm
macroporosity

## Slide 15
Material and methods — 3D X-ray CT: characterization of macropores
half distance between
macropores (m)
macroporosity
(m3 m-3soil)
Lissy et al. Geoderma., 2020
macroporosity
400
horizontal
slices
Voxel size 400 µm
Notes: Dans ce projet, nous proposons d’aborder 2 questions : fondamentale et appliquée
La 1ere, ...on se propose ici d’étudier la cascade d’effets depuis les effets sub individuels jusqu’au ES en passant par les effets sur les THV nivo individus/pop
La 2eme...appui aux politiques publiques et décisions réglementaires

## Slide 16
Material and methods — 4D X-ray CT : where is water flowing ?
Scan duration 10 s
30 images per rainfall
Water (ti) = image (ti) – image (t0)
Notes: At each time step: the local changes in grey levels
are thresholded and intersected with the macropore network.

## Slide 17
Material and methods — 4D X-ray CT : where is water flowing ?
Scan duration 10 s
30 images per rainfall
Loamy soil, initially dry
Water (ti) = image (ti) – image (t0)
Notes: At each time step: the local changes in grey levels
are thresholded and intersected with the macropore network.

## Slide 18
Material and methods — 4D X-ray CT : where is water flowing ?
Scan duration 10 s
30 images per rainfall
Sammartino et al. AGU Fall Meeting, 2015
matrix
Cross section of an active macropore
10 mm
macropore
Loamy soil, initially dry
Notes: At each time step: the local changes in grey levels
are thresholded and intersected with the macropore network.

## Slide 19
Material and methods — 4D X-ray CT : where is water flowing ?
Scan duration 10 s
30 images per rainfall
Sammartino et al. AGU Fall Meeting, 2015
wetted
macropore
specific
surface area
macropore
water content.
matrix
10 mm
macropore
Loamy soil, initially dry
Notes: At each time step: the local changes in grey levels
are thresholded and intersected with the macropore network.

## Slide 20
Material and methods — 4D X-ray CT : where is water flowing ?
Macropore water content (m3 m-3)
Wetted specific surface area (m²m-3)
β = 0.831 ± 0.002
matrix
10 mm
macropore
macropore
water content.
wetted
macropore
specific
surface area
d(z), θma,max(z), a, K(𝜃), 𝜃(h), b, ν
a =3- 2 β = 1.34
β = 0.544 ± 0.002
a =3- 2 β = 1.91
Calibrated
Determined from
X-ray CT
Determined from
specific exp.
Notes: We have constrained the model the best we could and we’re going to see how it is doing.

## Slide 21
Test of the model
initially dry
initially wet
Time (s)
Water amount stored in the soil (m)

## Slide 22
Test of the model
initially dry
initially wet
Water amount stored in the soil (m)
Time (s)

## Slide 23
Test of the model
Time (s)
initially dry
initially wet
Profile cumulated exchanged flux density
from macropores to the matrix (m s-1)
Time (s)
Water amount stored in the soil (m)
The first-order exchange term does not capture properly the exchange dynamics.

## Slide 24
A new — pseudo 2D — model of macropore & matrix flow
macropores
matrix
z

## Slide 25
A new, pseudo 2D, macropore – matrix exchange term
matrix
macropores
Kinematic
Dispersive Wave
Richards
equations
horizontal
Richards equation
matrix
Vertical
2
4
update
compute S
= difference between water content at t and t+dt in horizontal matrix)n x (Exchange Surface/n) ) m3eau s-1 m-2sol m2sol m-3sol
z
● The total specific surface area of the macropore–matrix interface is discretized in sections
● Each section corresponds to a horizontal représentation of the matrix where the horizontal Richards equation is solved
to keep track of the horizontal distribution of water in the soil matrix

## Slide 26
A new — pseudo 2D — model of macropore & matrix flow
Water amount stored in the soil (m)
initially dry
initially wet
old model
new model
Profile cumulated exchanged flux density
from macropores to the matrix (m s-1)

## Slide 27
Conclusion
● The new model opens up the possibility to use measured or modeled d values
Macropore water content (m3 m-3)
Wetted specific surface area
● 3D and 4D X-ray CT data were used for the first time to determine the parameters of a permeability model that were to date calibrated to fit the experimental data.
Link to the related paper
● Made it possible to test the model and propose an improved version.
vsoil.hub.inrae.fr/
● Both models will be made available in the Vsoil platform

## Slide 29
Link between total water amount exchanged and time

## Slide 32
Grey-level histogram

## Slide 33
Grey-level histogram of subtracted images