## Slide 1: Regime-Dependent Reactive Mixing Across a Mineral Precipitation Boundary
Anna Kottsova
Postdoctoral Researcher | ETH Zurich
May 20, 2026

## Slide 2: Introduction: Mineral Precipitation
Scaling in a pipe in Larderello
(Brehme et al., 2019)
(Kottsova et al., 2022)
Unintended – Chemical clogging in geothermal operations
(Nisbet et al., 2024)
(44.01.earth)
Intended – Carbon Mineralization
There is a need to characterize mineral precipitation processes in the subsurface
We need to be able to predict where it forms, how it affects the rock properties and how to detect it.

## Slide 3: Prior Experimental Research
0.05 cm
Residual micro-porosity allows for continued transport after initial front establishment
XRCT-assisted core-flooding experiments
XRCT scan, 2.2 μm res.
SEM image

## Slide 4: Research Questions
Does residual micro-porosity allow for further reactive transport?
How does the precipitation barrier modify mixing efficiency and reactive transport compared to the unaltered pore space?
How does this change vary across transport regimes?
Diffusion
Advection
Transition
Seigneur et al. (2019)
0.05 cm

## Slide 5: Pore Network Modeling Approach
Obstructed
network
XRCT scan
⌀4×4.5 mm
2.2 μm res.
reconstruction
Pore network
model
Pristine
network
Chongqing University
  A + B → C↓
Where A and B are transported and C ”precipitates” immediately
ETH Zürich
Scenario | Configuration | Pe | PV injected
1 | Pristine | 0.1 | 50
2 | Pristine | 1 | 50
3 | Pristine | 10 | 50
4 | Obstructed | 0.1 | 50
5 | Obstructed | 1 | 50
6 | Obstructed | 10 | 50

## Slide 6: Regime-Dependent Mixing Suppression
Diffusion
Advection
Obstructed
Pristine
Pristine VS Obstructed:
  Boundary suppresses transverse mixing ⇨ reduced spread, lower total precipitate amount
Diffusion VS Advection:
  Low Pe: Strongest suppressive effect on fluid mixing
  High Pe: Boundary effect is marginal due to strong advection
Transverse spread of mean concentration of the precipitate

## Slide 7: Self-regulating Feedback of the Precipitation Boundary
Diffusion
Advection
Obstructed
Pristine
  Boundary slows down early reaction but sustains high concentration gradient at later stages
Mineral precipitation boundary acts as a temporal regulator of mixing
Total mass of the precipitate produced

## Slide 8: Spatial Distribution Analysis
Concentration variance at 50 PV
Concentration entropy at 50 PV
Variance – how wide is the precipitation spread?
Entropy – Within the affected pores, how evenly is the precipitate distributed?
Obstructed VS Pristine:
  Systematically higher variance and lower entropy at all Pe — more localized deposition
Diffusion VS Advection:
  Low Pe: broad range of pores affected but high concentration variability within
  High Pe: fewer pores involved, but more equally affected

## Slide 9: Conclusions
Boundary suppresses mixing at all flow regimes
  Strongest spread suppression at low Pe (diffusion is impeded directly)
  Marginal at high Pe (advection already segregates reactive streams)
Self-regulating, not self-arresting behavior
  Boundary slows early reaction but sustains high concentration gradients
Flow regime controls not just how much mineral precipitate but how it is distributed
  Low Pe: larger area occupied, broadly distributed with larger variability
  High Pe: fewer pores affected but more uniformly (strongly) occupied ⇨ potentially more damaging per unit volume

## Slide 10: Thank you for attention! Anna Kottsova akottsova@ethz.ch ETH Zürich Geothermal Energy and Geofluids group